## Slide 1: Cornell ERL Prototype Injector DC Photocathode Gun Design Review Vacuum Systems
Yulin Li, January 5th– 6th, 2011

## Slide 2: Outline
Vacuum Requirements – In general
Present vacuum system and performance
Vacuum system Issues
Possible improvements

## Slide 3: Photocathode Gun Vacuum Requirements (I) (GaAs Cathode Dark Lifetime)
Dominated by photocathode lifetime – dark and beam operation
Base pressure – keep reactive residual gas pressure sufficiently low, dark lifetime > days
 | H2 | O2 | CO | CO2
Dmax (L) | ? | ~ 10-2 | ~ 1 | ~ 0.5
Pmax (torr) | ? | ~ 10-14 | ~ 10-12 | ~ 10-13
*) for dark time of 106 sec

## Slide 4: Photocathode Gun Vacuum Requirements (II) (GaAs Cathode Beam Lifetime)
“Sudden” death – HV arcing ?
Ion back-bombardment  Ions originated from cathode-anode gap  Ions originated from trapped ions beyond anode !
Estimate ion flux to the cathode beyond anode (ion  2x10-23 m-2):
For pressure of 10-8 Pa in the drift , and laser spot of Ф0.2cm, and Ld = 0.25m
(ions/sec·cm2 @ 100mA)
The ion flux seems not very high. But what is the mechanism of the QE damage ?
(Ref. 1)
Ref.1 Pozdeyev, Phys. Rev. ST Accel. Beams 10, 083501 (2007)

## Slide 5: ERL Prototype Injector Layout
1
2
3
4
5
1
2
3
4
5
DC Photo-cathode gun
keV Beamline (A1)
SC RF cavity Cryo-module
600 kW Beam Dump
MeV Beamlines w/ full suite of beam instrumentation
Conductance limited beampipes (Ф35mm typical) and cryo-pumping in the ICM effectively separated diagnostic beamlines and beam dump from the photocathode fun
A small (2°) angle in the dump beamline shield the photocathode from radiation originated in the dump, if any

## Slide 6: Achieving XHV in Photocathode Gun
The heat-treated (400°C bake in air for a duration of up to 100 hr) all stainless steel materials for the gun chamber.
SST outgassing rates below 10-13 torr·l/s·cm2 achieved with F0>3, a dimensionless time scale, F0.
Ultra-Low Outgassing in Stainless Steels by Mild Heat Treatment
t – heating time; d –thickness
D=D0 exp(-Ed /kT) – Hydrogen diffusion constant
Ref. C. D. Park, et al, J. Vac. Sci. Technol. A 26 1166 (2008)

## Slide 7: Pumping in the Photocathode Gun
The gun chamber is lined with 16 SAES WR 1650 st707 NEG modules
4 SAES WR 950 st707 NEG modules inserted into a 400-l/s noble diode ion pump
Total H2 pumping speed exceeding 10,000 l/s !! However:
Base pressure ~ 5x10-12 torr
Outgassing from thick flanges, ceramics, cathode structures, cathode support stock ??
Limited by equilibrium H2 pressure of the NEGs and ion pump ??
400 l/s Ion Pump
NEG Modules

## Slide 8: A1 Section – KeV Beamline
Very limited installed vacuum pumping due to lack of space
Very difficult for a thorough/good bakeout, due to many temperature sensitive hardware
1
2
3
5
4
DC Photo-cathode gun
BPM/Corrector/Solenoid
Laser Entrance with adjustable in-vacuum mirrors
RF Buncher
RF Shielded Sliding Joint and Beam Profile Viewer
1
2
2
3
4
5
1 Meter
Pumps (ion pumps and NEG)

## Slide 9: Vacuum Base Pressures in Gun & A1
For sufficiently low base pressure to ensure adequate GaAs cathode lifetime, improvements are needed for the A1 section
Many ‘trapped or hidden’ surfaces (viewer, SLDJT, BPM, buncher tuner, etc.)
Part of ICM warm beampipe that is not bakeable may be a major source of outgassing
1. A1 Connected to the Gun and ICM
2. A1 isolated from the Gun
3. A1 isolated from the Gun & the ICM

## Slide 10: ICM Warm Pipe as a Part of A1
Unbakeable surfaces exposed to A1 during A1 bakeout

## Slide 11
Gun/A1 Vacuum in Beam Runs – I

## Slide 12: Gun/A1 Vacuum in Beam Runs – II
Clear showing beam induced pressure rises in A1 (and the Gun). Causes :
 Beam halo ?  RF-induced in the buncher ?
Beam Current

## Slide 13: Calculated Pressure Profiles
Calculated using one-dimensional finite-element method, to fit measured data, assuming ONLY thermal gas-loads

## Slide 14: Improving Vacuum in the Gun
Understand outgassing from other components in the gun, such as the segmented ceramics, copper parts for the cathodes, etc.
Explored other pumping methods (better combination of NEGs and SIP, cryo-pumps)
NEG coating (gun chamber, gun components, ceramic guard rings, a NEG coated liner, etc.)
Double-walled thin SST chamber ?
Improving gun bakebility

## Slide 15: Improving Vacuum in “A1” Section
Increase installed pumping (adding pumps, increase conductance to the pumps, etc.)
Reducing ‘trapped’ surfaces, as much as possible
Enhance bakebility of the A1 section
Apply NEG thin film coating to the A1 section beam pipes and components.
NEG ?

## Slide 16: Calculated Pressure Profiles w/ NEG Coating

## Slide 17: Brief Summary
Present gun vacuum seem sufficiently good to maintain adequate GaAs cathode dark lifetime
However, base pressure in the preparation chamber needing improvement if multiple cathodes to be stored
Vacuum levels in both the gun and the A1 section needing improvement to achieve acceptable GaAs cathode beam-lifetime
However, significant improvement won’t be trivial
Reduce ion back-scattering using ion-rejecting biased anode/ring(s)
OR, alternative photocathodes, such as multi-alkali