## Slide 2: Welcome! Ivan Bazarov Cornell University
Organizing committee & conveners:
  Ivan Bazarov, Luca Cultrera, Bruce Dunham, David Dowell, Fay Hannon, Kathy Harkay, Carlos Hernandez-Garcia, Wayne Hess, Sven Lederer, Howard Padmore, Triveni Rao, Daniele Sertore, John Smedley, Dimitre Dimitrov, Kevin Jensen
Special thanks to the local organizers & helpers:
  Monica Wesley, Jeanne Butler, Peggy Steenrod, Mike Roman, Devin Bougie, Siddharth Karkare, Karl Smolenski

## Slide 3: Workshop charge:

## Slide 4: Cornell photoinjector for Energy Recovery Linac x-ray source
NSF-supported accelerator R&D test-bed, operational starting 2009
  Main goals: <1 mm normalized rms emittance (to best storage rings)
  average current 33mA @ 15MeV & 100mA @ 5MeV
  2-3 ps bunch length
  demonstrate cathode longevity, RF controls, parameter stability & reliability
photocathode
DC gun
buncher
cryomodule
beam dump
diagnostics beam lines
5 m
HV DC gun
laser system
SRF cryomodule
coldbox
RF 135 kW klystrons
world‘s highest avg brightness photoinjector!

## Slide 5: Cornell photoinjector achievements (so far!)
Maximum average current of 52 mA achieved
  Previous record from LANL/BOEING RF gun 32 mA (avg. over pulses), JLAB DC photoinjector 9.2 mA (CW);
Proved practicality of high current operation (~ kiloCoulomb extracted with no noticeable QE degradation from a single laser spot)
Original emittance spec. achieved:
  en,90% = 0.5 mm at 80pC/bunch (= 100mA at 1.3GHz)
  en,90% = 0.2 mm at 20pC/bunch (= 25 mA)
Would surpass best of existing storage rings in brightness today if this quality beam were to be accelerated to 5 GeV (~5 better than PETRA3!)

## Slide 6: Photocathode work at Cornell
dedicated MBE system
actual accelerator
antimonide growth & analysis chamber
Phillips
Wilson
over in Newman lab
over in Wilson lab
over in Phillips
Clark Hall
Newman

## Slide 7: Just the beginning…
phase space 20 pC/bunch
Example: x2 brightness increase after swapping a cathode with lower MTE (0.14 mm core norm. emittance at 75% core fraction for 20pC/bunch)
  – enormous potential for improvement!
emittance vs. fraction
MBE grown GaAs

## Slide 8: New photo-gun: (>5) improvement in the anticipated beam brightness
~3m
new HV DC gun with diagnostics beamline
new gun assembled
segmented ceramic

## Slide 9: Logistics
Please upload your talk slides ahead of time!
  Mike Roman, Siddharth Karkare;
All talks will be video-taped and posted online:
  If you have any questions, please talk to Fay Hannon;
Tour of Cornell photocathode & photoinjector labs tonight (please sign up for a better head count);
Cayuga Lake Tour tomorrow (Tuesday): bus boarding 16:00-16:10;
Future 2-year plan discussion in Session 5:
  1 slide from every lab on their plans (Fay Hannon);
Tuesday Cayuga lake cruise

## Slide 10
Looking forward to a productive P3 workshop!