## Slide 1: Monte-Carlo simulations of Charge transport and photoemission from GaAs photcathodes
Siddharth Karkare

## Slide 2: Outline
Motivation
3-step model for GaAs(Cs/O) photoemission
Need for a Monte-Carlo simulation
Photoemission step 1 – Excitation
Photoemission step 2 – Transport and scattering
Photoemission step 3 – emission and surface effects
Results obtained so far
Future work and direction

## Slide 3: MOTIVATION
GaAs as a photocathode – activation using Cs/O or Cs/NF3.
Despite extreme vacuum requirements, still one of the coldest sources of electrons
Various associated mysteries regarding QE, response time and mean transverse energy(MTE)

## Slide 4: 3-Step Photoemission Model for NEA-GaAs
Vacuum level
Negative electron affinity
Surface barrier

## Slide 5: Need for Monte-Carlo Transport in Photoemission
Current theory based on diffusion of thermalized electrons up to surface
This is valid only for infra red excitations or for transmission cathodes.
For visible excitation on reflection cathodes significant un-thermalized electrons are emitted
Diffusion model fails for this case.
Previous attempts by Spicer et. al and Yang et.al
Yang, J. Phys. D: Appl. Phys. 23 455 (1990)
Spicer et. al., Surface Science 436 83 (1999)

## Slide 6: 3-valley model for GaAs
http://www.ioffe.ru

## Slide 7: Photoemission Step 1 - Excitation
Heavy hole band
Split-off band
Light hole band
Direct transitions
Indirect transitions
Direct transitions – two body process
Indirect transitions – three body process (ignored)
Semiconductors and Semimetals, Volume 39
Minority Carriers in III-V Semiconductors : Physics and Applications
K-space
All transitions are direct and hence all electrons are excited into gamma valley
Real space
Surface
Exponentially decaying distribution within surface

## Slide 8: Absorption length
Perera et. al J. App Phy, 109, 103528 (2011)
Casey et. al J. Appl. Phys. 46, 1 (1975)

## Slide 9: Photoemission step 2 - Transport
Calculate k-vectors
Calculate velocity vectors
Calculate positions
Scatter
(change k and v vectors)

## Slide 10: Scattering Processes
Impurity Scattering
  Neutral Impurities – only important at very low temperatures
  Ionized Impurities – is elastic
Phonon Scattering
  Acoustic – is elastic
  Optical – inelastic, causes intervalley scattering
  Polar Optical – inelastic
  Piezoelectric – is elastic
Carrier Scattering
  Electron-Electron – only important for n-doping
  Electron-Hole – inelastic (still to be implemented)
  Electron-Plasmon – inelastic

## Slide 11: Scattering rate calculation
Based on Fermi golden rule
H’ is a perturbation to the Hamiltonian of the lattice
Then scattering matrix is given by
Scattering rate can be calculated by integrating over all possible states

## Slide 12: Rates for Gamma Valley

## Slide 13: Drift Velocity Verification

## Slide 14: The Surface – Band Bending
1N. G. Nilsson, Phys. Sta. Solidi (a), 19, K75,(1973)
2J.J. Scheer, J. van Laar, Solid St. Comm. 5, 303 (1967)
Implemented using electric field
Quantum effect ignored

## Slide 15: Surface - Conservation Laws during emission
Conservation of energy
Conservation of transverse momentum
CONSEQUENCES -
Analytic and simulation Results for step boundary, thermalized electrons
1.) No emission from L-valley at 100 surface
2.) Narrow cone (<150) emission from G-valley
L-valley electrons have very high transverse momentum at the 100 surface. Hence cannot get out.

## Slide 16: Narrow cone emission?
Bazarov et.al, J. Appl. Phys. 103, 054901 (2008)
Zhi Liu et.al, J. Vac. Sci. Technol. B 23(6) (2005)
Implies MTE of ~5meV
but
??

## Slide 17: Surface Roughness/Cs scattering/Non-uniform workfunction?
Recently measured MTE from MBE grown cathodes
Cathode | QE(532nm) | MTE(635nm) | MTE(532nm)
Fully Doped | 9% | 120meV | 150mev
100nm undoped | 5% | 77meV | 105meV
S.Karkare, I.Bazarov App. Phys. Lett. 98, 094104 (2011)

## Slide 18: Surface Barriers
*D.G.Fisher, J. Escher et. al., J. App.Phys 43, 3815 (1972)
+W.E. Spicer et al Surface Science 436 83 (1999)
Fisher estimated barrier by fitting data to QE analytic results
Spicer estimated barrier by fitting data to simulated energy distributions
Cause – Surface double dipole effect and image charge
Montecarlo code can simulate barrier of any shape
Double-dipole proposed by Fischer (1974)

## Slide 19: Simulation snapshots (t=0.0ps)
POSITION SPACE
K-SPACE
BLUE – Electrons in Gamma Valley
GREEN – Electrons in L Valley
PURPLE – Electrons in X Valley
RED– Emitted electrons
Excitation with 532nm photons

## Slide 20: Simulation snapshots (t=0.2ps)
POSITION SPACE
K-SPACE
BLUE – Electrons in Gamma Valley
GREEN – Electrons in L Valley
PURPLE – Electrons in X Valley
RED– Emitted electrons

## Slide 21: Simulation snapshots (t=0.6ps)
POSITION SPACE
K-SPACE
BLUE – Electrons in Gamma Valley
GREEN – Electrons in L Valley
PURPLE – Electrons in X Valley
RED– Emitted electrons

## Slide 22: Simulation snapshots (t=2.0ps)
POSITION SPACE
K-SPACE
BLUE – Electrons in Gamma Valley
GREEN – Electrons in L Valley
PURPLE – Electrons in X Valley
RED– Emitted electrons

## Slide 23: Simulation snapshots (t=5.0ps)
POSITION SPACE
K-SPACE
BLUE – Electrons in Gamma Valley
GREEN – Electrons in L Valley
PURPLE – Electrons in X Valley
RED– Emitted electrons

## Slide 24: Simulation snapshots (t=20.0ps)
POSITION SPACE
K-SPACE
BLUE – Electrons in Gamma Valley
GREEN – Electrons in L Valley
PURPLE – Electrons in X Valley
RED– Emitted electrons

## Slide 25: Results from code – QE dependencies

## Slide 26: Response time*
Bazarov et.al, J. Appl. Phys. 103, 054901 (2008)
*Time required for 50% of electrons to get out

## Slide 27: MTE vs Wavelength
Bazarov et.al, J. Appl. Phys. 103, 054901 (2008)

## Slide 28: MTE vs Wavelength using cosine distribution of angles
Bazarov et.al, J. Appl. Phys. 103, 054901 (2008)

## Slide 29: Future directions
Verify and reproduce GaAs results accurately
Incorporate multilayered structures with graded doping
Extend to other 3-5 semiconductors
Implement interfaces and junctions between different materials
Better approximations for the band bending quantum effects
Try to engineer multilayered structures to optimize emission parameters

## Slide 30: Acknowledgements
Ivan Bazarov for his help and guidance
Dimitre Dimitrov (TechX) for useful discussions
Eric Swayer and Adam Bartnik for help in code implementation
Luca Cultrera, Xianghong Liu and Bill Schaff for growing MBE cathodes and measurements
ERL team and NSF and DOE

## Slide 33: Rates for L Valley

## Slide 34: Rates for X Valley