## Slide 1
CW couplers;
KEK injector couplers
Eiji Kako (KEK, Japan)

## Slide 2
OUTLINE
compact-ERL injector cryomodule
Specification and fabrication
Conditioning of prototype couplers
Improvement of cooling by gas-flow
Improvement of water cooling
Conditioning at test-stand and cryomodule
Beam operation of compact-ERL
Summary and next step

## Slide 3
cERL Injector Cryomdule
e- beam
0.5  5.5 MeV
10 mA
Completed in 2012, June.
After low and high power
rf tests, beam operation
started in 2013, April.
CW Input Couplers

## Slide 4
Main Specification for Injector Cryomodule
 | Cavity - 1 | Cavity - 2 | Cavity - 3
Vc | 1.5 MV | 1.75 MV | 1.75 MV
Eacc | 6.5 MV/m | 7.6 MV/m | 7.6 MV/m
QL (10mA) | 7.2 x 105 | 8.4 x 105 | 8.4 x 105
PRF (10mA) | 15 kW /2 | 17.5 kW /2 | 17.5 kW /2
RF Source | Klystron – 1 30kW, CW | Klystron 300kW, | – 2 CW
(cERL injector ; Ibeam = 10 mA, Ebeam = 5 MeV)
Final target of required RF power = CW 180 kW / coupler
Ibeam = 100 mA, Ebeam = 10 MeV for future 3GeV-ERL

## Slide 5
Fabrication of CW Input Couplers
Two prototype input couplers
Six input couplers for cERL injector
(completed in 2009, Oct.)
(completed in 2011, June)
(finished conditioning in 2010, Nov.)
(finished conditioning in 2012, Jan.- Apr.)
(installed in cryomodule in 2012, May)

## Slide 6
Design of Prototype Input Couplers
5 K
80 K
300 K
Warm
window
Water Cooling
Zo =
41.5 W
Doorknob
Coaxial
line
Tristan-type
Coaxial Disk
Ceramics RF Window

## Slide 7
Conditioning of prototype input couplers
300kW
CW Klystron

## Slide 8
Conditioning results at Test Stand
Fan/on
Conditioning Results
1ms, 10Hz, (1%) 200kW for 2h
1s, 0.1Hz, (10%) 100kW for 2h
cw 30kW for 1.5h
cw 50kW for 0.5h
cw 100kW for 1 min
Day - 7

## Slide 9
Improvement of cooling by N2 gas-blow
Zo = 41.5 W
66 W
OD = 41 mm
27 mm
Inner
conductor
Outer conductor
Short-end plate
of doorknob
N2 blow
N2 blow
Halls for N2 flow
Material of
bellows & tube:
thin SUS with Cu plating
thick Cu tube & Cu bellows
5 K
80 K
300 K
2.0t, Cu
1.0t, Sus
+ 10mm Cu
N2 blow
Water Cooling

## Slide 10
Collaboration with HZB/Triumf/KEK
RF Conditioning of cERL Input Couplers
200 kW, <2ms, 5Hz (1%)
30~40 kW, CW

## Slide 11
Further Improvement for efficient cooling by water
Inner conductor
Outer conductor
Water
cooling
channel
Water
cooling
jacket
N2 gas
flow
N2 gas
flow

## Slide 12
Further Improvement for efficient cooling by water
Inner conductor
Outer conductor

## Slide 13
Assembly of input couplers for injector cryomodule

## Slide 14
Conditioning in Cryomodule at R.T.
70 kW, <0.2s, 1Hz (20%)
20 kW, CW

## Slide 15
Beam Operation of cERL
e- beam
5.0 MeV
0.3 mA  10 mA
Beam operation:
Eacc = 7.2, 7.3, 6.9 MV/m
PRF = 3.0, 8.9, 8.1 kW /2
QL = 12.0, 5.8, 4.8 x 105

## Slide 16
Summary and Next Step
KEK injector couplers were conditioned;
test stand: 200 kW (pulse, 1%), 40 kW (CW)
cryomodule: 70 kW (pulse, 20%), 20 kW (CW)
with beam: stable operation at ~ 5 kW (CW)
For the future 3-GeV ERL project;
Fabrication and conditioning at test-stand of
CW 100 kW level couplers with improved cooling
are scheduled.

## Slide 17
Thank you for your attentions.
END