## Slide 1: Cornell’s Main Linac Module (MLC)
Ralf Eichhorn CLASSE, Cornell University

## Slide 2: Not an Outline
I will not talk about:
Cavities (Nick and Sam did this)
HOM absorbers (did that yesterday)
Power couplers (see Vadim’s talk)
SC-Magnet & BPM section (design is halted)
But I will try to review
Choices we made
Questions we are working on

## Slide 3: Cryomodule unit
All ports are on aisle side in the tunnel
Coupler downstream of cavity
SC magnets downstream of cavities
Beamline string supported by HGRP via three posts
Cryogenic valves
Beam
Pneumatic gate valve
Manual gate valve
Cavity package

## Slide 4: Cornell Specifics
Tuner stepper replaceable while string is in cryomodule
Rail system for cold mass insertion
Gate valve inside of module with outside drive
Precision fixed cavity support surfaces between the beamline components and the HGRP -> easy “self” alignment

## Slide 5: Cool-Down shrinkage
Fixed point
9.8 m, vacuum vessel at room temperature
9.5 mm -- HGRP
19 mm – thermal shield
8 mm – beamline
1 mm – cavity LHe vessel
Axial displacement due to thermal contractions of materials at cold
Components | Material | Temperature | ∆L/L | ∆L
HGRP | Ti | 300K-2K | 0.172% | 17 mm
Thermal shield | Al 1100 | 300K-40K | 0.350% | 34.5 mm
Beamline (cavity) | Nb | 300K-2K | 0.146% | 14.5 mm
7.5 mm -- HGRP
15.5 mm – thermal shield
6.5 mm – beamline
Axial displacement is allowed by:
Sliding post
Cavity flexible support
Key alignment of component supports
Coupler design allows an offset of 10 mm
Bellows in HOMs
Sliding post
Sliding post

## Slide 6: Cryogenic manifolds: six lines
1 line for 2K supply | subcooled liquid @1.2 bar | 2K helium bath for cavities via 2K-2 phase line pre-cool gas for cool-down 90% heat load from RF losses in the cavities
2 lines for 4.5-6K | 3.0 bar He liquid Single phase flow | Thermal intercept for HOM absorbers and couplers 2/3 dynamic heat load
3 lines for 40-80K | 20 bar He gas | Thermal intercept for HOM absorbers and couplers 40K thermal shield, low thermal expansion rate over 40-120K range 90% heat load from HOM

## Slide 7: Cryogenic sketch of one Module (as of Sep 2012)
Inside each cryomodule
4 Valves control flow into local distribution lines:
1.8 K
Pre-cool
5 K
40 K
2K, 5K and 40K supply pipes run for the entire half linac

## Slide 8: Cryogenic sketch of one Module (as of today)

## Slide 9: Investigation of Parallel Flows
Q1
Q2

## Slide 10: Structural analysis (II)
Max. 0.1 mm displacement
Emittance growth due to cavity misalignment
Cavity Alignment:
  Transverse offset (x,y)
    Baseline (1-s): 0.5 mm
    Allowable (1-s): 2 mm
  Pitch
    Baseline (1-s): 1 mrad (0.8 mm over length of cavity)
    Allowable (1-s): 1.5 mrad (1.2 mm over length of cavity)

## Slide 11: Structural analysis
1). Deformation/stress of HGRP under 1 ton beamline weight
2). Deformation/stress of vacuum vessel with 4 ton cold mass weight on 3 support posts
3). Mechanical stresses during cool-down process

## Slide 12
Structural Analysis of HGRP
Fixed
∆Y = 0
∆Y = 0
Max. displacement = 0.1 mm
Beamline weight total 1 Ton
Natural frequency ~ 88 Hz
Conclusion: enough supports

## Slide 13: Structural Analysis
RF Power vs. detuning (16.2 MV/m, Qext= 6.5e7)
Natural frequency ~ 88 Hz

## Slide 14
Modal Analysis of 2-Phase Pipe
Fixed supports (Qty. 8)
Mode 1 @ 144 Hz
Mode 2 @ 164 Hz
Conclusion: enough supports
Material Ti Grade 2
Modulus of Elasticity: 102 GPa

## Slide 15
Modal Analysis of 4.5K Cooling Pipe
Fixed pipe support near cryo-valve
Six cylindrical supports
Fixed radial & tangential
Free axial
Natural frequency ~ 129 Hz
Fixed support near cryo-valve
of adjacent MLC
Same situation for 2K & 6K pipes

## Slide 16: You name it
Which specific part of the CM should be analyzed for mechanical eigenmodes?
Strategies to minimize microphonics, do they come via the cryolines?
HGRP (Ti) tolerances is a cost driver
Best and cheapest way to stress-relief?
Experience of weld cracking during cooldown?
Carbon steel vessel demagnetization?
Managing parallel cryogenic flows (expected heat-load for HOMs is 0-400 W, cooling is in parallel)?