## Slide 1: CORNELL ERL COUPLERS:
V. Veshcherevich
Cornell University
2. COUPLER FOR ERL INJECTOR

## Slide 2: Cornell ERL Injector
Each cavity of the Cornell ERL Injector (5 MeV, 100 mA) has two couplers for minimizing the transverse kick. Another benefit of this scheme is reduced RF power per coupler.

## Slide 3: TTF-III Coupler as Prototype
The design of the ERL Injector coupler is based on the design of classic TTF-III input coupler

## Slide 4: Parameters of ERL Injector Coupler

## Slide 5
Main challenges for the injector coupler:
Strong coupling
Wide range of coupling adjustment
High RF power and due to that:
  Risk of bellows overheating
  Risk of ceramic window overheating
Injector Coupler Challenges

## Slide 6: Large Antenna
A need for strong coupling
(Q ext = 9 × 10 4) leads
to a large antenna tip and a large diameter of cold coaxial line

## Slide 7: Large Cold Window
Cold window was enlarged to the size of warm window

## Slide 8: Sectioned Bellows
Outer bellows are subdivided in two sections with 80 K and 300 K intercepts between sections
5 K He Gas Cooling
80 K He Gas Cooling
80 K Intercept
300 K Intercept
300 K Port Flange

## Slide 9: Air Cooling of Bellows
Compressed
Air
Air cooling is applied to inner bellows and to whole warm inner conductor

## Slide 10: Bellows Temperature
Outer Warm Bellows
Inner Warm Bellows
Cold Bellows
Maximum temperature is 100 K on the cold bellows and 90‒100 °C on warm bellows

## Slide 11: Air Cooling of Ceramic
Compressed
Air
Heating of warm ceramic
window is non-uniform.
Local cooling by compressed
air is applied.

## Slide 12: ERL Injector Coupler

## Slide 13: ERL Injector Coupler
Water Cooling
Coupling adjustment screw

## Slide 14: ERL Injector Coupler: Main Parts
Warm Part,
Outer Assembly
Cold Part
Warm Part,
Inner Assembly
Waveguide Box
Antenna
Adjustment
+
Cooling Gas
Supply

## Slide 15: Coupler Test Stand

## Slide 16: CW Power Test Performance
RF Power
Cold Bellows Area Temperatures
Vacuum
Warm Bellows Area Temperatures

## Slide 17: Coupler Pulse Processing
Time required to reach 50 kW
Processing history
Pulse processing (1.5 msec, 50 Hz) of new couplers
installed in the injector cryomodule

## Slide 18: Injector Coupler Performance
Summary of the injector coupler performance:
Two prototype couplers were made (by CPI, Beverly) and tested at Cornell. After that the design was improved.
10 more couplers were fabricated and installed in the ERL Injector Cryomodule in 2008.
Two of ten couplers were tested on the test stand up to
61 kW CW.
In the cryomodule, couplers were processed in pulse and CW modes w/o beam; finally processing is going on during high current beam operation.
RF power up to 40 kW CW per coupler was applied so far during beam operation.
Beam current up to 75 mA was accelerated in the ERL Injector.
High current beam operation will be continued.