## Slide 1
CW Cryomodules;
KEK injector cryomodule
Eiji Kako (KEK, Japan)

## Slide 2
OUTLINE
cERL injector cryomodule
Cryomodule assembly in clean room
Cryomodule assembly in clean booth
Installation in beam line
Low power RF tests
High power RF tests
Static and dynamic heat loads
Beam operation
Summary

## Slide 3
cERL Injector Cryomdule
e- beam
0.5  5.5 MeV
10 mA

## Slide 4
cERL Injector Cryomdule
4
Vacuum Vessel
5K Panel
2K He Jacket
5K Support
80K Base-plate
80K Shield
2K Gas
Return Pipe
5K Panel
5K Duct
e-
Input Coupler
2-cell Cavity
HOM Coupler &
RF Feedthrough
10 mA
0.5 → 5.5 MeV
Magnetic shield

## Slide 5
Cryomdule Assembly in Clean Room
Cavity string assembly in clean room
Exchange of RF feedthroughs
Attachment of input couplers
April 25th, 2012

## Slide 6
Cryomdule Assembly in Clean Booth
Assembly of slide-jack tuner system
Alignment of three cavities
Assembly of 2K-He line
Installation of 5K-He panels

## Slide 7
Cold-mass Assembly
2K-He, 5K-He, 80K-N2 Cooling Line
May 23rd, 2012
5K-He Gas
Return Line
Liq. 5K-He
Supply Line
Liq. 2K-He
Supply Line
2K-He Gas
Return Line
Liq. 80K-N2

## Slide 8
Assembly of Injector Cryomodule
Insertion into vacuum vessel
Installation in the beam line

## Slide 9
Cool-down Tests

## Slide 10
Static Heat Loads
Static heat load ; 2K
Static heat load ; 4.2K
ave. 2K heat load = 12 W
(including 2K cold-box = 1 W)
Cryomodule = 11 W at 2K
Estimation = 14 W,
including 1 W/coupler (x6),
0.2 W/HOM-cable (x15) and others.
ave. 4.2K heat load = 48 W
(including 2K heat load = 12 W)
Cryomodule = 36 W at 4.2K
Estimation = 33 W,
including 3 W/coupler (x6),
1 W/HOM-cable (x15).

## Slide 11
Low Power RF Tests

## Slide 12
High Power RF Tests
Cavity-2
Cavity-3

## Slide 13
Dynamic Heat Loads
Cavity dynamic heat load at 2K
Qo vs. Eacc at 2K
Po = 8 W (at 7.5 MV/m)
Qo = 2 x 109 (at 7.5 MV/m)

## Slide 14
up-stream
mSv/h
down-stream
mSv/h
No.1 Cavity
No.2 Cavity
No.3 Cavity
50ms, 2Hz (10% duty)
50ms, 2Hz (10% duty)
50ms, 2Hz (10% duty)
Observation of x-ray radiation level
no x-ray
< 10 MV/m

## Slide 15
Beam Operation of Injector Section
Vc = 5 MeV operation
(3 cavities)

## Slide 16
SUMMARY
Cryomodule assembly (April-June, 2012)
First cool-down tests (Sept., 2012)
Low and high power RF tests (Jan.-Feb., 2013)
Beam operation (April, 2013)
Heat loads at 2K of three 2-cell cavities were ten
times larger than the expectation due to heating-up
at the antenna tip of HOM feedthroughs.
Stable beam operation at 5 MeV was successfully
demonstrated in the cERL injector cryomodule.

## Slide 17
Thank you for your attentions.
END