## Slide 1: Design of the 9-cell superconducting cavity for EUV light source accelerator
October 4, 2022
Taro Konomi*, Kensei Umemori, Hiroshi Sakai, Eiji Kako (KEK),
Tomoko Ota, Atsushi Miyamoto(Toshiba)
*Current affiliation is Michigan State University (MSU) - FRIB.
ERL2022, October 3-6, 2022, Cornell
SRF/24

## Slide 2: Outline
Introduction
  Accelerator Parameter
  Module and cavity layout
Cavity design for 10 mA class cERL-FEL.
  Cavity parameter
  Center cell design
  Beam pipe design
  End cell optimization method
  End cell optimization
  HOM parameter with ideal HOM damper
HOM damper design
  HOM damper structure
  Damper material property
  Damper design
  HOM parameter with designed HOM damper
Summary

## Slide 3: Introduction

## Slide 4: Introduction
KEK-cERL
KEK- EUV Light source
Parameters | Target value
Wavelength | 13.5 nm
EUV Power | 10 kW
Bunch charge | 60 pC
Beam energy | 800 MeV
Repetition frequency | 162.5 MHz
Average current | 9.75 mA
Accelerating gradient | 12.5 MV/m
Number of cavities | 64
The beam current is lower than KEK-cERL target
  ⇒ Requirement of HOM damping efficiency decreases.
12.5 MV/m can be realized with high reliability
cERL-FEL Accelerator Parameters

## Slide 5: Module and cavity Layout
W/C line
80K
300K
2K 2-Phase
Damper
HOM antenna &BPM
Tuner
Tuner
Tuning Shaft
Tuning Shaft
2K 2-Phase
5K
5K out
80K in
80K out
Cable
5K in
2K in
2K gas out
2K Return Pipe & Cavity Support
5K Shield
80K Shield
HOM Damper
Input Coupler
Room Temp.
Support
80K
80K
80K
80K
80K
80K
80K
80K
80K
80K
～10m
Cold Box
EUV module is designed based on ILC module.

## Slide 6: Cavity design

## Slide 7: Target cavity parameters
Cavity Parameters | KEK-EUV | KEK-cERL | TESLA
Frequency (MHz) | 1300 | 1300 | 1300
Iris diameter (mm) | 70 | 80 | 70
R/Q (Ω) | 1009 | 897 | 1036
G (Ω) | 269 | 289 | 270
Ep/Eacc | 2.0 | 3.0 | 2.0
Hp/Eacc (mT/(MV/m)) | 4.23 | 4.25 | 4.26
BBU limit | >195 mA | ~600 mA | ~80 mA
Concepts of Cavity design
EUV cavity designed based on KEK-cERL main linac
⇒Large beam pipe ＋ Beamline damper
Beam pipe diameters is Φ100mm and Φ110mm.
The center cell shape is TESLA cell to decrease Ep/Eacc=2
TESLA Center Cell
End Cell
End Cell
HOM Damper
HOM
Φ100 mm BP
Φ110 mm BP

## Slide 8: Center cell
Center Cell
End Cell
End Cell
HOM Damper
HOM
Passband of TESLA center cell
EUV cavity was designed focusing on the low frequency HOMs.
Passband of 9-cell HOMs are ruled by the center cell
⇒ R/Q and Rt/Q changes are small
⇒ Qext control the impedance R and Rt
Frequency matching lower R and Rt.

## Slide 9: Beam pipe
Beam pipe diameter | Cutoff monopole (TM01) | Cutoff Dipole (TE11)
φ110 | 2086.4 | 1597.1
φ100 | 2295.0 | 1756.8
Monopole TM01-mode
Dipole TE11-mode
Formula of cutoff
Passband of TESLA Center Cell
φ100mm and φ110mm Beam pipes are selected.
Beam pipe diameter are minimized.
Asymmetry design to damp the high frequency HOMs

## Slide 10: End cell optimization method
Low Frequency HOMs: TE111, TM110, and TM011
Sweep end cell HOM frequency and tune to high impedance HOMs of center cell.

## Slide 11: End cell tuning method (1)
End cell frequency was calculated by tuning curve method.
Electric
boundary
Magnetic
Boundary
Imaginary short plane is magnetic boundary.
⇒ End cell can be calculated only p mode.
Cavity resonance
Beam pipe resonance
TM010,TE111,TM110,TM011 response.
Cell length and iris diameter have the major effect.
B2
A2
R1
R2
xlen
Cavity side circle
A1
B1
A3
B3
Beam pipe side circle
Φ110 BP side cell
Zoom
Change the beam pipe length

## Slide 12: End cell tuning method (2)
Modify the end cell shape to match the center cell frequency.
There is no shape matching more than 3 HOMs at once.
φ110BP side cell adjust TE111 and TM011.
φ100BP side cell adjust TM110 and TM011.
B2
A2
R1
R2
xlen
Cavity side circle
A1
B1
A3
B3
Beam pipe side circle
Constrained conditions
Not re-entrant shape：
  Xlen-A1-A2>0mm
Pressing is possible :
  Absolute value>5mm
Feasible shape：
  Change amount <20mm
TE111 Qext of Φ110 BP side cell
Condition Δf (TE111)=0MHz, Δf(TM011)=0MHz
Qext
Minimum Qext.
This is the best shape.

## Slide 13: End cell optimization: Dipole
φ110BP side cell tuning for TE111
The end cell frequency is changed to match the high impedance mode.
Because the end cell frequency is the p mode frequency.
Target impedance is 5.5x104 which BBU threshold is 200mA.
  ⇒ All Shapes satisfy dipole mode target.
  ⇒ EUV shape is designed focusing on Monopole HOMs
φ100BP side cell tuning for TM110

## Slide 14: End cell optimization: Monopole
Highest impedance of monopole HOM is the TM110-p/9 mode.
Both end cells were tuned to the highest impedance mode.
Minimum value of R/Q*Qext is 5x104 Ohm.
⇒ Heating Power is 20W
TM011-p/9
Monopole HOM Power

## Slide 15: Cavity parameter with perfect HOM damper
Monopole HOM
Dipole HOM
Accelerating parameters
Cavity Parameters | KEK-EUV | KEK-cERL | TESLA
Frequency (MHz) | 1300 | 1300 | 1300
Iris diameter (mm) | 70 | 80 | 70
R/Q (Ω) | 1009 | 897 | 1036
G (Ω) | 269 | 289 | 270
Ep/Eacc | 2.0 | 3.0 | 2.0
Hp/Eacc (mT/(MV/m)) | 4.23 | 4.25 | 4.26
BBU limit | >190 mA | ~600 mA? | ~80 mA?

## Slide 16: HOM damper design

## Slide 17: HOM damper structure

## Slide 18: Damper material
AlN (Sienna Tec. : STL-150D) is one candidate for absorber.
We measured Loss tangent, outgassing and tested brazing.
RF parameter measurement
(a)
(b)

## Slide 19: Damper shape optimization method
TM01 mode From Port 1
TM01 mode From Port 2
TE11 mode From Port 1
TE11 mode From Port 2
3000MHz
3000MHz
Port1
Port2
2000MHz
2000MHz

## Slide 20: Full cavity HOM simulation: monopole mode
Magnetic or Electric
Magnetic or Electric
127
182
Accelerating
mode
2468.9 MHz

## Slide 21: Full cavity HOM simulation: Dipole mode
2590.9 MHz
1730.8 MHz

## Slide 22: Comparison Simulation
Cavity Parameters | KEK-EUV | TESLA
Frequency (MHz) | 1300 | 1300
Iris diameter (mm) | 70 | 70
R/Q (Ω) | 1009 | 1036
G (Ω) | 269 | 270
Ep/Eacc | 2.0 | 2.0
Hp/Eacc (mT/(MV/m)) | 4.23 | 4.26
BBU limit | >190 mA | ~80 mA
Monopole HOM
Dipole HOM
Monopole mode of EUV FULL (include HOM damper shape)
 2468.9 MHz HOM is higher than Ideal HOM damper simulation.
Dipole mode of EUV FULL
 Well agree with Ideal HOM damper simulation

## Slide 23: Summary
EUV cavity has been designing for EUV-ERL/FEL accelerator.
Cryomodule has been designing based on ILC cryomodule.
Cavity designed based on KEK-cERL cavity.
⇒9-cell cavity + beam line damper
Center cell is TESAL shape.
Maximum impedance of Dipole HOM is 3x104 Ohm/cm2/GHz.
⇒ BBU limit is more than 195 mA.
Maximum impedance of Monopole HOM is 1.1x105 Ohm.
  ⇒ This HOM power is about 40 W

## Slide 24: Damper Position requirement
ID110mm
OD130mm
L
φ110
100
左右・外周隙間5㎜
ID100mm
OD120mm
L
φ100
100
左右・外周隙間5㎜
HOMダンパーのQを1E12以上にしようとすると、
Φ100㎜側は260mm以上、Φ110㎜側は290mm以上

## Slide 25: Nb Beam Pipe requirement
SUS Conductivity:7.69e+06
L
L
 | Nb BP length Q>1E12 | AlN position Q>1E12
Φ100 BP | > 120mm | >260mm
Φ110 BP | > 150mm | >290mm