## Slide 1: Energy Recovery Linac Designs and Studies for Electron Cooling of Hadron Beams DoE Phase II SBIR October 4, 2022
Val Kostroun (PI), Christopher Mayes, Colwyn Gulliford, Nicholas Taylor,
Bruce Dunham, Ralf Eichhorn, Joseph Conway, David Douglas

## Slide 2: Outline
Xelera Background
EIC Cooler ERL Specs and Layout
Design Details
Next steps: Precooler
Conclusion
Notes: (karl = 25 years, Val = 50 years, Bruce = 35 years, Chris? 10 years? Ralf = 25 years… that’s 145, so let’s call it 150+ years)

## Slide 3: Xelera Research LLC: Company Overview
Formed in 2013 by 5 partners – 150+ years of accelerator design expertise
Most of Xelera came from the Cornell ERL development team, who designed and built the world’s highest current, high brightness photoinjector, which evolved into significant component of CBETA
Now at 10 total employees
Focus Areas:
  Accelerator design & simulations (EIC magnetized injector design, EIC Cooler)
  Radiation physics consulting (ASU BioDesign C safety systems design)
  Accelerator hardware:
    Electron & X-ray beam stops (ASU Graves Lab)
    Cathode transport systems (ASU Karkare Lab)
    Vacuum system designs, coatings (JLab, Poelker)
    Higher Order Mode loads (HZB, Germany)
    Electron source design and fabrication (JLEIC Cooler Magnetized Gun)
www.XeleraResearch.com
Notes: (karl = 25 years, Val = 50 years, Bruce = 35 years, Chris? 10 years? Ralf = 25 years… that’s 145, so let’s call it 150+ years)

## Slide 4: Project Technical Objectives
ERL Beam Dynamics Designs Satisfying Specifications for CeC of the EIC
  Optimized lattice from cathode to beam stop
  Include relevant effects: space charge, CSR
Tolerance Studies:
  Investigate error effects (misalignments, mis-powering, and field inhomogeneities)
  Practical correction strategies
  Cost/benefit analysis of higher quality hardware versus cost.
Beam Breakup (BBU) Studies: demonstrate the threshold current is below the operating current.
Start-to-End Simulation Studies: High fidelity simulations to confirm cooling specs satisfied and beam can be energy recovered
Beam Halo Studies: Catalogue likely sources, investigate mitigation strategies

## Slide 5: Collaboration
  Erdong Wang, Steve Peggs, Will Bergan, Derong Xu (BNL)
  Steve Benson, Kirsten Deitrick (JLab)
  Georg Hoffstaetter, Ningdong Wang (Cornell)

## Slide 6
ERL Designs: Specs and Original Layout
Electron Beam Parameters | Mode A: 275 GeV Hadrons | Mode B: 100 GeV Hadrons
Energy | 150 MeV | 55 MeV
Bunch charge | 1 nC | 1 nC
Bunch length | 7 mm | 14 mm
Slice energy spread | 1E-04 | 1E-04
Bunch rep. rate | 98.5 MHz | 98.5 MHz

## Slide 7: Layout: Plan View
Original Layout
Inside Layout
Addition of
Early turn around

## Slide 8: 3D Models and Renders (Blender)
End of Linac, Dump, to Hadrons, Return
Injector, Merger, Return

## Slide 9
3D Models and Renders (Blender)
Merge electrons with hadrons into common “Modulator” cooling section.
Demerge electrons from hadrons, into the “Amplifier” section.

## Slide 10: ERL Beam Dynamics Designs: Optics

## Slide 11
Distgen and LUME-GPT
Distgen: Python code for generating initial particles
- Standard distribution types
- Low-discrepancy (Hammersley, etc)
- Pseudo random generation (“rand”)
- Output to GPT, ASTRA, h5 (Bmad), etc
https://github.com/ColwynGulliford/distgen
LUME-GPT: Python wrapper for running and
displaying GPT simulations
- Generate GPT lattice files
- Plot lattice layouts
https://github.com/ColwynGulliford/lume-gpt
Part of larger ecosystem:
https://www.lume.science

## Slide 12
GPT:Bmad Hybrid Injector + Merger Model
GPT Injector Model
Bmad Merger + Linac Model
Optimize emittance vs. bunch length after 1st linac cryomodule

## Slide 13
Impact-T Injector: 10 Million particle tracking

## Slide 14
Multipass Linac Optics: Mode A (150 MeV)

## Slide 15
Beam Tracking, Mode A (100k particles)
LA.CRMOD01.Mar.END\1
LA.Mar.END\1 (150 MeV)
LA.Mar.END\2 (6 MeV)

## Slide 16
Beam Tracking, Mode A (100k particles)

## Slide 17
Beam Tracking, Mode A (100k particles)

## Slide 18
Incorporating Precooler:
Combined SHC with Precooler
(197 MHz SRF injector)
SHC only: 591 MHz Injector
(591 MHz SRF injector)
Ballistic compression
Chicane compression
Also requires significant modifications to cooling section

## Slide 19
Impact-T New Injector: 10 Million particle tracking

## Slide 20
Impact-T New Injector: 10 Million particle tracking

## Slide 21
Updated Layout

## Slide 22
Updated Layout

## Slide 23
https://www.youtube.com/watch?v=4CugHYR-bQI&t=65s

## Slide 24
Conclusions
Produced an initial closed lattice for EIC ERL cooler.
Used this as the basis for further studies (e.g. tolerances, start-to-end, BBU).
Incorporating major changes into the design (precooler and new cooling section design).
Thank you to our colleagues at BNL/JLAB/Cornell
Thank you ERL’22