## Slide 1: Status and Perspective of the Energy Recovery Linac at HZB
a new perspective for bERLinPro?
10/03/22, A. Neumann for the Sealab/bERLinPro Team
66th ICFA Advanced Beam Dynamics Workshop on Energy Recovery Linacs
Cornell University, Ithaca, NY

## Slide 2: bERLinPro: Past, present, future
What I would like to be the message of this talk:
bERLinPro seems to be quite a while around already….. ERL 2013, 2015, 2017, 2019,….2022
What is the current status of the facility?
Some highlights of the on-going work
What do we plan with bERLinPro?
When will we finally have first beam inside the accelerator hall?
All that above I hope to answer within the next 15 minutes Disclaimer: SRF related status will follow in the first SRF session on Tuesday
Introduction
Back to the Future?
>

## Slide 3: Where is bERLinPro?
Introduction
TH2, TH1: Cleanrooms, SRF Teststands
SLH
BESSY II
bERLinPro
Fala-FEL Place
N
bERLinPro in Berlin Adlershof
MLS
Orsay
Berlin
Mainz, Darmstadt
Cern, Geneva
ERLs in Europe
(past, present
future)
Daresbury
SEALAB

## Slide 4
Technical Hall
Basement
Accelerator Hall
Radiation protection cover
bERLinPro/SEALab: A quick orientation
bERLinPro is located in a sub-terranous radiation protection shelter prepared for maximum beam loss
All technical infrastructure, besides the klystron and some cryogenic installations are above ground in a technical hall
BESSY II
bERLinPro
HoBiCaT, sVTS
LVTs,mVTS

## Slide 5: bERLinPro ERL after re-scoping in 2012
introduction
beam dump
6.5 MeV, 100 mA
= 650 kW
linac module
3 x 7 cell SRF cavities
44 MeV
modified Cornell booster
3 x 2 cell SRF cavities
4.5 MeV
srf-gun
1.4 cell SRF cavities
1.5-2.3 MeV, single SC solenoid,
merger
dogleg
test and diagnostic line
Recirculator
bERLinPro: A demonstration facility for ERL science and technology
New developments:
Beam dynamics and manipulation (merger, recirculator, study beam break-up)
SRF systems: Photo-injector, high power booster, HOM damped Linac
Electron source: High repetition laser system high QE cathode development
Control of beam losses and radiation protection
High power beam dump
High power CW RF
  Few 100 kW class klystrons  Power couplers!
  Some 10 kW solid state amplifier
Diagnostics, synchronization machine protection, beam loss monitoring, LLRF and detuning control
A stable Cryoplant
Parameter | bERLinPro
Beam energy recirculator (MeV) | 50
Beam current ERL mode (mA) | 100
Frequency RF and Laser (GHz) | 1.3
Normalized emittance (mm mrad) | 1 (< 0.6 in simulations)
Bunch length (ps) | < 2 (ERL mode), 100 fs @ 10 mA
Beam losses | << 10-5 @ 100 mA
A fully funded 42 M€ project (including completely new building!)

## Slide 6: Why bERLinPro, why ERLs?
High energy electron cooling of bunched proton/ion beams
(e.g. hadron cooling of Electron-Ion-Collider EIC by BNL/JLAB)
Ultra high luminosity electron – ion collider (EIC, LHeC)
(ERL serving as high intensity electron factory for electron hadron collisions at LHeC (7TeV p, 50 GeV e-), similar as former HERA )
Compact radiation sources, nuclear physics
(FEL, inverse Compton sources, next generation lithography, THz facility, MESA, Triumf)
and more …: UED by injector
Next generation multi-user light source
(e.g XFEL oscillators, multi-ID facility as former ARC-en-ciel or 4GLS)
Many applications bERLinPro would deliver important results or milestones for
From next generation Lightsource to many applications, e.g. HEP
Introduction
High energy, high luminosity e+e- collider
(Two ERL based ring collider with larger luminosity than FCCee or ILC proposal: Physics Letters B 804 (2020) 135394)
Prospect: ERLs allow efficient operation at high average brightness/luminosity with Linac class beam quality  Reduces ecological footprint of large-scale science, especially when combining with higher TC SRF technology, vision of sustainable large-scale science driver

## Slide 7: Some recent achievements Status of the facilty (remember w/o SRF)
Achievements

## Slide 8: Design optics versus challenges
Achievements
Parameters at LINAC exit | 
Energy / MeV | 50.1
Bunch length / ps | 4.65
Emittance x,y / µm | 0.58/0.41
Energy spread / keV | 254
Injector and recirculator optics design, magnet layout, collimators
Start to end simulations (Astra+ Elegant), full 3D studies (OPAL), genetic optimization algorithms (MOGA), first look into ML
Wanted vs. unwanted beam studies, dark current, halo formation,
Beam break-up studies and countermeasures, wake analysis and component opt.
Orientation of injector cavities optimized to:
  Reduce coupler kick effects
  Limit back travelling dark current towards cathode
  Short pulse and low emittance modes
M. Abo-Bakr, M. McAteer, J. Völker
B. Kuske, M. Matveenko, E. Panofski et al. see Bettina’s talk on Tuesday
Dark current losses along
injector

## Slide 9: Beam vacuum system, magnets, cold boxes
Achievements
Vacuum system complete, realigned with coordinate system adjusted to building (moved over the years) Cabling of diagnostics well advanced
Linac section with coldbox for cryogenics
supplies
Rail system at ceiling to allow ISO5 flow- boxes everywhere at the machine to avoid particulates

## Slide 10: RF and cryogenics installation status
Achievements
1.3 GHz CW 270 kW Klystron Second test in dummy load
600 kW FuG power supply
Made by CPI
3 Klystrons in house, 1 tested in SLH and at bERLinPro up to 270kW, currently in use for coupler conditioning
2 Klystrons will power Booster, 1 an high-power gun at some point
15 kW solid state amplifiers for Linac Tcav and 1st Booster (zero-crossing)
N2 to cool L700
Final commissioning ongoing mainly cold compressor operation missing (1.8K)
Pics
courtesy
W. Anders
Booster+Gun coldbox

## Slide 11
Drive laser ready for operation, laser beamline on-going (80% complete)
Two oscillators (50 MHz and 1.3 GHz), many pulse schemes, high average power (up to ~40 Watt) at 515 nm output
last section of 20 m long vacuum pipeline for laser beam transport
laser window
laser spot in accelerator hall
photoinjector module
Water cooled fiber
power amplifier:
mode-locked (NIR) 1.3 GHz oscillator
G. Klemz, I. Will, et al
Bunch spacing and current options:
50 MHz Laser:
  1-100 Hz macro-pulse:  Iavg = 77 pA – 7.7 µA
  CW 3.8 mA
1.3 GHz Laser:
  1 Hz – 1 kHz macro-pulse:  Iavg = 77 pA – 20 µA
  CW 100 mA
All this with 77 pC bunch charge, laser power set up for QE of 1 %

## Slide 12: A glance at diagnostics and vacuum system
Achievements
Beamloss
diagnostics
Vacuum sectors
Beam
diagnostics
+ Control system EPICS, visualization and data archiving
Jupyter Notebooks for
Python based data analysis and measurement programs
18x screen stations
24x Striplines, of which 8 with Ion clearing
2x button ion clearing
6x current monitors (ICT)
5x collimators
2x Faraday cups
3x Beam dumps
2 segmented Faraday cups
1 transverse defl. Cavity
Option: 6x THz/Sync. Rad.

## Slide 13
Optimizing the recipe for Na-K-Sb growth by QE and XPS measurements
Investigations into Na-K-Sb as more temperature robust alternative to Cs-K-Sb (baseline cathode)
Time after deposition | Na-K-Sb (WH09) QE @ 515 nm | Cs-K-Sb (P18) QE @ 515 nm
0 days | 2.0% | 3.4 %
8 days | 2.4% | 1.5 %
14 days | 2.2% | 0.3 %
22 days | 2.0% | -
Photocathode Preparation & Analysis System
Sepctral Response Na-K-Sb (WH09)
Spectral response Cs-K-Sb (P18)
High QE photocathodes for SEALAB photoinjector:
Explore multi-alkali Cs- and Na-K-Sb systems, from theoretical modeling (DFG fund), growth and characterization, towards operation in a SRF gun.
Complete infrastructure: growth and characterization system, UHV transport vessels, access to materials science lab EMIL at HZB, collaboration with theory.
J. Kühn, S. Mistry, C. Wang, J. Dube, C. Cocchi, R. Schier, H. Sassnick, et al.
Remember:
Best so far 16.8% at 515 nm (specs 1%)

## Slide 14
beam dump
6.5 MeV, 100 mA
= 650 kW
linac module
3 x 7 cell SRF cavities
44 MeV
modified Cornell booster
3 x 2 cell SRF cavities
4.5 MeV
srf-gun
1.4 cell SRF cavities
2.0-2.7 MeV, single SC solenoid,
merger
dogleg
test and diagnostic line
How do we continue from here?
bERLinPro project accomplished in 2020, readiness of building, infrastructure, warm machine, diagnostics, cryo-plant and high-power RF stations
Commissioning of SRF photo-injector on-going, high quantum efficiency cathodes preparation , Laser system, high-power RF conditioning of SRF Booster module couplers are on track to allow first beam from the injector spring/summer 2023
Beam commissioning program in development to map the injector’s parameter space from short pulse-low charge to, via medium average currents to high charge regime
Status of bERLinPro:
SRF gun coldstring in cleanroom

## Slide 15: bERLinPro, quo vadis?
outlook
New project heads?
Old project heads?
ARD
JEAN LOUIS THÉODORE GÉRICAULT - La Balsa de la Medusa (Museo del Louvre, 1818-19)
John Tenniel - Punch, 29. März 1890, “Der Lotse geht von Bord”
The project was officially completed in 2020
….. to continue as an accelerator research facility!
What’s next?
bERLinPro?
HMS bERLinPro

## Slide 16: What is coming next?
From bERLinPro to SEALAB (SRF Electron Accelerator LABoratory)
outlook
  Completion of the injector and linac/dump lines: Commissioning Injector with beam (up to 5-10 mA, up to few 100 pC, up to 6.5 MeV)
  UED experiment  Aiming for shortest pulses, synchronization, exact LLRF control
  Offer the injector as a testbed to test and commission AI/machine learning techniques, digital twins, as long as Linac gap is open: Test area for (S)RF cavities, modules (e.g. MESA)
  Map the complete attainable injector phase space for many applications: From FEL, UED to HEP
  Testing of new diagnostics, acceleration concepts and controls
  Collaborate with external partners for a 100 mA compatible Linac module in most efficient design: Combine 4K operation with FE-FRT tuner to minimize Cryo and RF power consumption
  Contribute to the European ERL Roadmap in collaboration with PERLE with Injector and Linac studies
SRF Gun
SRF Booster
FOMZ1ZAF at 12.69
UED Detector
FCUPZGAF
Aperture
FOMZ1MAF at 7.64
UED Target & Viewscreen
Solenoid
Ultrafast Electron
Diffraction modifications
FE-FRT, courtesy N. Shipman CERN
We want to open the machine up to internal and external applications within Helmholtz ARD program and beyond:
Dual approach: Develop on SRF injector and follow up on Linac studies

## Slide 17
The dream: Opening up SEALAB
An accelerator test facility [3] with pilot application experiments, a multi-science factory [1,2]
[1] T. Kamps et al., arXiv:1910.00881v2 [physics.acc-ph] 8 Jan 2020
[2] J.-G. Hwang et al., J. Korean Phys. Soc. 77, 337–343 (2020). https://doi.org/10.3938/jkps.77.337
[3] A. Neumann et al., IPAC 2022
bERLinPro offers potentially a large range of beam parameters due to its two photo-cathode laser systems (50 MHz, 1.3 GHz) and their macro-pulse capabilities
As long as there is no Linac installed within the ERL recirculator, this can be used as a passive beam (no effective acceleration) test stand.
Adaptation to the existing cryogenic installations and particulate free installations are the key for success
Requires a Linac

## Slide 18
Ultra-fast scattering experiments with the SRF photoinjector
Many ARD aspects: SRF, beam dynamics, instrumentation, controls, …
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
SRF Gun
SRF Booster
Sample Area B
Detector Area
16
Aperture
Sample Area A
Dogleg option
Capabilities of the photoinjector:
1 to 3.5 MeV beam energy with variable bunch charge (1 fC to 100 pC), pulse length (10 fs to 6 ps) and spot size (10 to 100s μm), high stability at MHz repetition rate.
Very flexible longitudinal accelerator/lens system: one gun cavity and three booster cavities, done optimization for bunching scheme, see B. Alberdi et al. [1].
[1] B. Alberdi, et al, Sci. Rep. 12, 13365 (2022)
TOF jitter at position A in units of initial jitter
vs number of cavities in the photoinjector
Ultrafast science drivers:
Diffraction camera for molecular movies with MHz repetition rate (UED).
Imaging of macromolecular structures in liquid phase (UEI).
Complementary to SR and FEL light sources. Enabling multi-modal capabilities for Bessy II/III.
T. Kamps, B. Alberdi Esuain, J. Völker, T. Spohr, E. Ergenlik, A. Neumann, J.-G. Hwang, S. Barg, et al.
Demonstrator phase within funds!

## Slide 19: Realize a Linac for SEALab/bERLinPro
Linac for sealab
New baseline:
Cut down to a simplified more cost saving, less complicated design
A bERLinPro Linac was developed
Full three-cavity string HOM analysed, coupler kick studies, manufacturing study etc….
For a BBU threshold of 2x 100 mA
+ margin this design is an overkill threshold current in the Ampère regime!
Cornell shape cells
No waveguides, TTF coupler + Fast reactive tuner port
Beamtube HOM absorber like Booster/Gun
Simplified module concept, Cornell like, no room temperature parts
Cryo allows to potentially operate one cavity at 4 K as new material demonstrator
Contributes to European ERL roadmap
Not funded yet!

## Slide 20: When will we have first beam?
First beam?
“Banana line”
MESA
Gun
Booster
TCav
Cathode transfer system
30 kW dump
Injector line
Focus on commissioning injector with SRF gun and transverse deflecting cavity + diagnostic line
Next stage installation of the Booster module, possible beam transfer into the high power dump
Recirculation, when Linac funding is secured or an interim arrangement can be found
650 kW dump
SRF gun coldstring and cathode transfer system currently being reworked and setup in the cleanroom (Tuesday SRF talk)
First beam to be expected around late Spring 2023

## Slide 21: But…….
surpirse
….in case you did not know,
there is already a running multi-turn ERL in Berlin!

## Slide 22: Acknowledgements
Fin
Many thanks to:
J. Teichert, A. Arnold, P. Murcek, R. Rimmer, A. Burrill, F. Marhauser, S. Belomestnykh, E. Zaplatin, E. Kako, N. Shipman R. Eichhorn, J. Sekutowicz, P. Kneisel, G. Ciovati, A. Matheisen, B. van-der-Horst, M. Schmökel, W.A. Clemens, C. Dreyfuss, D. Forehand, T. Harris, R.B. Overton, L. Turlington, M. Schalwat, S. Lederer, V. Volkov, I. Will, MAC members
+many more
HZB bERLinPro Team & friends
former colleagues
Team Sealab
Thanks for your attention!
Funding: Bundesministerium für Bildung & Forschung Bundesland Berlin, Helmholtz Gemeinschaft