## Slide 1: SRF performance on the cERL at KEK
Hiroshi Sakai (on behalf of SRF development team)
Innovation Center for Applied Superconducting Accelerators (iCASA), Accelerator Division
High Energy Accelerator Research Organization (KEK)
ERL2022 workshop @ Cornell Univ. (2022.Oct.3-6)
15 min. + 5 min.
?? pages
Introduction of cERL cryomodules
SRF performance of cERL cryomodules under cERL beam operation in the latest three years
SRF R&D for future EUV-FEL and so on from cERL operation in KEK
Summary
Compact ERL (cERL)

## Slide 2: Comact ERL (cERL) in KEK & cERL cryomodules
Injector-linac
Dump
Recirculation (return) loop
Injector diagnostic line
Merger
Compact ERL Layout
Photocathode DC gun
(Not SRF Gun)
Main linac module
Main-linac
Input couplers
Cryostat
Tuner
HOM absorber
Two 9-cell SC cavities
e-
HOM damped (for 100mA circulation to suppress HOM-BBU in design)
9-cell cavity (ERL-model2)× 2
Requirement was satisfied at V.T. Issue: Heavy F.E was met @9-10MV/m after string assembly. & met quench shown later In detail
3MeV
20MeV
Input Coupler
HOM Coupler &
RF Feedthrough
2-cell Cavity
Tuner
Cryostat
e-
Injector module
2-cell cavity × 3
Double coupler
RF frequency: 1.3 GHz
Input power :
10kW/coupler (10mA, 5MeV)
180kW/coupler (100mA, 10MeV)
Eacc: 7.6MV/m（5MeV）
15MV/m (10MeV)
Unloaded-Q: Q0 > 11010
Target Energy : 35MeV
 Change 20MeV due to field emission
RF frequency: 1.3 GHz
Input power : 20kW CW (SW)
Eacc: 15 MV/m（design）
Unloaded-Q: Q0 > 11010
Issue: We met the HOM coupler heating if field inceased more than 7MV/m. It is the reason for heating not perfectly to be filiterd in HOM coupler iand results in lower Q0 than 1x1010.
Nominal beam energy | 35 MeV  20MeV 17.5MeV
Nominal Injector energy | 5 MeV 2.9MeV
Beam current | 10 mA (initial goal) 100mA (final)
Normalized emittance | 0.1 ‒ 1 mmmrad
Bunch length (bunch compressed) | 1-3ps (usual) 100fs (short bunch)
Design parameters of the cERL
17.5 MeV
Tuner
Irradiation beam
Line (IR) (2019)
K. Watanabe, et al. “Development of the superconducting rf 2-cell cavity for cERL injector at KEK” Nucl. Instru. Meth. A Vol. 714, p67-82 (2013)
H.Sakai et al. “Field emission studies in vertical test and during cryomodule operation using precise x-ray mapping system”. Phys. Rev. Accel. Beams 22, 022002 (2019)

## Slide 3: Operational history of cERL cryomodule (almost 10 years)
3
2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
Commissioning of injector& main linac
Commissioning of cERL (with loop)
Operation
Construction, Maintenance
Construction of recirculation loop
Increasing the beam current
Commissioning of LCS system
Construction of
Injector and main linac cryomodule
Construction of LCS system
High bunch charge
& THz study
1mA again
Start beam operation
Construction of RI beamline
RI beam test & production
Beam operation
What happened in long term beam operation ? And how do we keep cavity performance in latest three years?
1mA ERL achieved
Construction of IR-FEL
Cryogenic &Gun maintenance work
IR-FEL operation
CW 0.3mA ERL
with undulator
Talk about SRF operation (& SRF R&D )
ERL2019
But from 2017 ML1 did not reach more than 7MV after unknown burst event. (before reach >10MV)
H.Sakai et al. “LONG-TERM OPERATION WITH BEAM AND CAVITY PERFORMANCE
DEGRADATION IN COMPACT-ERL MAIN LINAC IN KEK” Proc. of LIINAC2018
(Main linac performance history) Unknown burst event was occurred at ML1 in 2017. Finally processed but quenched 6.9 MV.
cERL beam operation from Oct. 2019 to Feb. 2022 |  | 
Period(beam operation time) | Energy[MeV] (Comment) | Current
2019.Oct. (3 weeks) | 17.5 (loop) | 60 pC/ bunch
 | 19.0 (IR) | ~1 uA (CW)
2020.Jun. (4 weeks) | 17.5 (loop) | 60 pC/ bunch
2020.Jun. (3 weeks) | 17.5 (loop) | 60 pC/ bunch
2021.Feb-Mar. (6 weeks) | 17.5 (loop) | 60 pC/ bunch
 | 23.0 (IR) | 1pC/bunch (pulse)
2021.Oct. (3 weeks) | 17.5 (loop) | 40 pC/ bunch
 | 10.0 (IR) | ~1uA (CW)
2022.Feb-Mar. (3 weeks) | 17.5 (loop) | 300uA (CW)
 | 10.0 (IR) | ~1uA (CW)
(Injector performance history) field emitted electrons hitting Faraday cup leading to vacuum discharge and F.E much increased in injector cryomodule in 2015
High-power pulse processing found to reduce radiation. It works to recover nominal operation field of 7MV/m.
E. Kako “Degradation and Recovery of CavityPerformance in compact-ERL Injector Cryomodule” talk in ERL2019
We cooled 2K before beam operation and warmed up after beam operation

## Slide 4: Power & LLRF stability in cERL beam operation
Present (2022) | Inj1(2cell) | Inj2(2cell) | Inj3(2cell) | ML1(9cell) | ML2(9cell)
Acc. Field | 3.4 MV/m | 3.6 MV/m | 3.2 MV/m | 5.2 MV/m | 8.2 MV/m
power | 0.6 kW | 1.4 kW | 1.1 kW | 0.7 kW | 2kW
Power source | 25 kW klystron | 300kW klystron (Vector sum) |  | 16 kW solid state Amp | 8kW solid state Amp
QL | 1.2e6 | 5.8e5 | 4.8e5 | 1.3e7 | 1.0e7
DA/A(% rms) | 0.014% | 0.011% |  | 0.016% | 0.011%
Dq(deg rms) | 0.023deg | 0.025deg |  | 0.027deg | 0.015deg
Data taken in 2021.Feb.5. Basically suppress michrophonics and almost close our requirements of DA/A ~ 0.01% , Dq ~ 0.01 deg.
FPGA
Virtex5-FX
Beam stability was also achieved about 0.01% by measuring momentum jitter at screen monitor on arc section thanks to LLRF optimization
Hz
dBc/Hz
T. Miura, IPAC2014 @Dresden
Phase noise by Microphonics was suppressed well by RF FB.
Phase noise of Vc with FB was almost the same as that of Master Oscillator.
Microphonics suppression in ML
(Up to now, we keep the RF stability after ML1 field reduced 8.3 MV/m  5.2 MV/m in 2017 )
Inj1
Inj2,3
ML1
ML2
Total beam energy 17.5 MeV
Injector gain : 3.0 MV
Main linac gain : 14.0 MV

## Slide 5: Injector performance from Oct. 2019 to Feb. 2022
We once met the sudden severe X-ray increase during beam operation in Jun. 2020.
F.E onset reduced from 8 MV/m to 5 MV/m in Inj #2 cavity. We do not know the reason.
After pulse processing, F.E onset recovered at normal level.  kept 7 MV/m operation
final
Suddenly x-ray onset reduced
2020.Jun.18
X-ray onset before and after pulse processing、
Pulse duty (0.5ms 10Hz)
18 MV/m (~2 hours)
Pulse duty (5ms 10Hz)
12 MV/m (~1 hours)
(Before pulse processing)
CW = 8MV/m (onset 5MV/m)
(After Pulse processing)
CW = 8MV/m (onset 8MV/m)
2020.Jun.19
From now, we apply same pulse processing after 2 K cooldown before beam operation.

## Slide 6: Main linac performance (long-time Q-value history (2012.Dec – 2022.Feb))
Before the beam operation, we could keep 1x1010 at 10MV on both cavities in 2012.
Main degradation of ML1 is thermal breakdown from 2017. we doubt the some ceramic and/or HOM absorber crack and/or something from outside of the cryomodule (NEG?) might come into the ML1 cavity ??
After that quench limit and Q-values gradually reduced. But in latest three years both kept same level.
In first five years (2012-2016), we see the degradation by the field emission. In the latest three years, we kept the same Q-values in both cavities by applying the pulse processing on every cERL operational phase.
Kept same level of
Q-values on 3years
Chart: ML2 Vc (MV)
| 3 | 4 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5
Rad6(lower) (mSv/h) (before pulse aging) (2022/2/8) | 0.0003 | 0.0003 | 0.0015 | 0.024 | 0.1113 | 0.8396 | 6.722 | 33.04 | 121.5 | 353.9 | 844.8 | 1781
Rad6(lower) (mSv/h) (after pulse aging) (2022/2/8) | 0.0005 | 0.0005 | 0.0003 | 0.009 | 0.0188 | 0.4099 | 3.257 | 17.93 | 65.6 | 211.1 | 496.8 | 1156
ML Pulse processing (peak 11.7MV)
Vc = 8.8MV(CW) + 2.9MV(pulse 10Hz 4ms) (3 hours apply)
After pulse processing, 0.5 MV onset of x-ray was increased. X-ray monitor was set at the downstream of cryomodule.
Kept same level of
Q-values on 3years
ML1
ML2
Before
Beam operation
Before
Beam operation
Up to now, we apply same pulse processing for both ML cavities after 2 K cooldown before beam operation.

## Slide 7: ML Trip ratio (longterm) (2014.Apr. ~ 2022.Mar.) (almost 9 years) & Inj
After optimization of LLRF gain in 2014, we kept small trip ratio in 2015. If cavity field increased higher in 2015. trip ratio increased. Main reasons of trip come from the warm coupler (ML2) discharge event (light green). We did not know why these discharged events would occur. However, we could safely turn off RF within 10us by using ITL of arc sensor of input coupler.
We note that cERL injector did not meet the trip caused by Inj cryomodule itself in 3 years
Stably operated without severe hardware problem on both Inj and ML cryomodule until now.

## Slide 8: Successful ~ 0.3mA CW beam operation with energy recovery with Undulator
（upper） ML1
8.5 MV
（lower）ML2
5.5 MV
e-
Pin
Pref
Main linac
Change CW mode and increase the beam current :Reach 0.3 mA on Feb/2022 with undulator.
Beam current [mA]
ML1: Δ(Pin1-Pref1)
ML2: Δ(Pin2-Pref2)
Total (ML1+ML2): Δ(Pin-Pref)
Δ(Pin-Pref) [W]
Beam current [mA]
Required power without recovery is :
14.0 MV x 250 uA = 3.5 kW
Trend of beam current under energy recovery
2 hours
0.25 mA
Feed power : less than 10W !! (r.m.s 4 W)
Energy recovery was successfully done with 100%
Stable energy recovery of about 0.3 mA was successfully done without beam loss.
Next, we try to increase beam current more

## Slide 9: Trial for Pulsed beam operation for higher energy in cERL
Motivation
Courtesy of T. Miura , F.Qiu
For irradiation beam line, we would like to increase higher energy for not only produce 99Mo but also other RI like 67Cu,whose giant resonance is a little higher than 99Mo.
-> more than 23 MeV is required.
Inj.1
Inj.2
Inj.3
ML1
ML2
~2.2 MV ~2.2 MV ~2.2 MV ~6 MV ~10 MV
Einj ≈ 7 MeV
CAM8
Irradiation beam line
Pulse Pulse Pulse CW Pulse
10 MV/m
10 MV/m 10 MV/m
Pg=Vc^2/(4*r/Q*QL)
QL ~ 1e6
QL ~ 1e7
5.8 MV/m
9.7 MV/m
For cERL injector, it is difficult to increase higher field of > 8MV/m due to the HOM heat load. But we could escape from HOM heat load with pulse mode and can reach higher field. (ML2 also similar)
We made 5ms pulse mode operation with lower duty
Etotal ≈ 23 MeV
F. Qiu et al., “Application of disturbance observer-based control on pulsed superconducting radio frequency cavities”, Phys. Rev. Accel. Beams 24, 012804 (2021)

## Slide 10: Momentum stability (2020.Apr)
Momentum (Beam center @CAM14)
Peak beam current : 1.3mA (100ns)
Charge : 1 pC/bunch
Inj1: -0.6%
Inj2,3: -0.8%
ML1: -1.4%
ML2: -0.8%
Beam loading
Inj.1
Inj.2
Inj.3
ML1
ML2
~2.2 MV ~2.2 MV ~2.2 MV ~6 MV ~10 MV
Einj ≈ 7 MeV Etotal ≈ 23 MeV
Screen monitor (CAM14)
Irradiation beam line
Pulse Pulse Pulse CW Pulse
10 MV/m
10 MV/m 10 MV/m
We have stably operated with pulse operation on higher energy with ~1% beam loading
Beam stability is 0.012 %
We could proceed 67 Cu generation

## Slide 11: Toward more reliable operation for SRF cryomdule for high current beam on cERL & future EUV-FEL
 | ERL Model 2 | EUV
Rsh/Q | 897 Ω | ~1000 Ω
Ep/Eacc | 3.0 | ~ 2.0
Iris diameter | 80 mm | 70 mm
Hp/Eacc | 42.5 Oe/(MV/m) | ～42.0 Oe/(MV/m)
Field emission & crack of HOM damper are main issues for reliable operation.  How to overcome field emission
EUV cavity – TESLA-type 9-cell cavity + Large beam pipes(100f & 110f)
Stable operation at 12.5 MV/m seems achievable due to reduced Ep/Eacc.
Satisfy the HOM-BBU threshold of more than 100mA by EUV cavity.
EUV cavity design
H. Sakai, et., al. “SUPERCONDUCTING ACCELERATOR FOR ERL BASED FEL EUV LIGHT SOURCE AT KEK ” Porc, of SRF2017, Lanzhou, China, MOXA04, p13 (2017)
Done by T.Konomi
cERL HOM damper
Ferrite with HIP bonding
T. Ota, et. al. SRF workshop 2019
AlN cylinder
Fragile under thermal cyle
C-shaped waveguide
M.Sawamura, “Development of HOM coupler with C-shaped waveguidefor ERL operation” ERL2019
R&D for Clean assembly work
Open clean bench
KOACH (ISO class 1) for local clean bench
Slow pumping/venting system with vacuum particle sensor.
Both were already applied for STF cryomodule assembly work.
H. Sakai, et. al. SRF workshop 2019
T. Konomi
“Design of the 9-cell superconducting cavity for EUV light source accelerator”
Detailed talk in this ERL2022
T. Konomi
“Horizontal test of Superconducting RF gun #2 at KEK”
Detailed talk in this ERL2022
R&D for SRF Gun for more high quality and high current operation
Cavity
Test stand

## Slide 12: Toward High-Q cavity approach in KEK
Standard recipe (120deg,48h), 200deg,3h
300 ~ 400deg,3h
600 ~ 800deg,3h
For cavity baking.
We observed the drastic temperature dependence about Q-values. High-Q values were also observed by only applying Mid temperature about 300-400deg without Nitrogen doping
Mid-T furnace baking is new approach for producing Higher-Q cavity compared with N-doped cavity
Developed on recent 1-2 years
T. Ito et al, “Influence of furnace baking on Q–E behavior of superconducting accelerating cavities”
https://doi.org/10.1093/ptep/ptab056
Mid-T furnace baking
Surface condition was changed
Courtesy of T. Ito
Notes: 理由（仮説）：
１．従来から実はMulti-layer構造(Nb2O5 , NbO, NbH(tc = 1.4K), Nb(bulk))になっているのだが、この構造が変わって、従来よりhigh-Qが出ているかもしれない。(酸化ニオブがlossy、
2. 空洞側の処理でn-dopingの場合は窒素の拡散でdirtyにしている。  furnace bakingでは酸素に置き換えている。これでN-dopingと同等のHigh-Qが出ているのではないか？

## Slide 13: Nb3Sn cavity development in KEK
Can operate 4.2 K or higher temp ?
 Results in using cryocooler operation.
Cavity development already started. We will wait Nb3Sn accelerator
Nb3Sn cavity (coating) KEK
Courtesy of K. Takahashi, K. Umemori, T. Konomi, T. Ito, T. Yamada,
KEK first results
K.Takahashi, et al., FIRST NB3SN COATING AND CAVITY PERFORMANCE RESULT AT KEK”, Proc of SRF2021.
Nb3Sn furnace in KEK
x7
S. Posen and D. L. Hall. Superconductor Science and Technology, 30(3):033004, 2017
4.2K
2K

## Slide 14: Summary
KEK cERL cryomodule are operating from 2012 until now for almost 10 years.
For injector, one we met the severe degradation in 2020. But we could recover the normal radiation onset level by the pulse processing.
For Main iinac we met the cavity degradation under beam operation after the unknown burst event of ML1. But for the latest 3 years, we did not see more degradation. Main issues is field emission for ML2 and thermal breakdown for ML1.
Finally, by applying the pulse processing for both cryomodule before the beam operation, we kept the stable beam operation under LLRF optimization.
For higher energy operation, we applied pulsed operation to escape the HOM quench of injector. We could increase the energy from 17.5 MeV to 23.0 MeV for irradiation beam line.
More reliable operation, we design the F.E suppression and HOM suppression cavity for EUV-FEL and develop the F.E reduction approaches (clean assembly , HOM damper)
SRF Gun is under developing for CW high current beam generation in KEK. (now FRIB)
Higher-Q R&D and Nb3Sn cavity R&D also tried to reduce CW heat load.
We plan to make high-Q cryomodule for EUV-FEL R&D under cERL operation .