## Slide 1: Using Polynomial Chaos Expansion to determine Solenoid misalignment during the bERLinPro Commissioning
ERL 22, Cornell University,
Bettina Kuske, HZB, 04-10-2022
The magic of
surrogate models

## Slide 2
context: Work
Work presented here has been carried out 2019 / 2020
After gun cavity damage commissioning preparation stopped
Work still lacks experimental proof – hopefully in 2023!
During the last years AI applications became common use in accelerator physics
Polynomial Chaos Expansion (PCE) is much less prominent
  (PCE is commonly used in engineering and data science)
  quantifies uncertainty in parametric systems
  provides surrogate models
  works on relatively few data point
  easy to implement
  fast
Chaos – doesn’t relate to ‘chaos theory’, but was used in early 20th century for stochastic processes
PCE:

## Slide 3
Context: Solenoid misalignment
  Due to misalignment of solenoid:
    Beam position and size vary on screen with solenoid setting
    Strong impact on trajectory (larger than quadrupole misalignments) *
      bERLinPro solenoid mounted on ‘Hexapod’, highly precise 6D alignment
  Problem:
    No absolute positioning system of Hexapod
    Cold solenoid: no tracing of movements during cooldown
  Experience with GUN0:
    Very difficult to manually align (highly non-linear, highly coupled)
    Off-line fitting cumbersome
  => Need for beam-based alignment procedure
Beam position on FOMZ1GAF
* IPAC2014, Dresden, Germany, TUPRO038, doi:10.18429/JACoW-IPAC2014-TUPRO038

## Slide 4
Hardware Gunmodule
First screen 1.78m
behind cathode
The bERLinPro gun module:

## Slide 5
Content
Structure of the talk:
  PCE in a nutshell
  Small example and workflow
  Setting up the PCE surrogate model
  Sobol’s indices
  The ‘real’ problem: inverse PCE
  Summary

## Slide 6
Pce in a nutshell
Definition * : polynomial chaos is a way of representing random variables/random processes in terms of orthogonal polynomials (Comparable to Taylor expansions of functions)
Definition**: polynomial chaos can be used to determine the evolution of uncertainty in a dynamical system when there is probabilistic uncertainty in the system parameters
* Youtube: PyData meeting Berlin 2017, Emily Gorcenski https://www.youtube.com/watch?v=Z-Qio-n6yPc
** Wikipedia
Mathematical basis: Cameron-Martin theorem: Every random distribution (with finite variance) can be represented in terms of polynomial series developed around arbitrary probabilistic distributions (uniform, Gaussian…)

## Slide 7
Arbitrary distr.
of positions /
sizes on screen
Pce in a nutshell
Mapping to screen
(tracking /
measurement)
Distributions of solenoid
misalignments
Dx, Dy, Dtheta, Dphi
The surrogate model is fast to calculate
The coefficients of the polynomial represent the moments of the distribution
“Sobol’s indices” can be extracted from the coefficients
The polynomials used in expansion depend on the input distribution
  Uniform – Legendre polynomials
  Gaussian – Hermite polynomials
  …
Surrogate model
Approximate output
by polynomial series
PCE

## Slide 8
workflow
Create tracking/measured data with known input distribution
Build joint distribution
of input parameters
Set up generic polynomials
to different orders
Determine polynomial coefficients by a fitting
1
2
3
import chaospy as cp
1 distribution = cp.J(cp.Uniform(1.75, 3.40), cp.Normal(0, 1), cp.Normal(0,1))
2 polynomial_expansion3 = cp.orth_ttr(3, distribution)
3 approx3 = cp.fit_regression(polynomial_expansion3, sample, result.T)
Mathematics is implemented in Python package:
(MATLAB UQLab: a framework for uncertainty quantification)
Calculate polynomial
using test data
Compare PCE to tracking/measured results
Verification:

## Slide 9
Example
Tracking data:
Solenoid field variation -0.2T – 0.2T
-> uniform distribution
Offsets:
  Dx = Dy = 0.25 mm
  Dq = Dj = 0
PCE model:
Test data:
solenoid field variation -0.4 T - 0.4T
Dx, Dy = 0.23mm - 0.27mm
-> random distribution
Surrogate model for beam position on screen for different solenoid settings with transverse misalignment
Beam position on FOMZ1GAF
Beam position on FOMZ1GAF
Beam position on FOMZ1GAF
Tracking data:
Solenoid field variation -0.2T – 0.2T
-> uniform distr. offsets:
  Dx, Dy = 0.22, 0.25, 0.28 mm
  Dq = Dj = 0
PCE
model

## Slide 10
Example
Tracking data:
Solenoid field variation -0.2T – 0.2T
-> uniform distribution
Offsets:
  Dx = Dy = 0.25 mm
  Dq = Dj = 0
PCE model:
Test data:
solenoid field variation -0.4 T - 0.4T
Dx, Dy = 0.23mm - 0.27mm
-> random distribution
Calculate surrogate model for beam position on screen for transverse solenoid offsets
Beam position on FOMZ1GAF
Beam position on FOMZ1GAF
Beam position on FOMZ1GAF
Tracking data:
Solenoid field variation -0.2T – 0.2T
-> uniform distr. offsets:
  Dx, Dy = 0.22, 0.25, 0.28 mm
  Dq = Dj = 0
PCE
model
PCE calculation:
3 uniform input distributions: Sol, Dx, Dy
3x3x21=189 tracking runs
2 ‘Quantities of Interest’, QoI: pos-x, pos-y
Polynomial series order 7
msec runtime

## Slide 11
Setting up the PCE model*
* Matthias Frey, Andreas Adelmann: arXiv:2001.10411v4 [physics.comp-ph] 2 Sep 2020
** Bruno Sudret, “Surrogate models for global sensitivity analysis - Old and New”, 8th International Conference on Sensitivity Analysis of Model Output
d: number of input variables
p: order of the polynomial series
No. of polynomial coefficients to be determined (once):
Recommended no. of sample points to be calculated:
d | p | coeff. | no. SP
3 | 3 | 20 | 64
3 | 5 | 56 | 216
5 | 7 | 225 | 32768
10 | 7 | 3003 | >1e9
Need to test order of polynomial series :
Quality of PCE for different polynomial orders in L2-norm (hor. position on screen)
** “curse of dimensionality” –other math. option: “low-rank tensor approximation” linear in p, d

## Slide 12
Sensitivity analysis and Sobol’s coefficients
* Wikipedia: Variance-based sensitivity analysis
Bruno Sudret, “Global sensitivity analysis using polynomial chaos expansions”, Reliability Engineering & System Safety Volume 93, Issue 7, July 2008, Pages 964-979
Bruno Sudret: ETH Zurich, Professor of “Risk, Safety and Uncertainty Quantification”
Variance-based Sensitivity Analysis quantifies numerically the contribution of uncertain inputs (taken individually or in combinations) into output uncertainty; *
Sobol’s indices are obtained analytically, at any order, from the coefficients of the PC expansion
First order
Sobol’s indices
Second order
Sobol’s indices
Fractional part of the total output variance caused by varying the ith input parameter.
Effect of correlations of the ith input parameter with a single other parameter on output
Variance.
The sum of all Sobol’s coefficients is 1.

## Slide 13
Sobol’s coefficients of the example
import chaospy as cp
Sobol1 = cp.Sens_m(approx7, distribution) first order
Sobol2 = cp.Sens_m2(approx7, distribution) second order
SobolT = cp.Sens_t(approx7, distribution) total
2022-09-19 17:32:31
Sobol indices:
first order (3,2)
poly-order 7
x-pos y-pos
[[9.962e-01 9.962e-01] sol
[1.370e-04 1.020e-04] Dx
[9.600e-05 1.320e-04]] Dy
Sum(pos-x) = 0.99643
Sum(pos-x) = 0.99643
2022-09-19 17:32:58 27sec
2022-09-19 18:02:30
Sobol indices:
second order: (3, 3, 2)
poly-order 7
x-pos
[[0. 0.003 0.001]
[0.003 0. 0. ]
[0.001 0. 0. ]]
Sum(pos-x) = 0.0035607
y-pos
[[0. 0.001 0.003]
[0.001 0. 0. ]
[0.003 0. 0. ]]
Sum(pos-y) = 0.0035636
2022-09-19 18:03:15 45sec
Sol Dx Dy
Sol Dx Dy
Example:
pos-x
pos-y
1. Order Sobol’s indices

## Slide 14
The real problem
Mapping
(tracking /
measurement)
Solenoid misalignment
Dx, Dy, Dtheta, Dphi
Screen measurements
pos-x, pos-y,
sig-x, sig-y
Reverse problem
Create tracking / measured data
with distributed misalignments
Determine distributions
of 4 parameters
on screen
Set up PCE
for joint distribution
for screen data
Fit polynomial coefficients to
determine
misalignments
Solenoid field dominates everything – no solenoid field variation
Actual interest is the determination of the misalignment:

## Slide 15
Preparation 1
Solenoid scan -0.2T – 0.2T, Dx = Dy = 0.25mm, Dtheta = Dphi = 0
Screen dimensions
Beam size strongly depends on solenoid field
Beam size is independent of transverse displacements
Screen size of +/- 25mm, limits the detectable beam size to ~2mm RMS
Solenoid settings >0.1T result in beam sizes that exceed screen
For Sol ~ 0.05T focal point lies at screen – minimal beam size

## Slide 16
Reverse PCE
Create tracking/measurement data:
Solenoid = 0.05T
Random distribution of solenoid positions and angles
-10mm < Dx, Dy < 10mm
-20mrad < Dtheta, Dphi < 20mrad
PCE input: pos-x, pos-y, sig-x, sig-y on screen
PCE output: 4 solenoid misalignments
625 samples
d | p | coeff. | no. SP
4 | 3 | 35 | 256
4 | 4 | 70 | 625
4 | 5 | 126 | 1296
4 | 6 | 210 | 2401
=> Polynomial order 4, (maybe 5)

## Slide 17
Solving the reverse pce
Even polynomial order 4 does not seek satisfactory results!
Need (much) higher order polynomial => too many data points (curse of dimensionality)
Approximate positions and angles separately

## Slide 18
Backward fitting positions only
Create tracking/measurement data:
Solenoid = 0.05T
Random distribution of solenoid transverse offsets
-10mm < Dx, Dy < 10mm
Arbitrary but fixed angular offset
  Dtheta = -5mrad, Dphi=7mrad
PCE input: pos-x, pos-y, sig-x, sig-y on screen
PCE output: 2 solenoid transverse offsets
150 runs, 100 samples, 50 test cases
Position and size on FOMZ1GAF
=> Polynomial order 2, (maybe 3)
d | p | coeff. | no. SP
4 | 2 | 15 | 81
4 | 3 | 35 | 256
4 | 4 | 70 | 625
4 | 5 | 126 | 1296

## Slide 19
Solving the real problem
Perfect fit with second-order polynomial (on sample data)
Perfect prediction for test particles
PCE(pos-x(0), pos-y(0), sig-x(0), sig-y(0)) => DDx, DDy

## Slide 20
Backward fitting example 2
Sobol’s indices 1. order
pos-x
pos-y
sig-y
sig-x
pos-x
pos-y
sig-y
sig-x
Sobol’s indices 1. order
Sobol’s indices 2. order
S1(Dx) + S2(Dx) = 1
S1(Dy) + S2(Dy) = 1
Ok!
 Repeat procedure for angular misalignment
Asymmetry due to different angular offsets
Dx
Dy

## Slide 21
Thanks
Create tracking/measurement data:
Solenoid = 0.05T
Random distribution of solenoid angles
-20mm < Dtheta, Dphi < 20mm
Fixed arbitrary transverse offset
  Dx = -0.2mm, Dy=0.3mm
PCE input: pos-x, pos-y, sig-x, sig-y on screen
PCE output: 2 solenoid angular offsets
150 runs, 100 samples, 50 test cases
pos-x
pos-y
sig-y
sig-x
pos-x
pos-y
sig-y
sig-x
1. order Sobol’s indices
Dtheta
Dphi

## Slide 22
summary
PCE is an extremely powerful and very low-cost tool!
Beam based determination of solenoid misalignment
Impact of measurement errors should be simulated
  How accurately will we determine the beam size? Larger Sol-field?
Surrogate models including field flatness, cathode retreat, laser pulse length,
  laser spot size, solenoid field, and gun voltage look promising – not yet reverse
HZB active in AI: neural network-based model with 13 gun variables
~2.0 Mio data points needed; model dependent;

## Slide 23: Backup transparencies

## Slide 24
Context: bERLinPro
bERLinPro / SEALAB
bERLinPro 2010 – 2020
Energy Recovery Linac project @ HZB
  all superconducting (gun-booster-linac)
  50MeV
  Emphasis on high current (100mA)
    High current SRF gun
    Linac with high power HOM couplers
    600kW beam dump
  Warm machine and infrastructure all ready
  Project terminated without SRF modules running
Since 2021 SEALAB (SRF Electron Accelerator LABoratory)
  Operation and use of SRF gun and booster within
    “Accelerator Research and Development” (ARD)
    framework of the Helmholtz Association
Current status Gun:
  Cold string disassembly for integration of a different cavity
    and different (conditioned) couplers
  Gun module installed in bunker waiting for cold mass
  Cathode exchange training with transfer system
  RF commissioning, first electrons 2023
Current status Booster:
  Assembly after gun assembly and commissioning
Linac: not financed so fare

## Slide 25
Preparation 2
Solenoid scan -0.2T – 0.2T: very distinct signature for positive or negative transverse offsets
Sign of transverse offsets can be detected beforehand
Scan over respective quadrant is sufficient

## Slide 26
bERLinPro Injector
2 Q
Laser:
1-spot size
2-pulse length
3-charge
Cathode (CKSb):
4-retraction
Gun field:
5-amplitude
6-field flatness
Solenoid:
7: strength
Booster:
8-13: cavity phases and amplitude
Diag. Line
18,19 quadrupoles
Screens
TDC /
spectrometer
measurements
BP
Merger:
14-17: quadrupoles
19 ‚knobs‘ total
4 BPMs

## Slide 27
Sensitivity analysis and Sobol’s coefficients
* Wikipedia: Variance-based sensitivity analysis
Bruno Sudret, “Global sensitivity analysis using polynomial chaos expansions”, Reliability Engineering & System Safety Volume 93, Issue 7, July 2008, Pages 964-979
Bruno Sudret: ETH Zurich, Professor of “Risk, Safety and Uncertainty Quantification”
Variance-based Sensitivity Analysis quantifies numerically the contribution of uncertain inputs (taken individually or in combinations) into output uncertainty;
Sobol’s indices are obtained analytically, at any order, from the coefficients of the PC expansion
*Variance decomposition: Model Y = f(X), X = (x1, x3, x3 … xd), xi = uncertain model input parameter
First order
Sobol’s indices
Second order
Sobol’s indices