## Slide 1: SRF Systems for the EIC Hadron Cooling
Bob Rimmer
On behalf of the EIC SRF team
ERL22 workshop, Cornell
Oct 3-6, 2022

## Slide 2: Outline
Overview of EIC RF systems
Ongoing SRF R&D
  591 MHz ESR
  197 MHz Crab
  394 MHz ESR crab first look
  FPC and BLA progress
5-cell cavities required
  HSR, RCS and COOLER
  Possible low energy pre-cooler
  197 MHz QWR
  Shared injector
Modular cryostat
Summary

## Slide 3: EIC RF systems
Both rings –crab cavities
Hadron – 49.2 MHz and 98.5 MHz bunch splitter cavity
Hadron - 591 MHz bunch compression cavity
3
Electron - 591 MHz electron storage cavity
Hadron Cooling - 591 MHz acceleration cavity
Hadron – 24.5 MHz acceleration cavity
Hadron - 197 MHz bunch compression cavity
Rapid Cycling Synchrotron - 591 MHz acceleration cavity

## Slide 4: ESR RF system
Up to 68 MV using 17 new 591 MHz 1-cell SRF cavities
  maintain 1% Bucket height from 5-18 GeV
  Naturally short bunch length <1cm
  10MW maximum beam power
  >40 kW HOM power per cavity
  2.5A maximum current
Two fundamental power couplers per cavity, ~400kW ea.
  Thermal analysis under way
Developed asymmetric option
  25% shorter, 11% lower loss factor, power to remaining large BLA up 13%
  Eliminates one taper, more space for FPC
  Fits better in IR10 available space.
Preparing for prototype cavity fabrication
  Nb sheet and die material in hand
  Fabrication plan and die designs in progress
New asymmetric design

## Slide 5
EIC Crab Cavity Systems
 | Vt [MV] |  | No. of cavities (per IP) | 
System | HSR | ESR | HSR | ESR
197 MHz | 33.83 | – | 8 | –
394 MHz | 4.75 | 2.90 | 4 | 2
HSR will be installed with two 197 MHz RFD cryomodules and one 394 MHz cryomodule each side of the IP Total length < 12.5 m
ESR requires only one 394 MHz cavity each side of the IP
Impedance budget allows for second IP
197 MHz crab cavity is identified as one of first RF cavities to be prototyped
FPC
Pick Up
VHOM
Dogbone
HHOM
Dogbone

## Slide 6: ESR 394 MHz RFD Crab Cavity
Beam aperture = 100 mm
394 MHz design for the ESR has tighter impedance budget
Total impedance budget: Zz = 2.6×104 Ω-GHz and Zt = 0.96×106 Ω/m
Per cavity: Zz = 6.5×103 Ω-GHz and Zt = 0.24×106 Ω/m (For 4 cavities considering the two IPs) With increased crossing angle at the second IP, no of cavities may need to be increased to 8
  Will reduce the impedance threshold per cavity
WOW type crab cavity as the backup plan
Property | Bare Cavity | 
Operating frequency | 394.0 | 
1st HOM [MHz] | 537 | 
Ep/Et* | 3.87 | 
Bp/Et* [mT/(MV/m)] | 8.08 | 
Bp/Ep [mT/(MV/m)] | 2.09 | 
G [Ω] | 125.4 | 
R/Q [Ω] | 308.6 | 
RtRs [Ω2] | 3.9×104 | 
Vt [MV] | 2.9 | 1.45
Ep [MV/m] | 29.5 | 14.75
Bp [mT] | 61.56 | 30.78
Total Vt [MV] | 2.9 | 
No. of cavities | 1 | 2
Cavity Length [mm] (iris-to-iris) | 535.6 | 
Cavity Diameter [mm] | 356.3 | 
Pole Length [mm] | 300 | 
* Et = Vt/(λ/2)
Single ridged waveguide cross section
Preliminary

## Slide 7: High power FPC Status
A high power ( CW 500 kW standing wave) alumina window FPC was designed for EIC ESR SRF cavity.
The design was reviewed by an international technical review committee in June 2021.
The review committee stated their “support moving forward with this design into prototype stage”.
Detailed engineering design for window and vacuum side has been finalized and in the process of prototyping.
FPC airside is almost finalized, purchasing materials for fabrication.

## Slide 8: HOM damper R&D status
First outgassing test were completed with solid SiC HOM damper.
Low power measurement on solid SiC HOM damper, result is close to expectation.
SiC samples were ordered and RF properties measurements are ongoing
Back up segmented design being developed via SBIR
8

## Slide 9: HSR RF system
Keep existing 6 MV 6x197 MHz NCRF system
Re-tune existing 2x 28 MHz system to 24.6 MHz
Add 2x 49.2MHz and 2x 98.5MHz NCRF for binary bunch splitting
Add 20 MV 591 MHz SRF system
Up to 0.75A beam, up to 1160 bunches
Optimum detuning for reactive power (like LHC)
Beam loading transient and collective effects studies started
Hadron – 24.5 MHz acceleration cavity
Hadron – 49.2 MHz and 98.5 MHz bunch splitter cavity
Hadron - 197 MHz bunch compression cavity
Hadron - 591 MHz bunch compression cavity

## Slide 10: RCS
RCS- 591 MHz acceleration cavity
Requires rapid acceleration of one or two high charge bunches per cycle for full energy injection
3x 591 MHz 5-cell cavities
Bunch merging to achieve peak bunch charge
Harmonic injection kicker into RCS
Fast kickers for injection into ESR
Harmonic kicker cavity
new

## Slide 11: Cooler 591 MHz 5-cell
In CDR common design assumed for HSR, RCA and cooler ERL
Baseline scaled from ESR 1-cell
  Warm BLA HOM dampers
  Symmetric FPC’s
  Long tapers
ERL has the most 5-cell cavities
  Lower HOM power
  Tight space constraints
  Evaluating other HOM options
591 MHz 5-cellcavity

## Slide 12: Strong Hadron Cooler ERL layout
400-500kV DC gun for 100 mA of beam and 5.6 MV SRF injector
Dogleg ERL merger
149 MeV Superconducting Energy Recovery LINAC
Electron and hadron overlapped cooling sections.
Amplification section with chicanes and triplets for electrons
Hadron chicane path length matching & R56 adjust
Return transport of electron beam to ERL
Possibility to include injection pre-cooler in the same location
591 MHz 5-cells +
1773 MHz 5 cells
197 MHz QWR

## Slide 13
The SRF cavities for the cooler-ERL
A single-cell elliptical cavity @ 591MHz (booster)
A five-cell elliptical cavity @ 591MHz (Linac)
197 MHz QWR (booster + precooler)
Small beam pipes, weak HOM damping
Large beam pipes, strong HOM damping
HOM dampers
FPC

## Slide 14: Compact 5-cell options
210mm
DIA
150mm
DIA
WAVEGUIDE END GROUPS
For 100 mA HSR cavity may be overkill
Standard 5-cell
Two per string
Compact end groups
  Waveguide
    JLab, HZB
  Coaxial
    HERA, LHC,
    TESLA, C100
Need more analysis
COAXIAL END GROUPS

## Slide 15: Modular cryostat
Based on SNS cryostat dimensions
High degree of commonality of components
Takes advantage of much existing tooling
Cryogenic distribution TBD (SNS PPU shown)
ESR 591 MHz 1-cell
HSR 591 MHz 5-cell
Also RCS and ERL
HSR 197 MHz crab
And others!
394 MHz crab
197 MHz QWR
1773 MHz elliptical
Cooler injector

## Slide 16: Summary
Continuing to develop SRF designs
  ESR 591 MHz asymmetric cavity
  197 MHz Crab cavity
  394 MHz RF design starting, not just a simple scaling
  FPC and BLA R&D progressing according to plan
  Cooler ERL is a challenging machine by itself
    591 MHz 5-cells can be developed from the 1-cell
    Baseline BLA HOM damping
    More compact options possible
    197 MHz and 1773 MHz also needed
Modular cryostat
  Will speed up development, minimize total design effort

## Slide 17: Thank You
References:
EIC Conceptual Design Report, 2021, https://www.bnl.gov/ec/files/EIC_CDR_Final.pdf
Design of the Electron Ion Collider Electron Storage Ring SRF cavity, J. Guo et. Al., Proc. IPAC22
HOM damper design for BNL EIC 197MHz crab cavity, Binping Xiao et. al. Proc IPAC21, Brazil

## Slide 18: Back ups

## Slide 19: Strong Hadron Cooler ERL Specifications
The EIC cooler ERL features unprecedented beam current and small energy spread.
The 1D cooling simulation yields a cooling rate higher than the IBS heating.
Case 100 GeV 275 GeV
Electron Energy (MeV) 55 150
Electron Norm. Emit. (x/y) (mm-mrad) 2.8 / 2.8 2.8 / 2.8
Repetition rate (MHz) 98.5 98.5 Electron Bunch Charge (nC) 1 1 Electron Peak Current (A) 8.5 17 Electron Bunch Length (mm, rms)* 14 7 Electron Fractional Energy Spread 10-4 10-4 Hor./Vert. Elec. Betas in Modulator (m) 86.6 / 14.1 64/ 11
Hor./Vert. Electron Betas in Kicker (m) 49.7 / 10 16 / 2 Modulator Length (m) 55 55 Kicker Length (m) 55 55
H/V/L Cooling time(hr) 1.3/2.5/1.7 0.8/2.1/1.2
* Gaussian bunch assumed

## Slide 20: New design: SHC+precooler injector and Linac
R56=0.475 m
off-crest=30 deg
off-crest=1.2 deg
Precooler bunch charge is 2 nC for 10-4 dp/p, 197 MHz cavities will be needed.
SHC takes advantage of using 197 MHz and compresses the beam at 14 MeV using chicane.
The chicane has four dipoles for 14 MeV beam and other three dipoles for high energy return beam. They have the same time of flight.
Using 591 MHz+1774 MHz cavity to accelerate beam to the cooling energy.

## Slide 21
QWR HOM coupler tuning
Case | 28 | 39 | 40v1 | 40v2 | Target
Fundamental mode | 8.33 | 8.33 | 8.33 | 8.32 | 8.33
Dipole Mode 0 | 5.96 | 3.03 | 5.47 | 2.59 | 2.0
Dipole Mode 2 | 4.23 | 2.13 | 8.66 | 0.361 | 1.8
Dipole Mode 11 | 10.6 | 7.0 | 0.052 | 0.072 | 5.0
Qext (x105)
dipoleModeQ[0] = 2.0e5;
dipoleModeQ[2] = 1.8e5;
dipoleModeQ[11] = 5.0e5;

## Slide 22
cav_OR
cav_IR
gap_L
cav_L
Rounding_2
Starting point and geometry parameter scanning
cav_OR = 305 mm
cav_IR = 125 mm
cav_L = 408 mm
gap_L = 150 mm
Shaoheng Wang

## Slide 23
The 4th order Butterworth filter
The 9th order Chebyshev filter
The TESLA type
Alternative models for the HOM damper (transmission part)

## Slide 24
HOM spectrum pre-cooler 23.8 GeV Case, with Gap
ERL Mode
Electron bunches in one proton bunch interval
Electron bunches in one proton bunch interval

## Slide 25
ERL Challenges
1 kW
10 kW
100 kW
1 MW
10 MW
100 MW
1 GW
legacy
operating
under construction
proposed
S-DALINAC
CW with Pbeam>PRF
EUV FELs
CW multi-XFEL
EIC Cooler ERL
Low noise electron beam
High current ERL
Beam halo
BBU
Ion trapping
High current high charge electron source (EIC R&D)
Beam diagnostics: beam noise, beam halo, e-h alignment (~250 nm), energy spread measurement(<1e-4).