## Slide 1: Concept of a High-Power Linear Proton Accelerator
V.S. Morozov, RAD, SNS, NScD, Oak Ridge National Laboratory, Oak Ridge, TN
Consider RLA3: MeV, MV
2 m cavity spacing
Optimization problem with many local minima, use GA with population of 100k and 1k iterations
Linac Timing
Problem: incomplete use of available power by some of the cavities, the bottle neck is the current limit of the higher-energy linac section Solution: recirculate the beam through lower-energy sections up to their power limits

Problem: inefficient acceleration on the 2nd and subsequent passes due to loss of beam synchronization with the linac RF Solution: use larger number of passes to compensate for the loss of acceleration efficiency while staying under the cavity power limit

Problem: impractically large number of recirculation arcs Solution: use FFA arc optics

Problem: complicated arc to linac matching section Solution: adiabatic match
Optimization Concept
We present a new concept of a compact high-power linear proton accelerator with an average power of 10 MW at a kinetic beam energy of 1 GeV. Acceleration is accomplished in several stages. In each stage, the beam is recirculated a few times through the same set of SRF cavities. To avoid the complexity of multiple recirculating arcs and especially of multi-pass beam spreaders and recombiners, we implement the Fixed-Field Alternating-gradient arc design and adiabatic matching approach where all beam passes are transported and matched to the accelerating sections in a single beam line.
Abstract
Multiple applications
  Fundamental research
    Generation of high-flux neutron beams
    Neutrino, muon and kaon physics
  ADSR
    Production of electricity and heat
    Production of liquid fuels
    Processing of spent nuclear fuel
    Use of Pu and Th
  Applied research
    Nuclear medicine
    Generation of radioisotopes
    Material science
Natural follow up to the PPU and STS
Combined with ORNL’s reactor expertise, provides a path to ADSR
Motivation
Energy gain per cavity as function of for SNS, ESS, MYRRHA, Project X, JAEA ADS, CiADS, and HC HP-SPL
All these and other explored projects are straight linacs
Assume maximum coupled cavity power of 300 kW
Review of Existing Designs
Utilize the maximum RF power that can be provided by a cavity by recirculating the beam
Assume each FFA arcs covers a momentum ratio of 2 (Transition energies approximately align with SRF technology change points)
Number of cavities
  RLA:
  Straight linac:
Potential reduction in cavity number from ~160 to ~40
Acceleration Scheme
Bend allows for efficient tunnel use
Short cryogenic and RF power lines
Total circumference of ~400 m
Accelerator Layout
Arc FODO cell using combined function dipole magnets with quadrupole field components
Maximum field of 1 T at 20 mm radius
Consistent with permanent magnet technology
Adiabatic match of arcs to linacs using 22 cells
Cell parameters scale as
, ,
Arc Optics
Work supported by UT-Battelle, LLC, under contract DE-AC05-00OR22725 with the US DoE through LDRD project, LOIS 10908.
Acknowledgements
MeV
Deceleration
Acceleration
Linac
Arc