## Slide 1: WG2: Beam Dynamics and Instrumentation
Meghan McAteer Helmholtz-Zentrum Berlin
Alex Bogacz Jefferson Lab
ERL 2022, 66th ICFA Advanced Beam Dynamics Workshop on Energy Recovery Linacs

## Slide 2: The Ghost Collider
The Ghost Collider is a new concept for a high-energy, high-luminosity e+e- collider.
Accelerating electrons and decelerating positrons in the same bucket eliminates higher order mode excitation.
Interestingly, this means that there is no need for large aperture SRF cavities and high-power HOM couplers.
The Ghost Collider adds the concept of four-beam collisions to remove beam-beam interactions and disruption.
This concept brings up a series of new beam dynamics problems which make optimization of the parameters difficult, but exciting!
Andrew Hutton

## Slide 3: Optimizing beam filling patterns for multi-pass ERLs
Filling patterns and bucket transitions can drastically affect the performance and stability of ERLs
The developed mathematical formalism allows us to perform comprehensive studies to find a global optimum
This formalism allows for other applications such as optimisation of arc lengths
Rob Apsimon

## Slide 4: ERL Longitudinal Matches for Light Sources
Compressive match (FEL)
Energy spread minimization (FEL)
Common transport complications
Possible longitudinal matches
Construction of self-consistent longitudinal matches in multipass energy recovery linacs
Gustavo Perez Segurana

## Slide 5
S-DALINAC Twice recirculation SRF multi-turn ERL
S-DALINAC uses common beam transport
Reduced number of degrees of freedom for
  Transverse confinement
  Target momenta and momentum spread control
Beam-dynamics simulations prior to beam tuning necessary
Operating with low momenta can increase efficiency, but phase space has to be taken into account
Simulation results have been used to tune machine and realize twofold ERL in August 2021
First proof of efficiency in a SRF multi-turn ERL by measured beam loading decrease
Efficiency of up to 87 %
F. Schliessmann et al., publication under review
Felix Schliessmann

## Slide 6: Closed lattice design for EIC SHC-CeC ERL
Colwyn Gulliford

## Slide 7
Polynomial Chaos expansion
quantifies uncertainty in parametric systems
provides surrogate models
works on relatively few data point
easy to implement & fast
Create tracking / measured data
with distributed misalignments
Determine distributions
of 4 parameters on screen
Set up PCE
for joint distribution
for screen data
Fit polynomial coefficients to
determine
misalignments
Reverse PCE
Beam-based determination of solenoid transverse misalignment
using 100 sample points and a polynomial series of second order.
Sobol’s indices reveal the dominant impact of beam size determination
for uncertainty in the result.
Surrogate model determining
beam position on screen.
Bettina Kuske

## Slide 8
Beam Dynamics Studies of PERLE
Reduction of the bunch length to 1.4mm avoiding longitudinal effects from the RF cavities until a lattice featuring longitudinal matching is available.
Phase space at the dump from lossless tracking studies including CSR at nominal current with a reduced bunch length hence it seems comfortable with the nominal bunch length.
Multi-bunch tracking is stable at nominal current, the optimisation of the bunch filling pattern does not show unstable HOMs up to 10 times the nominal current as opposed to the original filling pattern.
Original filling pattern
Original filling pattern
‘Regular’ filling pattern
‘Regular’ filling pattern
Kevin Andre

## Slide 9: IR-FEL
Example of AI tuning (~ 3 hours)
U1 matching
R56, SX
U2 matching
U2 orbit
U2 orbit
R56, SX
R56, SX
R56, SX
ML2
Buncher,inj
U2, R56
We try AI beam tuning for maximizing IR-FEL intensity. It makes the beam tuning highly effective because 3~6 parameters are optimized at once
Beam tuning at Compact ERL after installing undulators
cam8
Beam halo
250 mA for 2 hours
The 250uA current operation is successful with low radiation level by collimating the halo and tail at low energy
High current operation at CW mode
Miho Shimada

## Slide 10: CBETA Instrumentation
Electron source
Injector cryomodule
Merger
Main linac cryomodule
Splitter A
Splitter B
Dump
FFA
Arc A
FFA
arc B
FFA
Transition A
FFA Transition B
FFA straight
Diagnostic line
DU
LA
IN
DI
SX
FA
TA
FB
TB
RX
ZA
ZB
ZM
Beam energy with each MLC pass:
6 to 42 MeV 150 to 114 MeV
42 to 78 MeV 114 to 78 MeV
78 to 114 MeV 78 to 42 MeV
114 to 150 MeV 42 MeV to 6
Robert Michnoff
view screens, beam position monitors (BPM), phase measurement bunch arrival monitors (BAMs), slow loss monitors and fast loss monitors

## Slide 11: CBETA Multi-Turn Performance Studies and Beam Dynamics Issues
Halo after injector
Quad centering (through S1-R1 splitters)
Tool: Quads as BPMs
1-turn commissioning (piecewise SVD correction)
1-turn intensity
Semi-empirical response matrix
Real full response matrix for diagnostic use
Tool: get_all_tunes for day-to-day tune variation
Multi-turn response matrix and correction
4-turn intensity
4-turn tunes vs. model
Tool: accelerating vs. decelerating splitter orbits
TOF adjustment
Degaussing
Closed bumps
Stephen Brooks
Full Response Matrices from CBETA-V
FFA correctors  FFA BPMs