## Slide 1: Uses & Applications WG Summary
Peter Williams & Erdong Wang

## Slide 2: Zhao: ERL Based Fully Coherent Light Source
We report a new method for high repetition rate fully coherent pulse generation by taking advantages of the ERL and ADM.
The proposed light source holds the merits such as fully coherent radiation with a brightness 5–6 orders of magnitude higher than that of a DLSR with the same beam energy, and much higher repetition rate comparing with an FEL.
We also proposed two future ERL light sources to generate fully coherent EUV and X-ray radiations, and we considered a multi-radiation source system consists of DBAs and radiators to support multi-user operation.
However, limited by the photoinjector and the HOM BBU effect, the 100-mA-level average current is a big challenge. Meanwhile, dominated by the injector, the energy jitter, temporal jitter and the temporal stability might become larger than storage rings.
The ADM scheme has not been experimentally demonstrated yet, but a proof-of-principle experiment of ADM is under preparation at SARI.

## Slide 3: Nakamura: ERL based EUV-FEL light source for lithography
Main Linac
Injector Linac
Beam Dump
Undulators(FEL)
1st Arc
2nd Arc
150 ~ 200 m
~20 m
Gun
Merger
Injector Diagnostic Line
©Rey.Hori/KEK
EUV Light
Advantages (compared to LPP source) :
(1) High EUV power ( > 10 kW ) without Tin debris
 1-kW EUV power x 10 scanners
(2) Upgradable to a Beyond EUV(BEUV) FEL (6.6 - 6.7 nm)
(3) Variable control of polarization
 polarization use for high-NA lithography
(4) Low electricity consumption
 carbon neutral & sustainability
ERL based EUV-FEL light source
Parameter | Design value
Beam Energy | 800 MeV
Bunch Charge | 60 pC
Bunch Repetition | 162.5 MHz
Average Current | 10 mA
RF Frequency | 1.3 GHz
EUV Wavelength | 13.5 nm
EUV Power | > 10 kW
N. Nakamura et al., Proc. ERL2015, pp.4-9(2015)
H. Kawata et al, J. Micro/Nanopattern Mater. Metrol. 212(2), 021210(2022)
EUV-FEL power with 4% tapering: 17.8/35.5 kW @ 9.75/19.5 mA (162.5/325 MHz)
109.4 mJ
79.2 mJ
N. Nakamura (KEK)
Bandwidth of
Mo/Si reflectivity

## Slide 4: Beck: “Wishlist” for next-generation photon sources
With the advent of LCB-generated photon beams, the field of photonuclear reactions experienced a renaissance. A next-generation photon source based on a multi-turn SRF-ERL offers critical improvements:
    narrower bandwidth
                selective manipulation of single excited states
    reduced beam-spot size
                improved spatial resolution
    increased luminosity
                competition with low cross-section
Tobias Beck, ERL’22, 05.10.2022

## Slide 5
Kayran: ERL potential as a g-ray source
Dmitry Kayran and Vladimir Litvinenko
Brookhaven National Laboratory Stony Brook University
Why Compton g-ray sources?
Conclusions
The backscattering Compton sources are promising high intensity, monoenergetic and high brightness γ-ray beams
Combination of high current Energy Recovery Linacs with high power lasers (both the “conventional” and FEL with only 100 kW of intra-cavity power!) opens possibility of generating a few order of magnitude higher flux of g-rays then currently available
Such sources can find applications expending from the high energy and nuclear physics to medical application and potentially disposal of radioactive waste

## Slide 6: Bernauer

## Slide 7: Hug: MESA Experiments
P2 experiment:
High target density, 0.15mA
External beam mode (EB)
Luminosity >1039 cm-2s-1
MAGIX experiment:
low target density, 1mA
Energy recovery mode (ERL)
Luminosity >1035 cm-2s-1
DarkMESA: Beam dump experiment running parasitically to P2
Versatile facility for nuclear physics, particle physics and dark sector searches
High accuracy in beam stability, energy spread and polarization needed
H.Merkel Talk at DPG Springmeeting 2022
Operation-modes | Target | Beam power@target
Ext. Beam (EB) | Solid/ Liquid | 0-25kW
Energy recovery(ERL) | Gas-jet | 0.1-1MW

## Slide 8: Wang: Strong Hadron Cooling in EIC with an ERL
EIC Strong hadron cooling is based on a coherent electron cooling concept using the micro-bunching amplifier.
It will boost EIC luminosity by a factor of 3-10.
The cooling needs a high-quality electron beam with 100 mA high current, 10-4 small energy spread, and small noise in the beam. It requires the development of an ERL with parameters beyond the state of the art.
Our simulations show that beam quality, energy spread, and beam noise can meet the cooling requirement.
E<E0
E>E0
Modulator
Kicker
H+
e-
R56
R56
R56
Case 100 GeV 275 GeV
Electron Energy (MeV) 55 150
Electron Norm. Emit. (x/y) (mm-mrad) 2.8 / 2.8 2.8 / 2.8
Repetition rate (MHz) 98.5 98.5 Electron Bunch Charge (nC) 1 1 Electron Peak Current (A) 10 17 Electron Bunch Length (mm, rms)* 12 7 Electron Fractional Energy Spread 10-4 10-4 Hor./Vert. Elec. Betas in Modulator (m) 86.6 / 14.1 64/ 11
Hor./Vert. Electron Betas in Kicker (m) 49.7 / 10 16 / 2 Modulator Length (m) 55 55 Kicker Length (m) 55 55
H/V/L Cooling time(hr) 1.3/2.5/1.7 0.8/2.1/1.2
H/V/L IBS time(hr) 2/4/2.5 2/5/2.9

## Slide 9
ERL injector 40MeV
Recirculating energy recovery system 1GeV
“non- emitting” Storage Ring (1GeV, 2km –diameter) to provide beams for photon factories and LERC
Photon factories – ERL FELs hubs driven by the Storage Ring
Linear Energy Recovery Collider driven by storage ring
Konoplev: Circular-Linear energy recovery accelerator to probe the energy-frontier
I.V. Konoplev, S.A. Bogacz, Ya. Shashkov
Asymmetric dual-axis cavity
ILC
CLER-C

## Slide 10
Common features
  Recycling of used particles
  Energy recovery & High luminosity
  High polarization of both e+ and e- beams
Differences
  ReLiC has potential of operating at higher luminosity and higher energy that CERC
Litvinenko: ReLiC and CERC: polarized e+e- colliders
Vladimir N Litvinenko, Nikhil Bachhawat, Yichao Jing, Francois Meot, Maria Chamizo Llatas, Irina Petrushina and Thomas Roser
SRF linac 1
SRF linac 2
Damping positron ring
Damp electron ring
ReLiC: Recycling Linear Collider
CERC: Circular Energy-Recovery Collider

## Slide 11: Serafini: Electrons and X-rays to muon pairs (EXMP)
Strongly asymmetric collision: relativistic Doppler → ECM above MPP threshold
Ee=500 GeV, hn=60 keV
Recoil parameter X=4gehn/Me=4.6∙105
Camilla Curatolo and Luca Serafini, Electrons and X-rays to Muon Pairs (EXMP) Appl. Sci. (2022), 12(6), 3149
GeV muon beams with picometer-class emittance from electron-photon collisions, ArXiv (2021)
normalized rms transverse emittance @ source
Nm~1011 /s
muon production in-vacuum → no target handling, no cooling
no beam-beam, no ring → very tight focus allowed, L ~ 1042 cm-2 s-1
av. curr. 200 mA
av. curr. 200 mA