## Slide 1
Aberration Corrector Tuning with Machine-Learning-Based Emittance Measurement and Bayesian Optimization
Chenyu Zhang1, Zhaslan Baraissov1, Cameron J. Duncan 2, Adi Hanuka3, Auralee L. Edelen3, Jared M. Maxson2, David A. Muller1
1 School of Applied and Engineering Physics, Cornell University, Ithaca, 14853, NY, USA
2 Cornell Laboratory for Accelerator-Based Science and Education, Cornell University, Ithaca, NY, 14853, USA
3 SLAC National Laboratory, Menlo Park, 94025, CA, USA
20 mrad
Aberration corrector
Electron Ronchigram
Bayesian optimization
Automatic tuning
Notes: Going to be an overview

## Slide 2
Probe Aberration and Aberration Corrector
Aberration corrector is an important component of scanning transmission electron microscope (STEM).
Aberration function describing the difference between actual wavefront and a spherical wavefront.
Aberration corrector cancels the aberration with a series of magnetic multipoles.
Advanced Transmission Electron Microscopy, ISBN 978-1-4939-6605-9
Ultramicroscopy 189 (2018): 46-53.
Atomic resolution image of Si <110> without (a),(b) and with (c), (d) aberration corrected.
Schematic of actual wavefront W’ and spherical wavefront WR
Notes: Convention of describing aberration in EM community, and we adopted emittance from accelerator community.

## Slide 3
Beam Quality Metric: Emittance Growth
Emittance growth(ε): increase of volume of beam in the phase space.
Single measurement of beam quality.
Minimized emittance gives highest brightness.
Minimum aberration
Defocus
Spherical Aberration
Emittance vs other aberration metrics for random aberration combinations
Consistent with other metrices such as phase difference.
3

## Slide 4
Electron Ronchigram: shadow image of a thin layer of amorphous material.
Center flat area: region with infinite magnification. All rays within this area go through the same point on the sample.
In a simple way: maximize the area of center flat region.
Next: estimate emittance from Ronchigram.
Ronchigram with (a) and without (b) spherical aberration corrected.
Beam Monitor: Electron Ronchigram
4

## Slide 5
Predict Emittance with Convolutional Neural Network (CNN)
Training data: simulated Ronchigrams
Training label: normalized emittance + normalized defocus as training label, between 0 and 1. A score of the probe quality.
Architecture of a VGG16 network.
https://ieeexplore.ieee.org/document/8258115
Extreme cases
~0 aberration and defocus
1 mm C3 and 1 μmdefocus
20 mrad
Examples of training Ronchigrams
Included different imaging conditions: noise level, center shift, collection angles.
5
Electron Ronchigram
Emittance

## Slide 6
Validate CNN Performance
A new set of simulated data to validate CNN performance.
Robust against changes in acquisition conditions.
Next: Minimize the output from CNN.
20 mrad
6

## Slide 7
Bayesian Optimization (BO)
Observations:
Predict
Inform next point
Global optimization of a black-box function.
Explore high-dimensional parameter space to optimize a single objective.
Predict underlying function and inform next acquisition.
Used Botorch as implementation.
https://en.wikipedia.org/wiki/Bayesian_optimization
Duris, Joseph, et al. "Bayesian optimization of a free-electron laser." Physical review letters 124.12 (2020): 124801.
7

## Slide 8
Bayesian Optimization
20 mrad
Normalized ε + defocus
Hexpole Strength (T/m2)
Electron Ronchigram
Convolutional Neural Network
(parameter, emittance)
Instrument parameters
8

## Slide 9
Optimization on GPT Simulation Model
Hexapole corrector model simulated by general particle tracer (GPT).
Model provided by Cameron Duncan.
Control magnetic lens strength, to get the Ronchigram that minimize CNN output score.
Overview of the corrector simulation model
HP: Hexapole SOL: Solenoid
9
Initial Ronchigram
Rough tuning
Fine tuning
30 mrad
20 mrad
Optimization process from random starting points
Two step tuning with aperture applied on fine tuning step.

## Slide 10
Benchmark Test, 2D Parameter Space
Bayesopt: https://github.com/fmfn/BayesianOptimization
Gpy: https://sheffieldml.github.io/GPy/
Simplex: scipy.optimize.minimize, method = ‘Nelder-Mead’
SLAC GP: https://github.com/adkoo/Bayesian-optimization-using-Gaussian-Process
Botorch: botorch.org
BOtorch
Test four different implementations of Bayesian optimization, and simplex method.
Benchmark test on 2 parameters and the parameter space
SLAC-GP
GPy
Simplex
BayesOpt
20x20 grid search
10
More measurement around minimum.

## Slide 11
Benchmark Test, 6D Parameter Space
11
Averaged convergence for different method on 6D parameter space
BoTorch has more reliable performance with higher-dimensional parameter space.
Using GPT model:
Able to automatically tune corrector system with six parameters.

## Slide 12
Alignment on a Real Aberration Corrector
http://www.nion.com/products.html
Controls pre-calibrated aberration coefficients.
12
Simulated new CNN training data as a result of different imaging conditions.

## Slide 13
Validate with experimental data.
Start with manually tuned corrector, perform linescan of each aberration corrector.
Valley shaped curves suggests the trained CNN is able to tell the zero point of each aberration coefficient.
Validate CNN Performance
13

## Slide 14
Correction up to 2nd Order Aberration
14
Optimize the CNN output over a total of 7 input parameters.
Use 20 measurements to initialize the model, then optimize for 100 iterations.
About 0.5 seconds per iteration.
Ronchigrams after optimization
Ronchigrams after initialization
Manually corrected example
iterations
~0.1

## Slide 15
Correction up to 3rd Order Aberration
15
Correct a total of 12 parameters.
Much worse performance when include 3rd order aberrations and increase the number of total parameters from 7 to 12.
>0.2

## Slide 16
Summary
Combination of CNN and BO to tune aberration corrector by minimizing emittance growth.
Faster and automated corrector tuning.
Tested on simulation model of a hexapole corrector and a real aberration corrector.
Test on a new GPT model with misalignment included and more parameters to be controlled.
Improve performance on experiments.
Implement on other STEMs.
Simulated Ronchigrams before and after tuning
Experimental Ronchigrams before and after tuning
20 mrad
20 mrad