## Slide 1: 4D Emittance Measurements for keV Ultrafast Microdiffraction with Stray Sextupole Correction
Matthew Gordon1 , W. H. Li2, A. C. Bartnik2, C. J. R. Duncan2, M. Kaemingk2 , C. A. Pennington2, Y.-K. Kim1, J. M. Maxson2
1University of Chicago
2Cornell University
BDC Theme Meeting
4/14/22

## Slide 2: Motivation
Make a molecular movie
MEDUSA beamline at Cornell
Photocathode with a sub 100 meV Mean Transverse Energy (MTE)
Produces low “temperature” electron beams capable of time resolved diffraction
Preserve good beam quality to the sample

## Slide 3: MEDUSA Beamline
Cathode transfer system
Na–K–Sb Photocathode
Cathode MTE < 100 meV

## Slide 4: Beamline overview
Gun
Final Beam energy: 140 keV

## Slide 5: Beamline overview
Focusing solenoid

## Slide 6: Beamline overview
Buncher
Viewscreen
Beam length: 10 ps <200 fs

## Slide 7: Beamline overview
Second focusing solenoid
Beam size: 100s of Microns 10s of Microns

## Slide 8: Beamline overview
Sample chamber
(Optional Pinhole)

## Slide 9: Beamline overview
Detector

## Slide 10: Correcting Stray Fields
Unintended (stray) fields mainly come from the solenoid and buncher
Non-linear fields and fields that couple x and y reduce beam quality
Quadrupole and sextupole correctors placed after second solenoid
HACLYI

## Slide 11: Quadrupole Correction
Stary quadrupole moment coming from solenoids
Simulated effect of quadrupole on beam quality in General Particle Tracer (GPT)
x-py phase space projection shows uncorrected correlation

## Slide 12: Sextupole Correction
Simulations of correcting a sextupole in GPT
Sextupole placed in buncher, correctors after second solenoid
Rotate angle of corrector and find correct strength

## Slide 13: Sextupole Correction
Sextupole Corrector Off
Sextupole Corrector High Current
Sextupole Corrected

## Slide 14: 4d Phase Space Reconstruction
Bring beam to a focus at pinhole
Use pinhole to pick out a small fraction of the beam
Measure the beam fraction downstream (Intensity/momentum)
Move the beam over the pinhole
Reconstruct 4d phase space
Camera Image of Ce:YAG
100 μm
500 μm
~10 μm steps
screen pinhole separation

## Slide 15: Phase Space 3D Projection

## Slide 16: Phase Space Portraits
Now let’s look at 2D projections
x and y have small correlations (skew quadrupoles corrected)

## Slide 17: Comparison to Simulation
Repeat this reconstruction procedure for different values of buncher voltages around peak bunching with (red) and without (blue) the sextupole corrector
Simulation in GPT with no sextupole in the buncher (red line) and with sextupole in the buncher (blue line)
Matches simulated electron beam with MTE of 80±20 meV

## Slide 18: Conclusions
Corrected stray fields up to sextupole in a UED beamline (MEDUSA)
xy correlation near zero
Electron beam with size and emittance that agrees with a simulated cathode MTE of ~80±20 meV with no stray fields
Performance paper published in Structural Dynamics: A kiloelectron-volt ultrafast electron micro-diffraction apparatus using low emittance semiconductor photocathodes
Paper detailing stray field correction upcoming

## Slide 19: MEDUSA Beamline
Ultrafast Electron Diffraction Beamline at Cornell operating at 140 keV
Record diffraction patterns of materials before + just after being hit with a femtosecond scale laser
Record the difference in the diffraction patterns before and after
Diffraction of Nb3Br8 seen on the final screen, beam stop obscures part of pattern

## Slide 20: Samples
Micron sized samples capable of being studied at MEDUSA
Nb3Br8

## Slide 21: Medusa Laser System

## Slide 22: Full Beamline Schematic

## Slide 23: UED Micro-diffraction Parameters

## Slide 24: UED of Gold Difference Images