## Slide 1
Joint Session Working Groups 1+2
Advanced Accelerator Concepts Workshop (AAC22)
Long Island, NY, USA November 6-11, 2022
Latest advances in the Particle-In-Cell code WarpX for efficient modeling of plasma accelerators at Exascale
Jean-Luc Vay
Lawrence Berkeley National Laboratory
On behalf of the WarpX team LBNL, LLNL, SLAC, CEA, DESY, Modern Electron, CERN

## Slide 2
Outline
2
WarpX overview
Latest advances in WarpX
  Coulomb collision module
  QED module
  a time-averaged pseudo-spectral PIC solver that enables larger timesteps,
  a hybrid nodal-staggered PIC loop that provides improved stability,
  an algorithm to handle particles crossing Perfectly Matched Layers,
  application of mesh refinement to the modeling of ion motion in a plasma accelerator.
Thoughts toward the establishment of a 10-year roadmap for advanced accelerator concepts computation

## Slide 3: Novel BLAST integrated ecosystem of accelerator (& more) codes
BLAST Particle-in-cell Codes
WarpX: t-based EM & ES PIC + lattice
ImpactX: s-based ES + lattice
HiPACE++: Quasistatic PIC (similar to QuickPIC, pyHeadtail, …)

## Slide 4: WarpX: Multi-Physics Particle-in-Cell Code for Exascale
Particle-in-Cell
Geometries
1D3V, 2D3V, 3D3V and RZ (quasi- cylindrical)
Multi-Node parallelization
MPI: 3D domain decomposition
dynamic load balancing
On-Node Parallelization
GPU: CUDA, HIP and SYCL
CPU: OpenMP
Scalable, Parallel I/O
AMReX plotfile and openPMD (HDF5 or ADIOS)
in situ diagnostics
Multi-Physics Modules
field ionization of atomic levels, Coulomb collisions, QED processes (e.g. pair creation), macroscopic materials, embedded boundaries + CAD, …
electro-
magnetic (EM) fields on a grid
macro-
particles
Advanced Algorithms Pioneered by our Team
boosted frame, spectral solvers, Galilean frame, MR, ...
ecp-warpx.github.io
Open source

## Slide 5: New module of Monte Carlo binary interactions
Interaction between macro-particles within the same cell
Physical interactions currently implemented in WarpX:
  Coulomb collisions
  Nuclear fusion (D+T, D+D, P+B11, …)
  Extensible to other interactions (impact ionization, …)
Works on CPU and GPU
  (Uses 1 thread per cell on GPU)
Works in different WarpX geometries:
  2D/3D Cartesian
  RZ (assuming pure cylindrical symmetry)
Used in production:
simulations of emittance growth due to Coulomb collisions
Y. Zhao, et al., Phys. Plasmas 29, 103109 (2022) https://doi.org/10.1063/5.0102919
Y. Zhao, et al., Phys. Plasmas 27, 113105 (2020) https://doi.org/10.1063/5.0023776

## Slide 6: New module for Quantum ElectroDynamic (QED) Processes
QED processes implemented:
  Nonlinear Breit-Wheeler pair production (a photon decays into an electron-positron pair)
  Quantum synchrotron (an accelerated charged particle emits a hard photon)
  Schwinger process (high electric field generates electron-positron pairs)
Works on CPU and GPU
Implemented in the library PICSAR
  github.com/ECP-WarpX/picsar
  Can be used in other codes
Has been used to simulate the interaction of Doppler-boosted lasers with matter and the quantum vacuum
(collaboration with CEA Saclay)
L. Fedeli, et al., New J. Phys. 24 025009 (2022) https://doi.org/10.1088/1367-2630/ac4ef1
L. Fedeli, et al., Phys. Rev. Lett. 127, 114801 (2001) https://doi.org/10.1103/PhysRevLett.127.114801
E. Zoni et al, Comp. Phys. Comm., 279, 108467 (2022) https://doi.org/10.1016/j.cpc.2022.108457

## Slide 7: Time-averaged pseudo-spectral PIC solver enables larger timesteps*
Average fields to gather over 1 time step
Push particles
Field solve in k-space
Gather forces
Deposit currents
FFT: xk
iFFT: kx
*O. Shapoval, et al., Phys. Rev. E 104, 055311 (2021) doi.org/10.1103/PhysRevE.104.055311
Takes advantage of Pseudo-Spectral Analytical Time-Domain (PSATD) solver to average fields analytically
in k-space over one time step before field gather
The fields that evolve with Maxwell’s
equations are untouched (there is no
field damping over time, i.e., no
spurious laser depletion)

## Slide 8: Averaged PSATD PIC speeds up laser plasma accelerator simulations
Standard Galilean PSATD-PIC
Unstable
laser
Averaged field within time step
Averaged Galilean PSATD-PIC
Stable
laser
Example: cΔt=Δz=10Δx
Velocity push:
Sampled fields within time step
 Enables full PIC simulations with computational costs similar to quasistatic PIC.
Dx
Dz=10Dx
*O. Shapoval, et al., Phys. Rev. E 104, 055311 (2021) doi.org/10.1103/PhysRevE.104.055311
~x10
speedup

## Slide 9: Hybrid nodal-staggered PIC loop provides improved stability*
Combines advantages of staggered Maxwell solver with nodal field gather (& current deposition).
Lower numerical dispersion
More compact support of high-order stencil
Higher parallel stability
No interpolation errors (E+VxB)
Higher PIC stability (e.g., numerical Cherenkov instability)
Staggered
Nodal
*E. Zoni, et al., Comput. Phys. Comm. 279, 108457 (2022) doi.org/10.1016/j.cpc.2022.108457
Finite centering = finite order approximation of shift in k-space: e-ikDx/2

## Slide 10: Hybrid nodal-staggered PIC loop provides significant speedup
*E. Zoni, et al., Comput. Phys. Comm. 279, 108457 (2022) doi.org/10.1016/j.cpc.2022.108457
laser
Nodal: stable
Staggered: unstable
Hybrid: order 2
Hybrid: order 4
Hybrid: order 6
Hybrid: order 8
~✕2 speedup simulations of laser-plasma accelerator
More guard cells
Less guard cells
~✕10 speedup simulations of high-field physics with QED effects*

## Slide 11: New algorithm to handle particles crossing Perfectly Matched Layers*
Standard Perfectly Matched Layer (PML)
New terms for particles crossing PML
*R. Lehe, et al., Phys. Rev. E 106, 045306 (2022) doi.org/10.1103/PhysRevE.106.045306
Additional terms are exact solution for absorbing layer for particles crossing PMLs at normal incidence.
Standard PML
PML w/ deposition
PML w/ damped deposition

## Slide 12: New algorithm provides efficient absorption of electrons ejected transversally in LPA simulations
*R. Lehe, et al., Phys. Rev. E 106, 045306 (2022) doi.org/10.1103/PhysRevE.106.045306

## Slide 13: Absorption is less perfect when particles are ejected at a lower angle.
Work is underway to extend algorithms to wider range of angles.
*R. Lehe, et al., Phys. Rev. E 106, 045306 (2022) doi.org/10.1103/PhysRevE.106.045306

## Slide 14: MR bring 2x computational cost reduction in modeling ion motion in LPA
Without Mesh Refinement
(#Nodes)*(Time)
= 32*0.195 = 6.24
With Mesh Refinement
(#Nodes)*(Time)
= 8*0.365 = 2.38
Computational Cost
Estimates
Transverse Field (
Ion Density (

## Slide 15
Outline
15
WarpX overview
Latest advances in WarpX
  Coulomb collision module
  QED module
  a time-averaged pseudo-spectral PIC solver that enables larger timesteps,
  a hybrid nodal-staggered PIC loop that provides improved stability,
  an algorithm to handle particles crossing Perfectly Matched Layers,
  application of mesh refinement to the modeling of ion motion in a plasma accelerator.
Thoughts toward the establishment of a 10-year roadmap for advanced accelerator concepts computation

## Slide 16
Ultimate goal: End-to-end Virtual Accelerator (EVA) with on-the-fly tunability from users of physics & numerics complexity
Reduced physics
Full physics
1D-1V
3D-3V
Low resolution
High resolution
Surrogate models
First principles
Speed
Great for ensemble runs for design studies
Fidelity
Great for detailed runs for physics studies
Present state of the art: complicated command-line workflows; each lab or group has its own code(s)

## Slide 17
Accelerator modeling: the norm used to be life without standards
Different input formats
Input code A
Input code B
Input …
Different output formats
Output Code A
Output Code B
Output …
Code A
Code B
...
Simulation codes
No standards
Fun comparison! Imagine:
the car makers not following standards
 drivers having to learn “from scratch” to drive each car
Difficult for benchmarks, workflows, optimization or AI/ML engines, …

## Slide 18
Complexity in accelerator modeling requires us to work together
Particle-In-Cell
Modeling Interface
open Particle Mesh Data standard
Code A
Code B
...
Simulation code
With standards

## Slide 19
Thoughts toward the establishment of a 10-year roadmap
for advanced accelerator concepts computation
19
Proposal
Ultimate goal: End-to-end Virtual Accelerators (EVA) with on-the-fly tunability from users of physics & numerics complexity
Development and adoption of input/output standards as early activities of roadmap
Development of workflows with plug & play swap of models/codes enabled by standards
Development of EVAs and Virtual Test Stands (VTS) for various AAC thrusts (LWFA, PWFA, SWFA, DLA, …)
Application of EVAs and Virtual Test Stands (VTS) for various AAC thrusts with milestones
  E.g., for LWFA: model chain of 10 multi-GeV stages for HEP collider, maximizing beam charge and energy gain, and minimizing energy spread and emittance growth

## Slide 20
Backups
20

## Slide 21: Transverse resolution scan (without mesh refinement)
Base case :
We decrease by a factor of two
(until convergence), while keeping
Transverse Field (
Ion Density (