## Slide 1
Laser Wakefield Acceleration to GeV Electron Energies for the Breit-Wheeler Experiment
AAC’22
Hyatt Regency Long Island, NY
2022/11/10
F.Salgado
M.Zepf
K.v.Grafenstein F.M.Foerster
F.Haberstroh
A.Döpp
F.Irshad
E.Travac
N.Weiße
S.Karsch
D.Campbell
A.Schletter

## Slide 2
Outline
Our Lab at CALA
Breit-Wheeler Experiment
Development of Gas Targets for LWFA
Measurement Results with different targets and injection methods
Summary/Outlook

## Slide 3
Electron and Thomson Test Facility (ETTF) at CALA
30fs, up to 3PW laser pulses from ATLAS3000, used for now with 300TW
f = 10m spherical mirror, F/56
gas jets / cells as targets
I = 8.9 x 1018 W/cm-3
a0 = 2.0

## Slide 4
Breit-Wheeler Experiment
T G Blackburn, M Marklund 2018 Plasma Phys. Control. Fusion 60 054009

## Slide 5
Breit-Wheeler Experiment
Electron Beam goal:
2.5 GeV
monoenergetic
high charge
low divergence
low pointing jitter
stable, reproducible
F C Salgado et al 2021 New J. Phys. 23 105002
S Schindler et al 2019 Proc. of SPIE 11037N-1

## Slide 6
Development of Gas Targets for LWFA

## Slide 7
Gas Nozzle Design – CFD Simulations of Convergent-Divergent Slit Nozzles
Simulation Software: Ansys Fluent
Width: 3 mm
Length: 20 mm
x
Width: 3 mm
Length: 20 mm
z

## Slide 8
Gas Nozzle Design – CFD Simulations of Convergent-Divergent Slit Nozzles
Old Design: Width: 0.75 mm
New Design: Width: 3 mm
Density gradient in y-direction is less steep for new nozzle
 wakefield and injected electrons are less strongly bend upwards

## Slide 9
Variable Length Gas Cell
Gas inlet
Optical shock inducing laser beam
LWFA driving laser beam

## Slide 10
Hydrodynamic Optical Field Ionized (HOFI) Shocks
0 ns
2 ns
-50 µm +50 µm
density
Background
density
Image courtesy to F.M.Foerster; Plasma simulation support from Oxford (A.Ross et al.)

## Slide 11
LWFA Measurements

## Slide 12
Gas Cell – Optically induced Shock Injection
~1 GeV; mean charge in peak ~ 24 pC
6m focal length optic

## Slide 13
Gas Cell – Self Injection
Gas density: 9.1 x 1017 cm-3
Energy reaching over 2 GeV
Mean Charge: ~10 pC over 2 GeV ( ~38 pC over 1.5 GeV)
RMS divergence: 0.3 mrad
Notes: Between 200-400pC charge in total (~650pC for one shot)

## Slide 14
Gas Cell – Length scan (Self Injection)
Gas density: 9.3 x 1017 cm-3

## Slide 16
Slit Nozzle in Laser Wakefield Acceleration Setup
Blade to produce shock
Optical shock inducing laser beam
LWFA driving laser beam
Gas flow

## Slide 17
Slit Nozzle – Shock Injection
Obstacle induced
Optically induced
~1 GeV; FWHM ~80 MeV; RMS divergence 0.5 mrad, ~100 pC in peak
Gas density: 9.4 x 1017 cm-3
Gas density: 1.0 x 1018 cm-3
~0.6 GeV; FWHM ~40 MeV; RMS divergence 0.7 mrad, ~93 pC in peak

## Slide 18
Slit Nozzle – Shock Injection
Optically induced
Obstacle induced
F.M.Foerster et al. (arXiv:2206.00507)
1 mm
onset of ionization trace
6 mm
onset of ionization trace
1.8 mm

## Slide 19
Variable Length Gas Cell
Gas inlet
Optical shock inducing laser beam
LWFA driving laser beam

## Slide 20
Slit Nozzle – Self Injection
Energy reaching over 1.5 GeV
Mean Charge: ~8 pC over 1.5 GeV ( ~32 pC over 1 GeV)

## Slide 21
Summary and Outlook
Energies of over 2 GeV reached (close to goal of 2.5 GeV)
High quality beams produced with optical shock injection in slit nozzles
Need to combine high quality with higher energy
Planned for next year: Gas Cell with injection hole further downstream, ramp-up laser energy, finish Breit-Wheeler Setup

## Slide 22
Thank you!