## Slide 1: Multi-Color Operation via Coherent Harmonic Generation in a Plasma Driven Attosecond X-Ray Source
Rafi Hessami on behalf of the PAX Collaboration
Advanced Accelerator Concepts Workshop 2022
November 7, 2022

## Slide 2: Motivation
Attosecond science can probe electron dynamics.
Facilities producing high-power (specifically TW-scale) attosecond X-ray pulses are currently nonexistent.
High-power attosecond X-ray pulses would be interesting to many fields!
Tunable isolated attosecond X-ray pulses with gigawatt peak power from a free electron laser,
J.Duris, et al., Nature Photonics 14, 30-36 (2020)
Notes: Talk about attosecond sources as a concept, intro that world, describe the plot, were like XFELs but short and attosecond

## Slide 3: PAX as a TW X-Ray Source
PAX plans to compress a PWFA beam with a large chirp to 10s of nm, producing radiation at that scale.
Terawatt attosecond x-ray source driven by a plasma accelerator,
C.Emma, et al., APL Photonics 6, 076107 (2021)

## Slide 4: Limitations
This is fantastic for light greater than 10 nm, but many attosecond science experiments want to see above the Carbon K edge at 283 eV.
Biomolecular Crystallography: Principles, Practice, and Application to Structural Biology,
B. Rupp, Garland Science, 1st edition (2009)

## Slide 5: Our Proposal
We propose to extend the beamline with undulators tuned to 1 nm.
Use the 10th harmonic bunching to jumpstart the FEL process at 1 nm in the beam.
Step 1: Pre-bunched at ~100 nm
Step 2: Pre-bunched at 10 nm
Step 2: Pre-bunched at 2 nm
Compress in chicane
10 nm undulator
2 nm undulator
TW as pulse at 2nm!
Notes: Paul Corkum said 30 attoseconds is the fastest process time
Advantages over FEL: shorter pulse time, shorter beamline because no SASE (CHECK WHAT TYPICAL FEL PULSE TIME IS)

## Slide 6: Wigner Plots Along the Beamline
1st Harmonic
5th Harmonic
1.12 m
1.12 m

## Slide 7: Wigner Plots Along the Beamline
1st Harmonic
5th Harmonic
10th Harmonic
1.12 m
1.12 m
1.12 m

## Slide 8: Bunching (Two Stage)
1st Harmonic:
5th Harmonic:
Red arrow indicates where 1st harmonic undulator ends, 5th harmonic undulator starts

## Slide 9: Pulse Length
Two Color:
Three Color:
Very short pulses!

## Slide 10: Space Charge
Simulations for this talk were done in PUFFIN, which does NOT include space charge.
This is a major limitation of this simulation.
, pondermotive force dominates

## Slide 11: Conclusions and Future Work
Future Work:
Add space charge to PUFFIN
Conclusions:
PAX can be upgraded to a TW-scale source of 2 nm radiation with very short pulse length

## Slide 12: Thanks!
Other talks related to this topic:
Status and Prospects for the Plasma-drived Attosecond X-ray (PAX) source experiment at FACET-II – Claudio Emma
  3:30 pm, 8/11
Plasma-based Attosecond X-ray Pulses – Agostino Marinelli
  9:30 am, 11/11, Ballroom Salon D-E
Radiation detection for the PAX Experiment at FACET-II (Poster) – Rafi Hessami
  5 pm, poster session
Thank you all for listening!

## Slide 13: Backup Slides

## Slide 14: Bunching (3 Stage)
10th Harmonic:

## Slide 15: Total Power After Each Undulator