## Slide 1: Stabilization & manipulation of laser-driven plasma acceleration with a weak auxiliary laser pulse
B. Bowers, R. Rudzinsky, M. LaBerge, M.C. Downer
The University of Texas at Austin
*
* PhD 2022
*LWFA driver: ≤ 4 J, ~30 fs, 0.8 µm, lin-pol;
self-truncated ionization injection (STII) regime1
*auxiliary pulse: < 0.5 J, co-propagates with variable ∆t,
strong shot-to-shot phase fluctuations.
T. Wang, G. Shvets
Cornell University
T. Püschel, J.P. Couperus-Cabadağ, Y.Y. Chang, A. Irman,
P. Ufer, M. Smĭd, R. Gebhardt, S. Bock, U. Schramm
Helmholtz-Zentrum Dresden-Rossendorf
1 Mirzaie et al., Sci. Rpts. 5, 1-9 (2015)
1
Notes: Shot-to-shot fluctuation in performance remain a major inhibitor of many potential applications of laser wakefield accelerators. In this work, we show, first of all, that a small fraction of the energy of an LWFA drive pulse can be responsible for such fluctuations, and, secondly, that an equally small fraction in the form of an auxiliary laser pulse much weaker than the drive pulse can manipulate LWFA performance in signficant ways. These experiments were carried out at HZDR by my former PhD student Brant Bowers
Change as you see fit. This is the author list on the paper. The order is arbitrary except for the first and last ones on each attribution. Once we include Thomas’s work, it would make more sense for him to be first on the HZDR line as the paper will then be a split between his work, Tianhong’s, and mine with only a slight weight towards mine.

## Slide 2
Phase jitter at drive pulse edges
compromises LWFA stability
2
Full LWFA Drive Beam (unoptimized)
Couperus et al., Nat. Commun. 20, 487 (2017)
Full LWFA Drive Beam (optimized)
Notes: This illustrates that the phase jitter causes the same issue even with no global delay, reinforcing that the effect may be due to envelope variation more than DLA variations

## Slide 3
Phase jitter at drive pulse edges
compromises LWFA stability
3
Full Drive Beam
Masked Drive Beam
• e-beam energy
& pointing
• X-ray yield
& spectrum
• charge
near field transverse
drive beam profile
mask blocks
outer edge
(10 -15%
of energy)
immediate, robust
improvement in
stability of:
Mask evidently
removes shot-
to-shot phase
fluctuations
from portions
of beam that
experienced
unsaturated gain.
Notes: This illustrates that the phase jitter causes the same issue even with no global delay, reinforcing that the effect may be due to envelope variation more than DLA variations

## Slide 4
To explore phase-controlled LWFA manipulation, we
re-shaped removed light into a delayed auxiliary pulse...
Focusing LWFA drive
pulse from OAP
segmented
turning
mirror
FAR FIELD
NEAR FIELD
LWFA drive pulse
auxiliary wake
manipulation pulse
*J. L. Shaw et al., Phys. Rev. Lett. 118, 064801 (2017)
J. L. Shaw et al., Plasma Phys. Control.Fusion 60, 044012 (2018)
• Auxiliary pulse delay ∆t0 controlled
independently of LWFA drive pulse,
a distinction from prior work.*
4
Notes: Because of its strong phase fluctuations, this is of course exactly the wrong auxiliary pulse that one would want to use for real LWFA control. One would want to use a CEP-stabilized pulse. But here we use the built-in phase fluctuations as a means to scan phase parameter space, in order to discover the ∆t ranges in which such control can be most effective.

## Slide 5
Simulations predict several 2-pulse effects
5
Shaw et. al.
• Pulse envelope evolves strongly as trailing pulse
overtakes and interferes with drive pulse.
• Overlap of laser with e- causes Direct Laser Acceleration (DLA), which
can increase e- energy, transverse momentum & betatron X-ray yield...
Zhang, Shvets et al., Plasm. Phys. and Contr. Fusion 10, 60 (2018)
Electron Energy
Transverse Momentum
Betatron X-ray Spectrum
LWDA*
LWFA
*LWDA = Laser Wakefield &
Direct-Laser Acceleration
Notes: Key here is that the second pulse can be made to overlap more or less with the accelerating electrons in order to change the direct laser interaction. Incidentally the following pulse will experience a different index of refraction from the leading pulse, causing a change in the evolution of the collective intensity.

## Slide 6
Simulations predict several 2-pulse effects
...but is sensitive to small phase differences
between drive and auxiliary pulses
Standard Peak
DLA Peak
Direct Laser
Deceleration
Direct Laser
Acceleration
6

## Slide 7
Experimental Setup
7
insertion mask 1
e-spectro-
(h)
(i)
(ii)
insertion mask
2, wedge
betatron
X-ray
diagnostics:
(i) photon-counting
X-ray CCD
(ii) HOPG spectro-
meter
gas
jet*
f/25 OAP
meter
segmented
turning
mirror
Pulse diagnostics
e-energy spectrum
delay
control
DRACO
drive
laser
4 J, 27 fs
*He + 1% N2, 3 mm,
ne ≈ 3 × 1018 cm-3
250 MeV
spectral interferometry
Notes: This is just a diagram of the experimental setup:
a is a pulse mask for determining the delay between any two points on the wavefront (not during experiment)
b is a pickoff mirror for the spectral interferometer line (one line bounces off inner mirror, other off outer mirror, and a flat ~3ps delay is added by a delay stage at f, flat mirror available to compare interference
c is the mirror itself, the outside is fixed and the inside slides on rails. The mirrors are balanced to create nearly zero torque on the system
d is the pulse masks and wedge, the masks allow us to isolate either the inner or outer pulse for focal diagnostics or to drive the LWFA (outer pulse fails at this as it has too low power)
e is the electron spectrometer dipole
f is the spectral interferometer line with the delay and a camera behind a beamsplitter to detect overlap between the two pulses
g is the INSIGHT/thru focus spectral interferometer for characterization of the full, unsplit pulse
h is the betatron profiler, showing the flux and opening angle of the x-rays
i is the single-pixel counting x-ray camera (at the end of a long line) for the x-ray spectrum
j is an alternate x-ray spectrometer using a HOP-G crystal

## Slide 8
Experimental results: correlated peak at ∆t ≈ 25 fs in several DLA indicators
8
Mean electron
energy
<Energy> (MeV)
Qe >100 MeV (pC)
Electron
charge
ne = 3 × 1018 cm-3
Normalized
Betatron
X-ray flux
time delay ∆t0 (fs)
0
50
100
-50
-100
Fx (10-20 keV) (arb. u.)
Notes: This illustrates that the ideal time delay (~20-30fs) creates fluctuation in energy, charge, and x-ray flux and that these fluctuations are coherent with each other. In other words, if a more stable phase difference could be achieved, the results on the right could be achieved consistently

## Slide 9
9
1-pulse
Electron spectra
2-pulse
(∆t = 25 fs)
0
200
400
0
200
400
Divergence (mrad)
Electron energy (MeV)
X-ray brightness
0
20
-20
Horizontal (mrad)
Vertical (mrad)
0
40
20
Brightness (arb. u.)
X-ray brightness
0
20
-20
Horizontal (mrad)
Vertical (mrad)
0
40
20
Brightness (arb. u.)
5
10
15
20
25
X-ray photon energy (keV)
100
102
104
106
Photon counts
X-ray spectra
2-pulse
1-pulse
Charge density
(pC/MeV)
0
1
2
Q/E/𝜃 (pC/MeV/mrad)
0
1
“Hook ‘em Horns”
DLA structures*
* Shaw et al. (2017, 2018)
Notes: This is meant to illustrate the change in peak electron energy, fluctuation, x-ray flux, x-ray energy

## Slide 10
Optimum ∆t changes with
plasma density ne
10
Peak at ∆t ≈ 45 fs for ne = 1.9 × 1018 cm-3 (top)
Peak at ∆t ≈ 25 fs for ne = 3.9 × 1018 cm-3 (bottom)
∆t = 0 accurate to ~10fs
∆t scales approximately as bubble size
Notes: This illustrates that the ideal time delay varies with the bubble size (the square root of gas density) and therefore the distance from lead pulse to injected electrons. The correlation is not 1:1 as indicated by the ratio of the peaks being less than root(2). This implies that the peak is linked to DLA effects from second pulse overlap but is also affected by a separate effect that is less dependent on gas density (for example the envelope intensity modulation).

## Slide 11
Summary
• Uncontrolled phase fluctuations in the periphery of LWFA drive
pulses contribute significantly to shot-to-shot LWFA instability.
• A weak, strategically-timed, independently-controlled auxiliary pulse
derived from this periphery substantially increases...
...electron energy
...e-beam divergence
...betatron X-ray brightness & photon energy
...charge
on average, but with large fluctuations.
• CEP-stabilized auxiliary pulses should avoid these fluctuations,
providing a low-cost, fine-tune control knob for LWFAs.
Work supported by DoE grant DE-SC0011617, Helmholtz Association (Matter & Technology
program, Accelerator R&D topic), Alexander von Humboldt Foundation.
11