## Slide 1: A Compact Source of Positron Beams with Small Thermal Emittance
Rafi Hessami, Stanford University
Spencer Gessner, SLAC
Advanced Accelerator Concepts Workshop 2022
November 7, 2022

## Slide 2: Motivation
  Positron plasma wakefield acceleration has only been studied at SLAC (FFTB, FACET, FACET-II).
  Significant infrastructure is required to produce intense, highly-compressed positron beams.
Are there alternative sources of positron beams that may be suitable for PWFA experiments?
Notes: “Positrons are 50% of a collider but 5% of research” – SAY IF YOU CAN FIND WHO SAID IT

## Slide 3: Current Positron Sources
  FACET-I used an rf gun-electron beam on a target and a damping ring.
  Expensive
  Large
  7.3 emittance
  5 Hz
  1 nC
Positron Beamlines and Dynamics,
G. White, FACET-II Science Workshop (2019)
Notes: All emittances mentioned are normalized

## Slide 4: GBAR’s Method of Making Positrons
  The GBAR experiment uses an MeV linac operating at pair production threshold.
    About 108 e+/s
  The ILC uses electron or photon beam on target.
    About 1014 e+/s
Neon moderator
This is not a replacement for traditional positron beam production from targets.
The GBAR antimatter gravity experiment,
P. Perez et al., Hyperfine Interactions 233, 21-27 (2015)
Notes: Highlight it’s good for R&D

## Slide 5: Penning-Malmberg Trap
The Penning-Malmberg trap consists of an axial magnetic field and two endcap potentials and can contain a non-neutral plasma.
We “spin” the plasma by having the electric field on the electrodes rotate
Particles drift back and forth between the endcaps, with transverse space charge countered by the inward-pointing Lorentz force produced by the rotation.
https://journals.aps.org/rmp/abstract/10.1103/RevModPhys.87.247
Single-Particle Trajectory
“Rotating Wall”
Notes: TRY TO UNDERSTAND ROTATING WALL ON THE PLANE

## Slide 6: Our Proposal
s-band cavity
Buncher/
accelerator
Electrostatic extraction/compression
Electrostatic acceleration

## Slide 7: Thermal Emittance
Using equations of state and the following definition of emittance:
We find:
for N positrons, B solenoid field, and Lp trap length.
Equations of State

## Slide 8: Thermal Emittance
For our study:
  Bz = 1 T
  T = 273 K
  𝜔r = 5.75 MHz
  𝛺c = 176 GHz
  rp = 1 mm
  Lp = 5 cm
  Ne+ = 1E8
This yields 𝜀n = 110 n!
Notes: Mention that far right side of upper plot is same charge as FACET-I
Can’t go higher than ~10^10 because the space charge is just too much, pushes particles out of the trap (CHECK THAT THAT’S THE MAX)

## Slide 9: Angular Emittance
The thermal emittance is not the whole story!
The positrons are damped (born) in a strong magnetic field.
The beam is magnetized.
Angular momentum emittance:
  ℒ = 300
Notes: High angular emittance makes this good for studying round to flat transforms, actually an opportunity since colliders like that to suppress beamstrahlung (READ PAPER FROM RIVER FIRST)

## Slide 10: GPT Simulation
To see if the trap is useful in a beamline, we simulated it in GPT
We see bunch length decrease to ~10s of mm before the S-band cavity at D
Positron trap from 0 to A
Electrostatic accelerator from B to C
S-band cavity from D to E

## Slide 11: Final Bunch Parameters
In our simulation, we were able to compress and accelerate the positron beam with low emittance!

## Slide 12: Future Work
Lots of work on optimization needs to be done
  Emittance growth at cavity start
  Charge loss at cavity start
Better ways to compress/accelerate a large/slow beam?

## Slide 13: Thanks!
GBAR: Dirk Peter Van Der Werf, Samuel Niang, Laszlo Liszkay
The AWAKE electron source team: Seongyeol Kim, Mohsen Dayyani Kelisani, Steffen Doebert.
Helpful discussions with Allen Mills, UC Riverside, and David Cassidy, University College London.
Thank you all for listening!

## Slide 14: Backup Slides

## Slide 15: GPT Simulation
To see if the trap is useful in a beamline, we simulated it in GPT
We see bunch length decrease to ~10s of mm before the S-band cavity at D
Positron trap from 0 to A
Electrostatic accelerator from B to C
S-band cavity from D to E

## Slide 16: Charge Loss
When entering the S-band cavity, significant charge loss is observed
This charge loss is due to the beam being so long (5 cm flat top) and slow (AFTER the electrostatic accelerator) when reaching the cavity.

## Slide 17: Final Bunch Parameters
In our simulation, we are able to compress and accelerate the positron bunch with low emittance!
But we also observe significant charge loss

## Slide 18: Assorted Properties of the GPT Simulation

## Slide 19: Beamline CAD Idea