## Slide 1: High Efficiency RF Source Development
Lawrence Ives, Calabazas Creek Research, San Mateo, CA. USA
.
100 kW, 1.3 GHz Magnetron w/ Phase and amplitude control
Magnetron frequency/phase control with varactors
100 kW, High efficiency, L-Band klystron
350 – 700 MHz, 200 kW Power Grid Tube RF sources
700 MHz Multiple Beam IOT

## Slide 2: A 100 kW, 1.3 GHz Amplitude and Phase Controlled Magnetron for Accelerators
Michael Read1, R. Lawrence Ives1, Brian Chase2, John Reid2, Chris Walker3 and Jeff Conant3
[1] Calabazas Creek Research Inc., San Mateo, CA 94404
[2] Fermi National Accelerator Laboratory Batavia IL 60510-5011
[3] Communications and Power Industries LLC, Beverly, MA, USA 01915
Funded by the US Department of Energy under SBIR grant DE-SC0011229

## Slide 3: Fermilab Approach
Externally phase lock the magnetron,
Achieve amplitude control by phase modulating the locking signal to transfer power to side bands
  Side bands are rejected by high Q accelerator cavity
  Power into the cavity = Magnetron power less the side band power

## Slide 4: CPI Magnetron
1.30 GHz
100 kW peak
10 kW average
1.5 ms pulsewidth

## Slide 5: Packaged Magnetron System

## Slide 6: Efficiency
Efficiency varied between 81% and 87%, depending on parameters

## Slide 7: Phase Modulation
122° Modulation
60° Modulation
No Modulation
50 kHz Phase Modulation
2 MHz
2 MHz
1 MHz
9.6
-10.4
-70.4
0.0
-30.4
-40.4
-50.4
-60.4
-80.4
-20.4

## Slide 8: Magnetron Amplitude vs Phase Modulation
Chart: Modulation (Degrees)
| 0 | 5.7295645530939652 | 11.45912910618793 | 17.188693659281896 | 22.918258212375861 | 28.647822765469826 | 34.377387318563791 | 40.106951871657749 | 45.836516424751721 | 51.566080977845687 | 57.295645530939652 | 63.025210084033624 | 68.754774637127582 | 74.484339190221547 | 80.213903743315498 | 85.943468296409478 | 91.673032849503443 | 97.402597402597408 | 103.13216195569137 | 108.86172650878534 | 114.5912910618793 | 120.32085561497327 | 126.05042016806725 | 131.77998472116118
Theory | 0 | -0.021728 | -0.087077 | -0.19654 | -0.35097 | -0.55159 | -0.80006 | -1.0985 | -1.4496 | -1.8569 | -2.3245 | -2.8579 | -3.4638 | -4.151 | -4.9306 | -5.8175 | -6.8321 | -8.0027 | -9.3708 | -11.0006 | -12.9993 | -15.5661 | -19.1436 | -25.1079
Experiment | 0 | -2.25 | -21.73
Theory:

## Slide 9: Cost for 100 kW System
(Exclusive of high voltage supply)
Magnetron | $40,000
500 W SS amplifier | $17,000
Circulator w waveguide | $20,000
Controls | $10,000
Packaging | $10,000
Total | $97,000
Magnetron System Cost ~ $1/Watt
(Klystron cost ~ $4/Watt)

## Slide 10: A 1.3 GHz 100 kW Ultra-high Efficiency Klystron
[1] Calabazas Creek Research Inc., 490 Port Drive San Mateo, CA 94404
[2] Leidos, Center for EM Manager DEOST, Billerica, MA 01821
Communications & Power Industries, LLC, Palo Alto, CA 95304
Funded by the US Department of Energy under SBIR grant DE-SC0017789.
Michael Read1, Aaron Jensen2, R. Lawrence Ives1, Thomas Haberman1, David Marsden1, and George Collins1
Poster: 2.09 Wednesday 5:00 PM

## Slide 11: Core Oscillation Method (COM)*
Cavity spacing set wider than the normal bunch oscillation length
Antibunch particles monotonically approach the central bunch
Circuits are long
* A. Yu.Bajkov, D.M.Petrov “Problems of creation powerful and super- power klystrons with efficiency up to 90%”, International University Conference “Electronics and Radio physics of Ultra-high Frequencies”, St. Petersburg, May 24–28, 1999, pp. 5–8.

## Slide 12: Design Parameters
COM design with 7 cavities
Parameters
  Voltage 53.5 kV
  Current 2.46 A (0.2 micropervs)
  Beam diam 0.6 cm
  Drift tube diam 1.0 cm
  RF structure length 205 cm

## Slide 13: Simulation Summary
Chart: Input Power (W)
| 0 | 3.9301951843628079E-2 | 7.8603903687256158E-2 | 0.1965097592181404 | 0.3930195184362808 | 0.982548796090702 | 1.965097592181404 | 3.930195184362808
MAGIC2D (Avg. Beam Radius ~ 3.2 mm) | 0 | 36.4 | 61.3 | 91.25 | 98.1 | 101.98 | 103.3 | 105
Tesla (Avg. Beam Radius ~ 3.2 mm) | 0 | 72.5 | 92.4 | 98.7 | 101.4 | 103 | 106
AJDISK 1D (3.2 mm Beam Radius) | 0 | 73.14 | 98.097 | 104.33 | 105.16 | 103.8 | 106.27
KlyC | 103.5 | 103.5

## Slide 14: Cavity Locations and B-Field Profile
2.2 m
P = 104.5 kW
η = 79.5%

## Slide 15: Beam Trajectories Near Output
Phase with most interception
Phase with least interception
~ 200 W/cm2 over ~ 5 mm

## Slide 16: Solid Models of Klystron
279 cm

## Slide 17: Partial Seal-in

## Slide 18: High Efficiency Klystron Summary
Seven Cavity COM design
Simulation of ‘as built’ klystron predicts 78.2% efficiency
Final seal in next two weeks
Testing to start January 2023

## Slide 19: Multiple Beam Power Grid Tubes for High Frequency and High-Power Operation
Lawrence Ives, Michael Read, David Marsden, Thuc Bui Calabazas Creek Research, San Mateo, CA. USA
Ricky Ho, Nileshwar Chaudar, Christopher McVey, Tom Cox Communications & Power Industries, LLC Palo Alto, CA 94304 USA
James M. Potter JP Accelerator Works Los Alamos, NM USA
This research funded by DOE SBIR Grant DE-SC0018838
.

## Slide 20: 25 kW 425 MHz Triode-based RF Source
YU-176 Triode
Efficiency 90% (Class C)

## Slide 21: YU-176 Grid Cathode Assembly
Features
Oxide cathode - $916 factory cost
Grid - cut from commercial tungsten screen - brazed to tungsten supports
Integral ceramics and vacuum seals
Beam power – 28 kW
Total cost - $1,500

## Slide 22: Beam Power for 200 kW RF Source
Eight YU-176 grid cathode assemblies
230 kW of beam power

## Slide 23: 350 MHz Cavities
MB triode tube installs from top (blue)
Single input cavity below tube
Upper and lower output cavities with coax output between
Upper cavity is frequency tuning element
Lower cavity is variable output coupling element

## Slide 24: Output Cavity Simulation
Tuning range for output cavity (325 – 500 MHz)

## Slide 25: Gain Issue
Gain ~14 dB for triode based sources
200kW RF source requires 6.5 kW driver
Driver: Single-beam triode driver - Same length as multi-beam source with smaller diameter

## Slide 26: 200 kW, 350 MHz RF System
Net Gain 28 dB
Net Efficiency ~80?%

## Slide 27: 200 kW CW RF Source Cost 350 – 700 MHz
Estimated cost: $100K for 200 kW source and driver
Triode-based system $0.50/Watt ~72%
Klystron: ($4/W) 50-65% MBIOT: ($2-$4/W) 65-75% Solid State: ($4/W) ~60%

## Slide 28: MB Triode Assembly Status and Scheduled
MB Triode assembly completed and testing in progress (grid to cathode resistance, peak emission, current division, cutoff voltage)
Once tube is successfully verified, will assemble the multiple beam cavities for testing in early 2023

## Slide 29
HIGH-EFFICENCY, HIGH AVERAGE POWER INDUCTIVE OUTPUT TUBES
Work supported by the US Department of Energy Grant No. DE-SC0019800
H.P. Freund,1 R.L. Ives,1 M. Read, T. Bui1, T. Habermann1, David Marsden1, Paul Krzeminski2, Takuji Kamura2
1Calabazas Creek Research, San Mateo, CA
2Communications & Power Industries, LLC, Palo Alto, CA

## Slide 30: Goals and Approach
Goals:
Output power 200 kW CW
Frequency 700 MHz
Number of beams eight
Efficiency 80+%
Reduce size and cost
Approach
Include 3rd harmonic drive power to increase efficiency
Implement compact input coupler to reduce size and cost
Use molybdenum grids to reduce cost and risk

## Slide 31
3rd HARMONIC TEST CASE
Simulated annular beam at 700 MHz with:
  37 kV/6.67 A
  Annular Beam with inner/outer radii = 5.128 cm/8.079 cm
  Iavg/Ip = 0.15  twidth/tpulse = 0.3
  R/Q = 100 W
  Q = 84.6 (loaded)
  Cavity Radius = 9.009 cm
  Cavity Length = 9.144 cm
  Gap Length = 3.1 cm (centered in the Cavity)
  Solenoid Field = 126 G (Brillouin Field)
Simulation results indicate:
  Optimal performance when the phase of the 3rd harmonic relative to the fundamental is p
  Efficiency is enhanced from 84.4% to 86.3%

## Slide 32
NEMISIS MBIOT SIMULATON
Perveance » 1.3 mP
Peak efficiency with the 3rd harmonic
  Peaks for phase shift of p radians
  Peak efficiency » 94%
  Expect to reach wallplug efficiency above 80%
Eight beam configuration circulating the cavity at the midpoint
  f =700 MHz
  30 kV/6.67 A
  R/Q = 186 W, Q = 120
  Lcavity = 9.144 cm, Lgap = 3.9 cm (centered)

## Slide 33
METAL GRID DESIGN
Current IOTs use pyrolytic graphite (PG) grids
Difficult to fabricate
Expensive
Relatively low yield
MBIOT beam power distributed over multiple beams
Reduced power loading
Thermomechanical analysis predicts good performance
Significantly cheaper and higher yield
Beam Optics Analyzer thermomechanical analysis with beam interception and cathode radiation

## Slide 34: Temperatures
Emitter
Grid
Moly grids considerably cooler than PG grids

## Slide 35: Thermal Stress & Axial Displacement
Highest stress is on the grid rim, but still below Moly tensile strength
At temperature, grid OD moves closer to the emitter 1.9 mils, ID closer 3.3 mils
Compensation required for increased thermal expansion

## Slide 36: Input Coupler
Input Coupler for CPI/Thales and L3 MBIOTS large and complex
CCR input coupler design much simpler
Input coupler for CCR MBIOT
Input coupler for CPI/Thales MBIOT

## Slide 37: Input Coupler
Challenge – develop coupler transmitting fundamental and 3rd harmonic
Incorporated structures/tuners specific to each frequency
2100 MHz
700 MHz

## Slide 38: Input Cavity Tuning
Note – Input cavity is at atmospheric pressure
Top
Side
Annular

## Slide 39: MBIOT Design
Coaxial output window
Single collector for all beams
Simple output cavity

## Slide 40: 200 kW, 700 MHz MBIOT
Computational design complete
Drawings and parts procurement in progress
Tests scheduled for spring 2023

## Slide 41: MBIOT Status and Summary
Investigating three improvements
Adding 3rd harmonic drive to improve efficiency - is efficiency gain achieved - does improvement justify the cost
Replacing PG grids with molybdenum grids
Simplifying the input coupler
Status
Most drawings completed
Long lead time parts are on order
Expect to start assembly in January 2023
Testing scheduled for spring 2023

## Slide 42: Summary
RF Sources and Key Features
Magnetron System 100 kW 1.3 GHz Amp/Phase Control 80+% efficiency $1/Watt Completed
High Efficiency Klystron 100 kW CW 1.3 GHz 78% Freq/Pwr Scalable Test in January 2023
Triode-base RF sources 200 kW CW 350–700 MHz $0.5/Watt compact MB Triode in test
Multiple Beam IOT 700 MHz 200 CW kW 80% Drawings and fabrication in progress Test in spring 2023

## Slide 43: New RF Source Development
RF Sources and Key Features
Magnetron System 100 kW 1.3 GHz Amp/Phase Control 80+% efficiency $1/Watt Completed
High Efficiency Klystron 100 kW CW 1.3 GHz 78% Freq/Pwr Scalable Test in January 2023
Triode-base RF sources 200 kW CW 350–700 MHz $0.5/Watt compact MB Triode in test
Multiple Beam IOT 700 MHz 200 CW kW 80% Drawings and fabrication in progress Test in spring 2023