## Slide 1: Short Pulse High Gradient Accelerating Structures
Sergey V. Kuzikov
Euclid TechLabs, LLC, Bolingbrook, IL
Outline:
Short pulse high-gradient acceleration concept:
  Breakdown threshold
  Efficiency
  Lifetime
Experiments with nanosecond X-band components;
THz single-cycle structures;
Mm- and cm- single-cycle structures:
a) GV/m wakefield structures
b) multi-mode wakefield structures.

## Slide 2
Euclid Techlabs/Euclid Beamlabs
Euclid Techlabs, LLC is a research and development company specializing in linear particle accelerators, ultrafast electron microscopy, and advanced material technologies. The company was formed in 2003. Euclid Beamlabs LLC, formed in the winter of 2014, is a sister (spin-off) company of Euclid Techlabs LLC, particularly to commercialize industrial accelerator and related advanced material technologies developed at Euclid Techlabs. Euclid has developed expertise and products in several innovative technologies: time-resolved ultra-fast electron microscopy; ultra-compact linear accelerators; electron guns with thermionic, field emission or photo-emission cathodes; fast tuners for SRF cavities; advanced dielectric materials; HPHT and CVD diamond growth and applications; thin-film for accelerator technologies; Present: 27 people research staff (researchers, engineers, technicians) and 5 administrative. 16 PhDs in accelerator physics and material science, 32 staff. 2 labs: Bolingbrook, IL (accelerator R&D lab) and Beltsville, MD (material science lab). Long term collaborations with National Labs and Institutes: ANL, Fermilab, BNL, Jlab, LBL, SLAC, LANL, NIST, NIU, IIT, etc.
www.euclidtechlabs.com
Fermilab
Euclid
Argonne
Euclid
UMD
NRL, JLab
NIST
BNL

## Slide 3
Products & Capabilities Snapshot
Products
UltraFast Pulser (UFPTM) for TEM
Dislocation free diamond for Xray optics
Compact X-Ray Source
NCRF and SRF electron sources
Low loss ceramics (linear and non-linear)
LINAC
RF window
In flange BPM
Capabilities
Femtosecond Laser Ablation System
Thin Film Deposition Lab
EM Testing Lab
Radiation Shielding/Testing Lab

## Slide 4
Feeding by short, high repetition rate pulses, in order to avoid breakdown and excessive pulse heating according to scaling laws:
Accelerating fields more than 100 MV/m have already been obtained at ~100 ns pulses in X-band. Extrapolating scaling law one must conclude that in order to reach 1 GV/m, as short as ~ 1 ps (1 THz width) pulses are needed.
Challenges:
Broad band systems are necessary;
High repetition rate;
High efficiency;
Structure lifetime must be large enough.
Pulse Length Scaling & Challenges

## Slide 5
High-Gradient X-Band Gun Fed by 9 ns RF Pulses
11.7 GHz field structure
RF

## Slide 6
High-Gradient Test and Beam Energy Characterization
~3% fluctuation
1000 shots as total
Energy measured by the spectrometer dipole
~3% fluctuation, likely due to the drive charge instability.
Max achieved gradient is 388 MV/m from the beam energy measurement
Simulated kinetic-energy isoclines as function of RF gun operating conditions K(E0, φ0) and retrieved operating points (“+” symbols). The shaded areas represent the uncertainty on the measured φ0 and inferred E0 values.
Emittance was measured by quad scan:
  (due to geometry asymmetry)
  Kinetic energy: 5.9 MeV
BDR~10-6 , 100 pC
Low average dark current

## Slide 7
1. A. D. Cahill et al. High gradient experiments with X-band cryogenic copper accelerating cavities, 2018.
A Short Pulse Gun at Cryogenic Temperatures
Breakdown rate vs gradient [1].
For the 11.7 GHz 9 ns gun the cathode gradient at 45 K could be as high as more than 500 MV/m, maximum surface electric field might be as high as 750 MV/m.
2. V.A. Dolgashev, Recent High Gradient Tests at SLAC, 2016.
Peak pulse heating is a reasonably good predictor of the breakdown probability [2].
Comparison of the transient cathode gradient when driven by long (blue) and short (red) pulse. The input power is f300 MW and the rising/falling is fixed at 3 ns.

## Slide 8
A Nanosecond Accelerating Structure with Individually Fed Cells
5-cell side coupled accelerating structure: E-field structure of the operating mode at 11.7 GHz (a), several structures assembly (b), S11 for the feeding antenna (c).
splitter
Bent delay waveguides
5 independent cells
Power | 150 MW
RF pulse length | 10 ns
Q-factor | 350
Accelerator type | -mode
Bending angle | 69.2
Beam channel | 10 mm
Shunt impedance | 44 M/m
Surface Emax | 750 MV/m
Surface Bmax | 0.8 MA/m
Parameters of the 11.7 GHz, 300 MV/m, 5-cell structure (T=300 K).
The TM010 accelerating cells are powered individually!
This principle allows:
- to mitigate the influence of RF breakdown if appears in one cell;
- to increase the shunt impedance due to the smaller than usual beam channel;
- to reduce sensitivity to the tolerances on the size of the cells.
a)
b)
c)

## Slide 9
Because the luminosity is required to be high, the repetition rate for a short-pulse structure must be increased by factor of pulse length reduction. It could be as high as sub-MHz level.
Estimations for Structure Lifetime
long-pulse structure
short-pulse
structure
0

=0/N
N
1
2
3
N
for N short pulses, i.e.
…
.
Let us take BDRN=BDR and assume that in case of breakdown event all RF power stored in a cell can be deposited in material erosion:
To “kill” the structure completely one need evaporating as much material as:
.
Eventually, the full number of macro- pulses to destroy the structure:
micro-pulses
macro-pulse
for a long-pulse structure.

## Slide 10
Frequency | 10 GHz | 10 GHz
Waveguide type | WR90 | WR90
RF pulse duration | 1 ns | 0.5 ns
RF pulse period | 10 ns | 5 ns
Peak RF power | 170 MW | 140 MW
Power gain | 47 | 55
Bunch charge | 1 nC | 3.5 nC
Efficiency | 0.7% | 6%
High-Efficiency Short Pulse Acceleration
Steady state traveling RF pulse (blue) and the feeding RF pulse (red).
Resonator with equidistant mode spectrum.
TE10
time
Eacc
Field in accelerating gap
500 MV/m accelerating structure
Delay waveguide
Fourier spectrum of pulses and eigen mode spectrum of resonator
Power gain (blue) and field enhancement in accelerating gap (red)

## Slide 11
Beam
channel
E
E
TEM travelling wave delay lines
Coaxial Travelling Wave Structure
Frequency dispersion is almost absent!
Power gain (~20) depends on losses in delay waveguides,
It can be increased using special coating or working at cryogenic temperatures.
E-field

## Slide 12
High-Power Short-Pulse RF Sources
G. G. Denisov, S. V. Kuzikov, A. V. Savilov. Q-switching in the electron backward-wave oscillator, Physics of plasmas 18, 103102 (2011).
S.V. Kuzikov, A.V. Savilov, Parametric Phase Locking in an Electron RF Oscillator, Phys. Rev. Lett. 110, 174801 (2013).
BWO with Q-switching:
- Stationary pulse-periodic generation of short rf pulses.
- RF pulses are phase locked by Q-modulation shape.
Q-switched BWO : Efficiency = 60-70%
peak rf power = 350 %

## Slide 13
VBS test stand with installed test resonator: a – overall view, b – test resonator in vacuum chamber installed in the bottom, c – view through quartz window to YAG-screen.
VBS beam modulation (5 Hz)
Electron beam
Beam on
(50% of time)
Beam off
(50% of time)
RF Modulation by Electron Beam and AC Bias Voltage
Diamond
Bias (3 kV) modulation frequency is 100 Hz.
(I=1-7 A)
Avalanche effect

## Slide 14
Emitted Terahertz spectrum
*C. Vicario et al. Optics Letters, Vol. 39, Iss. 23, 2014.
High-fields have been produced by optical rectification in a large-size organic crystal by a powerful pump lasing. The phase-locked single-cycle pulses carry peak fields of more than 80 MV/cm at diffraction limited spot size. The scheme has 3% conversion efficiency.
Generation of mJ Single THz Pulses with Electric Field Exceeding 80 MV/cm*

## Slide 15
E-field distributions at the lens while focusing the short THz pulse, for the time correspondent to THz pulse arrives to lens (a), for time when focusing begins (b), for time when focusing is close to maximum (c), and in maximum of focusing (d).
Multi-Cell Accelerating Structures Driven by Focused THz Pulses
Timing of THz pulses in the structure.

## Slide 16
High current drive beam
Witness beam
Single Cycle Wakefield Accelerating Structure

## Slide 17
A Wakefield Single-Cycle Accelerating Structure
Excitation of a single-cycle wake in a gap with a parabolic shape. Time flows evenly as a-b-c-d.
a)
b)
c)
d)
Single-cycle acceleration cell.
Shape of the single-cycle wake (a) and spectrum of this wake (b) at the output of the parabolic mirror with a length of 9.6 mm and an aperture of 150 mm generated by a 50-nC, 5-mm-long (Gaussian) single bunch.
a)
b)

## Slide 18
Field excitation by a single bunch in parabolic mirrors, and evolution of this field in the delay line waveguides. The bunch travels from left to right.
Summation of pulses in the combiner and focusing of the resulted single-cycle pulse by the parabolic mirror. Time flows evenly from left to right.
Field shapes for the pulse entering the pulse combiner (green curve), for the pulse at the entrance of the focusing parabola (pink curve), and at the focus of the final parabolic mirror for 50 nC.
Parameters of the accelerating structures.
Parameters |  |  | 
Bunch charge, nC | 50 | 150 | 250
Number of bunches | 5 | 2 | 1
Number of cells | 11 | 20 | 11
Accelerating field, MV/m | 170 | 470 | 570

## Slide 19
A Multi-Mode Wakefield Accelerating Structure
Field patterns at the time points shown in Fig. 5: a – point A, b – point B, c – point C, d – point D.
E-field mode structures in a slice of the square resonator: a – TM1,1,0 , b – TM3,3,0, c - TM5,5,0, d- TM7,7,0, e – TM9,9,0.
E-field in the middle of the resonator with mode spectrum correction excited by 100 bunches.
Enlarged portion of the previous figure.
S.V. Kuzikov et al, Phys. Rev. Lett. 104, 214801 (2010). S.V. Kuzikov et al. Phys. Rev. Lett. ST Accel. Beams, Vol. 13, No.7, 071303 (2010).

## Slide 20
Conclusion
Short-pulse structures show prospects to achieve ~GV/m gradients. Its can have high efficiencies that are comparable with efficiencies of classical structures.
Breakdown threshold (theoretical and experimental) study for ultra short RF pulses is needed. The temperature dependence is also extremely interesting.
High repetition rate, short pulse RF sources are necessary. So far experiments with wakefield class structures are only available.
The synergistic effect of short pulse technology and cryogenic technology would allow reaching world record gradients as well as high efficiency due to a higher wall conductance.