## Slide 1
11/11/2022
Design Optimization of Permanent-Magnet Based Compact Transport Systems for Laser-Driven Proton Beams
J. T. De Chant*, K. Nakamura, Q. Ji, L. Obst-Huebl, S. Steinke, S. Barber, A. M. Snijders,
T. Schenkel, J. van Tilborg, C. G. R. Geddes, C. B. Schroeder, and E. Esarey
The work was supported by Laboratory Directed Research and Development (LDRD) funding from LBNL provided by the Director, and the U.S. Department of Energy Office of Science, Offices of Fusion Energy Sciences and High Energy Physics under Contract No. DE-AC02-05CH11231.Work was also supported by the US Department of Energy, Office of Science, High Energy Physics under Cooperative Agreement award number DE-SC0018362.
AAC 2022
*

## Slide 2: Compact proton beam transport system is needed for application experiments at the new BELLA PW iP2 experimental area
Wall
2.5 m
Short focal length OAP
Difficult to transport due to:
Broadband energy spectra
Large divergence up to ~25°

## Slide 3: Permanent magnet quadrupoles (PMQs) are compact, high field gradient focusing elements with a large bore
Strong focusing gradient (100s T/m) with a large bore (6-30 mm) needed for collection efficiency
Compact transversely and longitudinally and no large cryostat required (like in stronger SC magnets)
Not easily tunable due to fixed gradient
We have performed a design study to explore different transport systems for iP2 proton beams
PMQ parameters | 
Inner radius | 10 mm
Outer radius | 30 mm
Bulk magnetization (NdFeB) | 1.29 T
Field Gradient | 110 T/m
Modeled in Radia

## Slide 4: Beam transport systems were designed using COSY Infinity while performance was evaluated with particle tracking
Radia
To provide base design of permanent magnet
COSY Infinity
Matrix-based charged particle transport calculation code
Particle Tracking
Homemade MATLAB script for particle tracking to evaluate performance
Permanent magnet quadrupole doublet
(30 MeV 24 MeV 36 MeV)
x
z
y
z

## Slide 5: More complex configurations were explored to improve beam quality and tunability at sample site
x
z
y
z
Quartet
This work allows us to respond to need from users more effectively
Quartet Chicane Quartet
Improves symmetry of beam spot
Energy selection
Reduced aberrations
x
z

## Slide 6: A 10 MeV collimating transport system will be implemented for radiation biology experiments
Wall
2.5 m
Short focal length OAP
Ion Energy
Uniform dose dist.
Charge distribution at sample site
x
Dipole
ions
PMQ
PMQ

## Slide 7
Summary
Compact proton transport beamline is needed for application experiments at the new BELLA PW iP2
Beam transport systems were designed using COSY Infinity
Performance was evaluated with particle tracking
More complex configurations were explored to improve beam quality and tunability
A 10 MeV collimating transport system will be implemented for radiation biology experiments
The work was supported by Laboratory Directed Research and Development (LDRD) funding from LBNL provided by the Director, and the U.S. Department of Energy Office of Science, Offices of Fusion Energy Sciences and High Energy Physics under Contract No. DE-AC02-05CH11231.Work was also supported by the US Department of Energy, Office of Science, High Energy Physics under Cooperative Agreement award number DE-SC0018362.

## Slide 8: Various configurations were explored to determine which is best for applications; each require different desired beam properties
x
z
y
z
 | η (%) | npk (109/mm2) | δE (MeV) | σx (mm) | σy (mm)
Doublet | 2.2 | 18 | 0.75 | 0.84 | 0.03
Triplet | 2.5 | 25 | 0.85 | 0.13 | 0.17
Quartet | 1.3 | 6.6 | 1.2 | 0.34 | 0.35
Doublet
Quartet
Triplet
This work allows us to respond to need from users more effectively
Energy tunability

## Slide 9: High order transfer maps are required due to large momentum spread of the LD beam
The motion of a particle in an arrangement of EM fields can be described by a map relating its final positions to its initial position and some other parameters , such as the energy spread
Each element in the matrix represents the contribution of one variable to another i.e.
The matrix can be Taylor expanded with respect to the trajectory of a reference particle
High order map (3rd order and above) is required for LDA due to the extreme energy spread

## Slide 10: Main result of previous RadBio campaign: first demonstration of healthy tissue sparing under laser-proton irradiation
J. H. Bin, L. Obst-Huebl, et al., Sci. Rep. 12, 1484 (2022)
Low differential sparing of healthy cells versus tumor cells when irradiated with X-rays (0.02 Gy/s)
normal
tumor
normal
tumor
High differential sparing of healthy cells versus tumor cells when irradiated with laser-driven protons
(~107 Gy/s)
Laser-driven protons
Reference X-rays

## Slide 11: Magnetic Vortex Acceleration may yield a better beam with less transport difficulties
Initial simulation work done by Hakimi et al. at BELLA shows improvement in the in divergence by using an alternative acceleration scheme

## Slide 12: Recently, the first small animal tumor irradiations were conducted for the first time with laser-accelerated protons
Kroll F, Brack F, Bernert C, et al. Tumor irradiation in mice with a laser-accelerated proton beam. Nat Phys. 2022;18(March):13-16. doi:10.1038/s41567-022-01520-3

## Slide 13: Future design to collimate 30 MeV ion beams
*dipoles not shown

## Slide 14: PMQ Housing and ablation shield

## Slide 15: Laser Driven (LD) ion beams have desirable properties for applications but are difficult to transport effectively
Applications
Warm dense matter experiments
(e.g. isochoric heating)
Radiobiological studies
(e.g. FLASH proton therapy)
nm - μm
1013 ions/shot
~ps pulse duration
S. C. Wilks et al. Phys. Plasmas 10.1063/1.1333697, Macchi et al. Rev. Mod. Phys. 10.1103/RevModPhys.85.751
Use high intensity lasers (>1021 W/cm2) to accelerate ions
Produce large amount of ions per shot (1013 ions/shot) with ultra-short pulse duration (~ps) at source
High intensity laser
>1021 W/cm2
Difficult to transport due to:
Continuous broadband energy spectra up to a cutoff energy (expected >50 MeV for iP2)
Large initial divergence (up to ~25°) at the source
25°
B. Mahieu et al. Nat Comm. 2018
J. Bin et al., Sci Rep 12, 1484 (2022)