## Slide 1: Fulfilling the mission of Brookhaven ATF as a Doe Flagship user facility in Accelerator Stewardship
AAC 2022
Igor Pogorelsky (ATF)
co-authors: M. Babzien, M. Fedurin, W. Li, M. N. Polyanskiy and M. A. Palmer (ATF)
N. Vafai-Najafabadi (Stony Brook University)
The Accelerator Test Facility

## Slide 2: ATF: Designated a DOE National User Facility in 2015 It is a flagship facility in Accelerator Stewardship
Accelerator R&D Stewardship Mission:
  Support fundamental accelerator science and technology R&D
  Disseminate accelerator knowledge and training
Program Implementation:
  Facilitate access to national laboratory accelerator facilities and infrastructure for industrial and U.S. government agency users/developers of accelerators and related technology
  Support basic R&D necessary for sustained innovation across a broad range of accelerator applications

## Slide 3: ATF Research Capabilities

## Slide 4
  Novel electron acceleration techniques R&D for smaller, more cost-effective accelerators
    Laser and beam driven plasma and dielectric wakefield acceleration
    Direct laser acceleration
    Inverse free-electron lasers…
  Ion generation and acceleration
    Supersonic hydrogen gas jets provide capabilities for generating mono-energetic multi-MeV proton beams
  High-brightness radiation sources New techniques to produce electromagnetic radiation from THz to X-rays:
    FEL R&D
    Inverse Compton scattering
    THz radiation from dielectric structures…
  Electron beam instrumentation and manipulation Sophisticated longitudinal and transverse beam manipulation capabilities
    Wide range of beam parameters enabling development and testing of advanced accelerator hardware, beam diagnostics and detectors
  Ultrafast Electron Diffraction/Microscopy Technique for characterizing materials that is complementary to x-ray sources
    Experimental station for diffraction and imaging studies with MeV-class electron beams
Scope of ATF research

## Slide 5
Major Facility Upgrade Thrusts
guided by the ATF Science Planning process
Laser R&D program
  CO2 laser power upgrade to ≥25 TW peak power with pulse-width <500 fs
  First femtosecond multi-TW LWIR laser!
  This would enable a world-leading research program into advanced particle acceleration
  Completing in vacuum NIR and LWIR laser beam transport to user experiments
  to ensure the best beam quality
Electron Beam
  Continue to move towards providing 10 fs compressed bunches
  Exploit and expand short bunch diagnostic capabilities
UED/UEM
  Focus on unique UED measurement options for users
    Wavelength flexible OPA pump laser
    Improved system performance
  Apply AI/ML techniques to both beam line tuning and real-time structural analysis
5
UED principle
ATF experimental hall with two electron beamlines
In-vacuum laser transports to experiments

## Slide 6
Outline
Motivation for multi-TW ultra-fast LWIR
State of art in picosecond CO2 laser technology
Path to femtoseconds via nonlinear post-compression
Simulations
Experimental results
Outlook

## Slide 7
LWFA
Ion Acceleration
ne/n0
ne = 1016cm-3
ne = 2x1019cm-3
λdrive= 0.8 µm 25 TW, 30 fs
λdrive= 10 µm 25 TW, 500fs
simulations courtesy G. Shvets
Motivation for multi-TW ultra-fast LWIR
CO2
10TW, 0.5 ps
TiS
A proposed two-color LWFA with ionization injection opens opportunity for ultra-low beam emittance .
εn=50 nm
TNSA
CSWA
and
1 MeV protons with 1 TW CO2 laser focused
to 1016 W/cm2 thanks to
Collisionless Shock Wave Acceleration
need CO2 because

## Slide 8
State of art in LWIR laser technology
BNL LWIR
Laser System
CO2
CO2
Compressor
Stretcher
OPA seed pulse generator
High-pressure, isotopic
gas amplifiers
5 TW
2 ps
Advanced features
Solid-state laser based front-end
High-pressure, mixed-isotope CO2 amplifiers
Chirped-pulse amplification in gas laser
Leading-edge parameters
Shortest multi-TW LWIR pulse
Clean, single-pulse output

## Slide 9: 5 TW, 2 ps LWIR laser
Polyanskiy et al. OSA Continuum 3, 459 (2020)
Notes: Accelerators & ultrafast lasers
How lasers
Unique features
Techniques
Overview of history
Plans

## Slide 10
,
Can we do better than 2 picoseconds?
Strong, broadband seed pulse
Gain spectrum allows to amplify 500 fs pulses.
However, bandwidth narrowing over >12 decades of amplification brings the pulse to 2 ps.
Providing a several mJ seed pulse for the final amplifier allows productive use of two rotational bands bringing the output pulse to 500 fs.
Such broadband seed pulse can be produced by OPCPA or by Raman conversion of a near-IR-pulse followed by a difference frequency generation illustrated below.
See talk of William Li on ATF R&D towards generating such seed pulses.
Possible routes to
ultra-fast CO2 lasers:
Nonlinear post-compression (NLPC)
500 fs
20 Tw
5 Tw
Current:
Seed <1 mJ
Regen 1012
Final 103
Prospect:
Seed 5-10 mJ
Final 103

## Slide 11
,
Can we do better than 2 picoseconds?
Strong, broadband seed pulse
Possible routes to
ultra-fast CO2 lasers:
Nonlinear post-compression (NLPC)
  Self-phase modulation due to Kerr effect in a nonlinear material results in a quasi-linear frequency chirp.
  A chirped pulse gets compressed in a material with a negative group dispersion.
n(t) = n0 + n2I(t)
Self-phase modulation
Dispersive compression
=
compressible linear chirp

## Slide 12
Simulations for our initial experiment
Transparent to CO2 laser NaCl material provides and GVD.
Our simulations done for 10 cm NaCl in approximation of a flat beam profile .
Quasi-gaussian beam from the ATF CO2 laser system is close to this.
Down to 80 fs pulse compression predicted.

## Slide 13
0.4 J/cm2
0.6 J/cm2
0.3 J/cm2
Autocorrelation traces versus laser fluence
Results from initial NLPC test with a single bulk (10 cm thick) NaCl crystal

## Slide 14
More simulations
Compressed pulses and their autocorrelation functions
Autocorrelation function considerably enhances the pedestal
Time, ps
best compression
under-compression
over-compression
Two observations:
Compression highly critical to laser intensity

## Slide 15
Path to improvement
B>>1 is needed to see an appreciable pulse compression.
However micro-filamentation and color center formation may hinder the process at B>3.
We can suppress micro-filamentation by segmenting the nonlinear material.
Opportunities for improving efficiency of energy conversion to femtoseconds :
  using flat-top beams,
  NLPC staging,
  beam size manipulation between NLPC stages,
  and possible combination of different NLPC materials.

## Slide 16: Two-stage NLPC by separating chirping and compression
Material properties at 9.2 mm
 | n0 | n2 (m2/W) | (fs2/mm)
NaCl | 1.500 | 3.5 × 10−20 | -1010
KCl | 1.459 | 3.4 × 10−20 | -558
BaF2 | 1.412 | 1.7 × 10−20 | -2340
 | n0 | n2 (m2/W) | 
NaCl | 1.500 | 3.5 × 10−20 | -1010
KCl | 1.459 | 3.4 × 10−20 | -558
BaF2 | 1.412 | 1.7 × 10−20 | -2340
100 mm
13 mm
compressed from 2 ps to 290 fs
13 mm
5 mm
Laser output
at the NLPC
well-controlled Gaussian distribution 14 m after the aperture
5cm
5cm

## Slide 17
Funding:
US DOE Accelerator Stewardship Program grant, B&R #KA2601020
BNL Laboratory Directed Research and Development grant #20-010
Full-energy design
Autocorrelation
τpulse = 290 fs
Polyanskiy, et al. Opt. Express 29, 31714 (2021)
Low-energy demo
LWIR laser R&D towards 10+ TW, <1 ps

## Slide 18: Full Scale Experiment
Two chambers for inserting NLPC optical elements within LWIR beam transport line.
Preliminary results obtained.
2ps
Autocorrelation traces
Spatial filtering requires putting the experimental setup in vacuum.

## Slide 19: Our goal: Entire 10J beam compression to <500fs, >10TW (supported by simulations)
Assumptions:
an ideal super-Gaussian (8th order) beam
beam size (1/e^2 radius = 27.5mm)
input energy 10J (~4.5TW)
KCl+BaF2 (50 mm thick each)
B-integrals of both components are ~3
350 fs
input beam
after KCl
after BaF2

## Slide 20
,
Path to Petawatt pulses of 2 optical cycles
Strong, broadband seed pulse
Nonlinear post-compression (NLPC)
1) Combining two compression techniques
CO2
SPA Compressor
Stretcher
High-pressure, isotopic
amplifier
NLPC
NIR fs laser
LWIR converter
200 mJ
300 fs
200 mJ
100 ps
10 mJ
100 ps
14 J
100 ps
10 J
500 fs
20 TW
5 J
50 fs
100TW
Simulations of post-compression


## Slide 21
,
Path to Petawatt pulses of 2 optical cycles
2) Bigger laser amplifier might allow to reach PW !
70 J
8-meter CO2 laser amplifier at BNL for future upgrades

## Slide 22
Ongoing LWIR Beam Transport Upgrade
Future upgrade to BL2
Ion
Acceleration
LWFA
Linac Experimental Hall
with two beamlines
LWIR Laser Room
CPA Compressor
Polarization Rotator
ICS

## Slide 23
Alternate location for NIR compressor
NIR Vacuum Transport
NIR vacuum transport runs along the floor in the laser rooms
NIR vacuum transport runs along the ceiling in the ebeam experimental hall
LWIR Components removed for clarity
NIR compressor

## Slide 24: Summary of laser upgrades
CO2 Vacuum transport will deliver high quality TW beam to experiments for stronger particle acceleration.
A platform is provided to test the next stages of pulse compression (i.e. non-linear pulse compression) in the LWIR.
Polarization rotator will provide adjustable polarity from horizontal to vertical, and circular.
LWIR vacuum transport to BL2 planned.
NIR vacuum transport & compressor will improve beam stability and optics lifetime.

## Slide 26: UED with recently installed microscope
UEM
LDRD funded project: Demonstration of feasibility of sub-nm, picosecond electron microscope for the life sciences
Objective is to obtain tissue sample images with minimal sample degradation due to high speed, short duration pulse

## Slide 27
Thank you!