## Slide 1: Establishing a Relativistic Ultrafast Electron Diffraction & Imaging Facility in the UK
Julian McKenzie (on behalf of the RUEDI team)
Physics and Applications of High Brightness Beams
21st June 2023 San Sebastian, Spain

## Slide 2: Contents
Introduction to RUEDI
  Science Themes
Project formation
Timescales
Key aspects of RUEDI:
  Imaging / Electron Microscopy
  Ultrafast diffraction beamline
  Temporal diagnostics
  Laser pumps
  Overall concept overview
Summary

## Slide 3: The RUEDI Facility Proposal
Proposal for a new UK National User Facility
Relativistic Ultrafast Electron Diffraction & Imaging (RUEDI)
MeV UED and UEM
Time-resolved pump-probe experiments in both real and reciprocal space
With a large variety of pumps and sample environments
To enable a large range of science
Pumps:
  Wide variety of laser wavelengths, THz, TW, keV ion source
Environments:
  Solid, liquid cells, liquid/gas jets, plasmas, cryogenic (down to mK level)

## Slide 4: The RUEDI National Project
The Materials Innovation Factory
Harwell Campus Hub
Cockcroft Institute
Daresbury Laboratory
Lead institute (University of Liverpool – Prof. Nigel Browning)
And main partners: (RFI – Prof. Angus Kirkland)
Other science theme leads:
UK Infrastructure Fund:

## Slide 5
Leveraging STFC Daresbury Expertise
Design, build, and operation of particle accelerator facilities
Femtosecond photoinjector development
MeV ED experience
Proof-of principle static MeV electron diffraction on VELA
5
Site host in existing building
Measurement of dynamics of relativistic electrons with laser-driven THz sources, and high power TW lasers

## Slide 6: Timeline
TODAY
2018
2025
2026
2027
2028
2029
2030
2031
2019
2020
2021
2022
2024
2023
Initial funding
TDR
Final design
Capital funding
Construction
Funding decision!
Assume 5-year operation cycles after commissioning
With capital for upgrades on same timescales
Initial bid
Bid
CDR
Science case
Commissioning
Infrastructure Fund Bid
Ops
Users

## Slide 7: Enabling Science
Town hall meetings held throughout 2022
Identified experiments and requests electron parameters, pump sources and sample environments
Dynamics of Chemical Change
  Chemical complexity across scales
  Hydrogen bonding
  Pulse radiolysis
  Heterogenous catalysis
  Ultrafast low-energy optical switching
  Magnetic textures & skyrmions
  Topological superconductors
  Thermoelectric energy harvesting
Quantum Materials & Processes
  Astrophysics & warm dense matter
  Advanced manufacturing
  Nuclear fission/fusion/space
  Response to shocks
Materials in Extremes
Biosciences
  Photosynthesis & energy transfer
  Cardiac disease related dynamics
  Virology & infection
  Biological self-assembly/toxicity
Mostly Imaging
Mostly Diffraction
Energy Generation, Conversion & Storage
  Photocatalysis & induced electro-chemistry
  Defect kinetics in solar cells
  Ion solvation kinetics in batteries
  Kinetics of glasses
Notes: Dynamics of Chemical Change
  Chemical complexity across scales
  Hydrogen bonding
  Pulse radiolysis
  Heterogenous catalysis
Materials in Extremes
  Astrophysics & warm dense matter
  Advanced manufacturing
  Nuclear fission/fusion/space
  Response to shocks
Quantum Materials & Processes
  Ultrafast low-energy optical switching
  Magnetic textures & skyrmions
  Topological superconductors
  Thermoelectric energy harvesting
Energy Generation, Conversion & Storage
  Photocatalysis & induced electro-chemistry
  Defect kinetics in solar cells
  Ion solvation kinetics in batteries
  Kinetics of glasses
Biosciences
  Photosynthesis & energy transfer
  Cardiac disease related dynamics
  Virology & infection
  Biological self-assembly/toxicity
(Artificial Intelligence/Data Science)
(example experiments, which university leading)

## Slide 8: Facility concept
Microscopy/
Imaging line
Ultrafast diffraction line
S-band photoinjector 4 MeV
10s of nm rad emittance
Current concept is one gun feeding two separately shielded beamlines
ps scale
200fC - 20pC
Stroboscopic + Single-shot
10-100s fs scale
Up to 400 fC
Stroboscopic + Single-shot

## Slide 9: Best spatial resolution
Microscopy/
Imaging line
Ultrafast diffraction line
S-band photoinjector
ps scale
200fC - 20pC
Stroboscopic + Single-shot

## Slide 10: Imaging Beamline
Objective lens
The key to the whole system
Samples inserted into middle
Multiple pump laser entry ports
Compatible with commercial TEM sample stages (enabling experiments in solid, liquid, cryogenic, heating etc)
Imaging lens system
Series of magnetic lenses
Aiming for 6500x magnification
Comparing round lenses (solenoids)
vs quadrupole quintuplets
Round lens limited to 2 MeV beam energy at 1.7 T peak field
Quadrupoles have worse aberrations
Detector
16-64 MegaPixel
direct electron
~6.5um pixel size
e-beam
e-beam
pump laser entry
pump laser entry
Sample stage loading
Dechirper cavity to reduce energy spread (see next slide)
pump laser entry
DETECTOR
Electrons from source
Objective lens
coils
yoke

## Slide 11: Microscopy Resolution
Blue – pre-dechirper
Yellow – post-dechirper
Resolution limit simplified…
RF dechirper cavity
  Also used to decelerate from 4 to 2 MeV
For 1nm resolution, need <10-4 relative energy spread
11
Also need ~10s nm rad level emittance to be able to focus beam down to ~10µm samples
Stroboscopic mode (10^6 electrons) has potential to reach down to 1nm resolution
Single-shot mode (10^8 electrons (20pC)) has resolution limited to 50 – 100 nm range, and hard to focus beam onto small samples
Cs = Spherical aberration (~10mm @ 2MeV)
𝛼 = objective aperture collection semi-angle
Cc = Chromatic aberration (~10mm @ 2MeV)
𝛿𝛾/𝛾 = relative beam energy spread
Poster yesterday

## Slide 12
Microscopy/
Imaging line
S-band photoinjector
Ultrafast diffraction line
Best temporal resolution
10-100s fs scale
Up to 400 fC
Stroboscopic + Single-shot

## Slide 13: Ultrafast diffraction beamline
Simultaneously achieve:*
  Jitter suppression
  Bunch compression
Four dipole arc to separate beamline, completely tuneable to both signs of R56
Jitter suppression
Bunch compression
Aim to provide ultrashort bunches with small time of arrival jitter
Poster yesterday
*H.W. Kim et al, "Towards jitter-free ultrafast electron diffraction
technology", Nature Photonics, Vol. 14, Pages 245–249,
2020.

## Slide 14: Ultrafast Diffraction Beamline
  Cryogenic (down to mK)
  Gas/liquid jets
  Best sample control and diagnostics
14
Bunch length monitoring via RF Transverse Deflecting Cavity + THz
RF Beam Arrival Monitor
Option for detector with hole to allow shot by shot measurements on non-diffracted beam
Lenses post-sample to magnify image (and for streaking diagnostics)
Pump lasers
THz
diagnostic
RF TDC
THz
diagnostic
Electrons from source
Interchangeable sample chambers
Solenoidal lens
Quadrupole
Large variety of pump laser wavelengths/energies/durations
Final focus lenses

## Slide 15: Concept Electron Beamline Layout
Microscopy/
Imaging line
Ultrafast diffraction line
S-band photoinjector 4 MeV
10s nm rad emittance
ps scale
200fC - 20pC
Stroboscopic + Single-shot
10-100s fs scale
Up to 400 fC
Stroboscopic + Single-shot

## Slide 16: High Brightness Beams Challenges
Ultra-low emittance (nm-rad level)
Ultrashort pulses (fs-scale)
Low temporal + spatial jitter (fs-scale)
Low energy beams:
  Non-relativistic ballistic/velocity effects
  Space-charge dominated beam transport
Diagnostics of:
  Low charge bunches (fC level)
  Small transverse bunches (um-scale)
  Ultrashort bunches (fs-scale)
Minimise dark current (high signal-to-noise ratio)

## Slide 17: Laser Systems
Standard frequency conversions:
  200nm - 5um
  OPAs + harmonic generation
Unique features:
  Ultrashort 10fs
  THz
  TW
  HHG
Laser room
Ultrafast diffraction
Microscopy
R&D/Prep room
All fed by same oscillator for synchronisation
Gun

## Slide 18: Facility Conceptual Design
Laser rooms
Photoinjector and microscopy beamline
Ultrafast diffraction beamline
Control room
To be located in the Daresbury Laboratory Electron Hall.

## Slide 19: Summary
RUEDI is a proposed UK National User Facility
For time-resolved pump-probe experiments
Ultrafast Electron Diffraction & Imaging
To probe both real and reciprocal space
Large variety of sample environments
Wide range of laser pumps, including 10fs, THz, TW, HHG
Currently halfway through design stage
Capital funding decision expected end of this year

## Slide 20: Acknowledgements
Nigel Browning
Angus Kirkland
Yoshie Murooka
Jan Nugara
Will Bryan
Simon Maskell
B. Layla Mehdi
Sven Schroeder
Carsten Welsch
Oznur Apsimon
Gwyndaf Evans
Dwayne Miller
Ian Robinson
Jasper Van Thor
Lee Kelsall
Alberto Acuto
Maulik Patel
and more…
Alex Bainbridge
James Bebbington
Rachael Buckley
Jim Clarke
Louise Cowie
Graham Cox
Joe Crone
Mike Ellis
Aaron Farricker
Omair Ghafur
Anthony Gilfellon
Clive Hill
Phil Hornickel
Ben Hounsell
Frank Jackson
James Jones
Nirav Joshi
Daniel Lake
Storm Mathisen
Russell McLean
Boris Militsyn
Bruno Muratori
Tim Noakes
Tom Pacey
Suzanna Percival
Lewis Reid
Mark Roper
Yuri Saveliev
Ben Shepherd
Rob Smith
Calum Tollervey
Andrew Vick
Alan Wheelhouse
Fatih Yaman
and more…
Daresbury Laboratory