## Slide 1: Physics-Informed Machine Learning for Particle Accelerators
Christopher M. Pierce

## Slide 2: Surrogate Models – Fast, Differentiable, Data-Driven
SURROGATE MODEL
A blackbox model mapping system inputs to outputs. Often used when the exact workings of the system are difficult to know or expensive to calculate.
Gupta, L., Edelen, A., Neveu, N., Mishra, A., Mayes, C., & Kim, Y. K. (2021). Machine Learning: Science and Technology, 2(4), 045025.

## Slide 3: Surrogate Models – Fast, Differentiable, Data-Driven
SPEED
GRADIENT INFO
DATA-DRIVEN
Physics-based simulations are expensive
Efficiently query precalculated results over wide range of parameters
speedup
Many existing codes are incompatible with auto-diff
Surrogate models inherently make gradient calculations easy (IE neural nets)
Training surrogates may be less costly than re-engineering existing tools
Physics-based simulation tools have difficulty incorporating real-world data
Surrogates treat data from machine and simulation on “same level”
Naturally combine types of data to produce better model
Optimization Sped up x
Edelen, A., Neveu, N., Frey, M., Huber, Y., Mayes, C., & Adelmann, A. (2020). PRAB, 23(4), 044601.
Phase Space Reconstruction by Differentiable Modeling
Roussel, R., Edelen, A., Mayes, C., Ratner, D., Gonzalez-Aguilera, J. P., Kim, S., ... & Power, J. (2022)..
Incorporating Data from SLAC into Model of Longitudinal Phase Space
Emma, C., Edelen, A., Hogan, M. J., O’Shea, B., White, G., & Yakimenko, V. (2018). PRAB, 21(11),.

## Slide 4: Surrogate Models – Fast, Differentiable, Data-Driven
THE PROBLEM
The (relative) difficulty of acquiring data for accelerator physics problems makes building surrogate models hard. Simulation tools are expensive and data collection at real machines is even more expensive.
PHYSICS PRIORS - A SOLUTION?
We already know the governing equations of charged particles in a beamline. Instead of making models re-learn this info from first principles, can we impose it as a constraint? Can make cheaper models?
Karniadakis, G. E., Kevrekidis, I. G., Lu, L., Perdikaris, P., Wang, S., & Yang, L. (2021). Nature Reviews Physics, 3(6), 422-440.

## Slide 5: Physics Informed Neural Networks Primer
https://benmoseley.blog/my-research/so-what-is-a-physics-informed-neural-network/
PHYSICS INFORMED NEURAL NETWORK (PINN)
Neural networks are a “universal approximator” and can represent solutions of ODEs and PDEs. Train the neural network with a loss that represents the ODE or PDE residual at a set of “collocation points.”
Opportunity to Reduce Data Requirements for Accelerator Surrogates
Without Priors
With Priors

## Slide 6: Ongoing and Future Work
INVERSE PROB.: PHASE SPACE MEASUREMENT
Given images of a charged particle beam for different accelerator settings, reconstruct the initial phase space. Important for measurements of real world system. PINN-based methods could be the first general method of reconstructing beams w/ intense space charge forces. Demonstrated in non-accelerator system.
Phase Space
Screen Image
PINN w/ Knowledge of Solenoid Lens
Screen Images
Initial Beam Dist.
Karniadakis, G. E., Kevrekidis, I. G., Lu, L., Perdikaris, P., Wang, S., & Yang, L. (2021). Nature Reviews Physics, 3(6), 422-440.

## Slide 7: PINNs for Accelerator Physics
WHICH PDE TO USE AS A PRIOR IN ACCELERATOR PHYSICS?

## Slide 8: PINNs for Accelerator Physics
VLASOV EQUATION
Consider the multi-particle phase space distribution function f(r, p, s) with s the independent variable. Only considering long range force, it obeys the Vlasov equation. It is a generalization of Liouville’s Theorem. Space charge is calculated in self-consistent manner.
J. Math. Phys. 57, 042905 (2016)
G.A. Krafft Old Dominion University Slides

## Slide 9: Progress on PINN Surrogate Modeling
A FIRST TEST OF PHYSICS-INFORMED PRIORS
Physics priors should improve sample efficiency and generalization of surrogate models. Put that to test with a direct comparison of two systems:
Conventional neural network of the kind already used in accelerator physics
Physics-informed network with strong priors
Conventional Surrogate Model
“Knobs”
(, , , …)
Measurable Quantities
MODEL A
“Conventional” Surrogate Model
MODEL B
PINN
Phase Space Density
Measurable Quantities
“Knobs”
(, , , …)
Phase-Space Coordinate
(, , , )
Time-Like Coordinate
( or )
Physics-Informed Surrogate Model
Will the benefits of a PINN outweigh the complexity of modeling the beam instead of the observables?
“Knobs” are: magnet/cavity settings, laser parameters, etc

## Slide 10: Progress on PINN Surrogate Modeling
A TOY ACCELERATOR SYSTEM
Sonnendrücker, E., Filbet, F., Friedman, A., Oudet, E., & Vay, J. L. (2004 Computer Physics Communications, 164(1-3), 390-395.
Beam with Space Charge, Uniform Focusing Channel
Which accelerator system to choose? I claim that beam transport in a uniform focusing channel is an ideal test system:
Few dimensions (2D) makes training the PINN much less costly
Doesn’t have longitudinal coordinate, which we expect to pose some challenges for PINN (distribution not centered at z=0, Pz=0)
Trivial beamline elements makes for simple implementation
Space charge should lead to complex behavior

## Slide 11: Progress on PINN Surrogate Modeling
EMITTANCE GROWTH IN FOCUSING CHANNEL
For purposes of study, calculate emittance growth as beam parameters are varied. Done using a PIC code.
Twiss Beta: Gaussian beam’s aspect ratio at s=0m
Perveance (K): Unitless measure of charge density normalized to beam energy.

## Slide 12: Progress on PINN Surrogate Modeling
FIRST STEPS AT FOCUSING CHANNEL PINN
The PDE describing the beam in phase space is the Vlasov Eqn.
This is coupled with the Poisson Eqn. to give the space charge forces Er (K is perveance)
Ignore space charge for now. Using this as the loss term in the PINN with as a boundary condition, a NN can be trained to represent the function .
Neural network represents density at every point along focusing channel

## Slide 13: Progress on PINN Surrogate Modeling
INCLUSION OF SPACE CHARGE FORCES
Self-consistent space charge forces can be “trained” at same time as the PINN for beam density by introducing second NN that represents .
Optimize parameters for both networks at the same time using the coupled loss function.
Results in the expected tune depression and nonlinear focusing forces.

## Slide 14: Progress on PINN Surrogate Modeling

## Slide 15: Progress on PINN Surrogate Modeling
Particle Tracking
PINN (no data): 0.007 mm-mrad MAE!
NN (n=32): 0.015 mm-mrad MSE
2x better accuracy than baseline model w/ few datapoints!

## Slide 16: Ongoing and Future Work
SURROGATE MODELING W/ LONGITUDINAL COORDINATE AND REAL-WORLD DATA
Next in complexity is surrogate modeling of axisymmetric bunched beams. This includes modeling longitudinal phase space which comes with some challenges related to picking colocation points.
USPAS Lecture Notes, Lecture 5 Beam Dynamics with Space Charge, William Barletta (2010)
INDUCTIVE BIASES FOR ACCELERATOR MODELS
Neural network models of particle distributions should:
Fall off quickly away from origin with some length scale related to beam’s second order statistics.
Move by shearing and rotations
Longitudinal phase space tracks a “reference particle” who’s motion is easily calculated
Hamiltonian motion exists in phase space w/ Symplectic geometry and associated symmetries

## Slide 17: Acknowledgments
This work was supported by the U.S. National Science Foundation under Award PHY-1549132, the Center for Bright Beams. Additional support for computing resources comes from the UChicago Research Computing Center Midway3 Cluster.
UNIVERISTY OF CHICAGO
ACCELERATOR PHYSICS GROUP
SLAC ACCELERATOR MACHINE LEARNING GROUP
FUNDING SOURCES
Young-Kee Kim
Juan Pablo Gonzalez Aguilera
Auralee Edelen
Ryan Roussel

## Slide 18: PINNs for Accelerator Physics
BACKUP SLIDES

## Slide 19: Uniform Focusing Channel Extras
UNIFORM FOCUSING CHANNEL BASICS
The envelope of the particle beam oscillates with wavevector that depends on focusing strength and beam longitudinal momentum.
If beam density is constant along phase space trajectories, the density will not change. The beam is “matched” to the channel.
Matched
Unmatched
EFFECTS OF SPACE CHARGE
Linear space charge forces oppose focusing and result in smaller “depressed” wavevector.
Nonlinear forces cause particles at different amplitudes to experience different periods of oscillation. Results in emittance growth. In extreme cases results in “filamentation.”
Depressed and Nonlinear Forces
Reiser, Martin. Theory and Design of Charged Particle Beams, n.d.
Tecker, F. (2021). Injection and Extraction. arXiv preprint arXiv:2108.11160.

## Slide 20: Varying PINN Knobs

## Slide 21: Varying PINN Knobs