## Slide 1: Production, Acceleration and Stability of High Brightness Electron Beams in Cryogenic RF Structures
Speaker: F. Bosco*
PI: Prof. J. Rosenzweig
* fbosco@physics.ucla.edu
This work was supported by the U.S. National Science Foundation under Award PHY-1549132, the Center for Bright Beams
Beam Dynamics and Control CBB Meeting – 2023/09/28
Notes: My PI and I, postdoc at ucla and cbb member since April
the project I am working on is

## Slide 2: About Me
Education
Jan 2023 – PhD in Accelerator Physics at the University of Rome “La Sapienza”
May 2019 – Master degree in Electronics Engineering at the University of Rome “La Sapienza”
October 2016 – Bachelor degree in Electronics Engineering at the University of Rome “La Sapienza”
Research experience
2019 – 2023: PhD Researcher at La Sapienza’s Department for Basic and Applied Engineering
2022: Visiting graduate researcher at UCLA in the Particle Beam Physics Laboratory (PBPL)
2018: Internship at Fermi National Accelerator Lab
Main research interests
Accelerator physics, beam dynamics, collective effects, tracking codes, high brightness electron
linacs, RF photo-injectors, electrodynamics and RF-systems, particle driven radiation sources
Notes: My background is in EE, I majored art URLS where I also got my PhD in acc physics. Collab with ucla and

## Slide 3: Outiline
Cryogenic RF Initiatives
  High field C-band RF structures
  State of the art facilities: UC-XFEL, C3
  Investigating solutions to enhance the brightness
CYBORG Beamline at MOTHRA
  Present status
  Next steps towards commissioning
MILES – Beam Dynamics
  Simplified modeling for self-induced fields
  Example of applications: e.g. stability and mitigation of BBU effects
Notes: What’s next? Research goals for my postdoc

## Slide 4: Cryogenic RF Initiatives
Scientific collaboration of research institutes in the fields of accelerators and beam physics
Interest in high brightness electron linac-based facilities exploiting advanced accelerator concepts
  Compact, high brilliance radiation sources (FEL, ICS)
  High luminosity linear colliders for HEP
Initiatives
Ultra-Compact X-rays Free Electron Laser (UC-XFEL): new paradigm for university-scale facilities
Cool Copper Collider (): based on C-band (6 GHz) cryo-cooled, distributed coupling linacs ()
High gradient acceleration in RF Structures
Distributed coupling linacs: use of guiding manifolds
Optimized cavity topology to enhance the efficiency of acceleration
Cryogenic operation (77K) to reduce the breakdown probability rates
Notes: Larger picture
This work takes place in the framework of an international collaboration
The partners involved share the interest in exploiting advanced accelerator and beam physics concepts in order to realize state-of-the-art facilities based on high brightness electron linear accelerators
The main initiatives of the collaboration are addressed to compact, particle-driven radiation sources such as FEL and ICS machines but there is, in addition, a strong interest for high luminosity lepton colliders
In this context, our research group contributes to the beam dynamics studies with a special dedication for the collective effects attributed to space charge forces and wakefileds. The former describe the field produced and experienced by the charged beam itself whereas the latter is responsible for the interaction of the beam with the surrounding environment

## Slide 5: Beam Brightness
M. Reiser, Theory and Design of Charged Particle Beams,
John Wiley & Sons, New York, 1994
The performance of advanced linac-based application relies on the high beam brightness: high current, low transverse emittances and narrow energy spectrum
A demanding example: efficient FEL radiation: and where is the Pierce parameter
Brightness is hard to preserve: must be high at source and not diluted by the linac
RF photoinjectors: a “recipe” for high brightness beams
Photo-emission: UV, sub-ps laser pulse illuminating a metallic photo-cathode
Acceleration: high field multi-cell standing wave RF cavity
Focusing: a solenoid magnets controls emittance and spotsize
Energy-boost: matching to a linac where the beam experiences gentle focusing and emittance compensation
Notes: The 6D brightness is a quantity that provides information on the beam intensity, spectrum and solid angle as it depends on the peak current, the energy spread and the rms emittances.
The brightness is thus a measure of the 6D phase space density and crucially impacts the quality of the radiation in electron-driven light sources
In addition, the rms emittances account for the transverse phase space area as well as its distortion which allows to describe the confinement of the beam nearby the reference trajectory
High brightness electron beams are typically produced by rf photoinjectors where the photo-emission occurs inside a SW multi-cell cavity which rapidly accelerates the particles acting against the intense repulsive intra-beam forces
Photoinjectors also exist in the hybrid configuration which combines a SW and a TW section through a coupling cell
The SW section still provides for the energy gain, a solenoid magnet introduces transverse focusing and emittance control as in the case of conventional rf guns whereas the TW can provide longitudinal focusing
In fact, the peculiarity of this device is that the field in the two sections is 90 degrees out of phase which introduces an energy-time correlation so that, as the beam propagates in a drift space, it experiences a ballistic compresses which enhances the peak current with a positive impact on the brightness

## Slide 6: How to Improve the Brightness at Source?
Additional knobs
Maximum achievable current density: high launch field at cathode
Laser wavelength tuning: for (physical material temperature)
Materials: novel photo-cathodes with enhanced performance
Effective temperature (MTE) and QE trade-off: for

## Slide 7: CYBORG Beamline
CYBORG (CrYogenic Brightness Optimized RF Gun)
  Investigate the attainable brightness at the source in high field (>120 MV/m) cryogenic (<90 K) RF guns at the emission threshold ()
  Stepping stone for the UC-XFEL cryogenic 1.6 cell RF gun
The beamline is situated in MOTHRA Lab (Multi-Objective Testing for High field RF Accelerators), on-campus lab at UCLA
Courtesy of G. Lawler
Notes: MOTHRA is an on-campus lab at UCLA that performs studies for the development of high gradient rf accelerators. In particular the beamline sketched here is under development and it aims to investigate the attainable beam brightness of cryogenic photocathodes by use of a half cell gun
The latter will establish a proof-of-principle for the operation of cryogenic rf guns and a stepping stone for the actual 1.6 cell photoinjector foreseen by the UCXFEL

## Slide 8: CYBORG Beamline (2)
Half-cell C-band (5.712 GHz) RF gun in thermal contact with a cryostat cold-head
  Phase 1: Copper photo-cathode
  Phase 2: Design of a load-lock system to test alternative photo-cathodes
Optics (solenoid and quadrupole magnets)
Diagnostics (screens, spectrometer, FC/ICT, emittance-meter)
Klystron+modulator
0.5 gun + cryostat
Courtesy of G. Lawler

## Slide 9: Current Status
Characterization of the cryo-RF infrastructure
  Cooling capabilities
  Temperature dependent surface resistivity
  Frequency detuning
  Vacuum tests
Klystron to gun connection (waveguide, circulator, probes): ready for high field tests (e.g. dark current)
Crystal detector probe calibration
Surface resistance vs temperature

## Slide 10: What’s Next?
Steps towards the commissioning of the beamline
Installing the optics/diagnostics: alignment with HeNe laser
Transport of the UV Laser to the cathode
UV Laser & RF Gun field synchronization: design of a MW circuit that controls the phase delay
Design of a TEM grid system for the emittance measurement of low charge beams
Design of an ICT system for non-destructive charge measurement
(*tasks I have started to work on recently/will start soon)

## Slide 11
Beam Dynamics Studies with the code MILES
Notes: Imagine we produce a decent emittance at the source: we don’t want

## Slide 12: Collective Effects in Linacs
Space Charge Forces
Wakefield Interaction
Charged particles exert mutual repulsive forces
For two particles at distance traveling with velocity one has radial force ()
For an arbitrary distribution, the strength of the force depends on both its shape and size
Generally slice-dependent
Space charge forces – PIC Methods
Solve Poisson equation in the beam frame
Lorentz field transformation in the lab frame
Integration of the equations of motion
Wakefield interaction – Convolution integral
Knowledge of the wake-function
Calculate the wake-potential (convolution integral with the current)
Field generated by the beam, diffracted by the discontinuities and acting back on the beam itself
Responsible for energy spread and transverse deflection
Slice-dependent deflection dilutes the projected rms emittance: BBU effects
Courtesy of M. Migliorati
Notes: To be clear, when we talk about fast algorithms we should mention the conventional approaches utilized to describe the two types of collective effects we are interested in
The strength of the space charge forces arising from the local field produced by the charge distribution itself, generally depends on both the shape and the size of the beam and therefore common models utilize PIC methods
On the other hand the wakefields arising from the interaction of the charges with surrounding environment and responsible for energy spread as well as transverse deflections are commonly described by the convolution between the charge density and the so-called wakefunctions accounting for the interaction between two charges

## Slide 13: The Code MILES
Dedicated tracking code
Motivation to investigate wakefields effects in linacs in presence of non-negligible space charge endangering the nominal beam quality
Use of simple semi-analytical models: flexible and time-efficient tool (factors 1/40-1/10) with acceptable reduction of the accuracy
Main applications: investigation of misalignment effects and design of possible correction schemes
MILES = Multi-bunch and Intra-beam effects in Linacs Evaluating Stability
Miles Davis (May 26, 1926 – September 28, 1991)
Modeling overview and comparison with other codes
 | MILES approach | Commonly utilized approaches
Space Charge | Equivalelent ellipsoid or Multi-slice superposition | Particle in cell (PIC)
Wakefields | Algebraic formalism | Convolution integral or FFT equivalent
F. Bosco et al., “Fast models for the evaluation of self-induced field effects in linear accelerators,” NIM-A vol. 1056, p. 168642, 2023 https://doi.org/10.1016/j.nima.2023.168642
Notes: The necessity to perform customized studies on wakefield effects has motivated us to develop MILES: a dedicated tracking code investigating wakefield effects in linacs while also including simple models for space charge forces
The code uses semi-analytical approaches that yield a flexible and time-efficient tool at the expenses of an acceptable reduction of the accuracy
For the sake of time today I will not focus on the models adopted by this code however if anyone is curious to know more you can find the details on this paper that was accepted in NIM las week
----
Floquet expansion of the longitudinal field on axis
The fundamental harmonic (𝑎_1) is resonant with the beam and provides acceleration
The non-synchronous harmonics (𝑎_𝑛, 𝑛>1) provide transverse focusing
-----
It is well known that high intensity electron beams, such as those employed for radiation sources or linear colliders, are subjected to a strong wakefield interaction when accelerated in high gradient linacs. This can result in a significant loss in terms of phase space quality or can lead to instabilities such as the Beam Breakup.
In this work we describe the development of a custom tracking code meant to investigate the effects of transverse wakefields in linacs. Based on simple models, the code turns out to be very light and flexible with typical run-times below one minute.
As the code accounts also for space charge forces through the model of an ellipsoidal beam, we called it MILES which is an acronym for Modeling Instabilities in Linacs with Ellipsoidal Space charge.

## Slide 14: Injection in a Linac Booster - WP
Emittance compensation in a split RF photo-injector: RF gun + linac booster
Beam-linac matching: proper combination of acc. gradient, transverse focusing, current, energy and spotsize
Shift the injection position and adjust the avg accelerating field to minimize the final emittance
(total drift = 112 cm + d)

## Slide 15: Beam Based Alignment (BBA)
Alignment errors cause off-axis motion: excitation of dipole wakes leads to emittance growth
Design of correction schemes: BPM readings are used to adjust the strength in the steering dipole correctors
Reference case from the UC-XFEL
Two section linac ()
Section 1 is 100 off-axis
Moderate corrector strength (order of )
vs
vs
Notes: An alternative approach I have recently investigated is to find a trajectory for which the excitation of dipole wakefield is minimized so that we can expect minimum emittance growth
If two dipole correctors per linac module are employed instead of a single one, we have two degrees of freedom which allow to adjust the offset and the angle independently at each section’s input
This procedure forces the beam to travel always on the axis of a given linac section so that dipole wakes are not excited and the emittance growth is limited
The solution is very simple and it works with moderate strength of the dipole correctors

## Slide 16: What’s Next?
Long range BBU effetcs: mutual interaction among different bunches in multi-pulse operation
  High luminosity linear colliders -> C3 and its intermediate stages (250 GeV, 550 GeV, TeV-scale)
  Hard X-rays FELs for chip metrology (2.44 GeV)
Identify potential new problems that can be described by and benefit from the fast simulation framework
  E.g. Dielectric wakefield accelerators (DWA) rectangular slabs with alternating gradient for BNS damping

## Slide 17: Conclusions
Advanced accelerator applications rely on high brightness electron beams: motivation to increase the beam brightness
Near threshold emission at cryogenic temperatures with high launch fields has notable advantages
CYBORG beamline: a demonstrator for this emission scheme
  Progress in the development of the cryo-RF infrastructure
  Excitement for the next steps leading to the machine commissioning
Potential quality dilution due to strong self-induced EM fields: modeling and mitigation with dedicated codes
Beam Dynamics and Control CBB Meeting – 2023/09/28
Thank you for your attention
(Questions are welcome)
* fbosco@physics.ucla.edu
This work was supported by the U.S. National Science Foundation under Award PHY-1549132, the Center for Bright Beams
Acknowledgements
G. Lawler, A. Fukasawa, Y. Sakai, O. Williams, J. Rosenzweig, G. Andonian,
P. Manwani, M. Yadav, W. Lynn, J. Mann, S. O’Tool, J. Pan, J. Phillips, G. Anand

## Slide 18: Acknowledgements
Acknowledgements
G. Lawler, A. Fukasawa, Y. Sakai, O. Williams, J. Rosenzweig, G. Andonian, P. Manwani, M. Yadav, W. Lynn, J. Mann, S. O’Tool, J. Pan, J. Phillips, G. Anand

## Slide 19
Spare slides

## Slide 20: Modeling Space Charge Forces
Beams consist of large ensembles of charged particles exerting mutual repulsive forces
For arbitrary distributions, the strength of the force depends on both its shape and size
Exact solution typically utilizes particle in cell (PIC) approaches
Equivalent ellipsoid method
Multi-slice superposition method
An equivalent uniform ellipsoid is associated to the actual beam distribution
Self-induced forces are known analytically
Forces are linear: self consistent model
Advantages
Very fast ( times of 3D PIC )
Successfully reproduces rms size () and energy spread ()
Limitations
Absence of correlation prevents the observation of emittance dynamics
Loss of axial symmetry in presence of strong transverse wakefield
Divide the beam in cylindrical slices with individual size, energy and aspect ratio
Field produced by each (uniform) slice is known analytically (, )
Superposition of the fields produced by all the slices
Correlation between the planes describes the emittance dynamics
Allows description of more arbitrary geometries
More time-consuming but still faster than PIC
Advantages/Limitations
Notes: For what concerns SC forces, the strength of such effects depends on the shape and the size of the distribution, and therefore their description utilizes PIC methods
Here I am showing two alternative semi-analytical methods:
The first one associates the actual beam to an equivalent uniform ellipsoid which produces well-known self induced forces
whereas the second one divides the beam in cylindrical slices with individual size and energy and producing a field in this form in the surrounding space
The force acting on each particle is then given by the superposition of the EM field produced by all the slices
The ellipsoid method is very fast and in many practical cases reproduces the rms beam dimension and energy spread correctly
However, since the forces are not slice-dependent, the model forbids to observe well-known emittance dynamics that are induced by the independent evolution of the beam slices
In addition, in presence of wakefields, the deflection introduced by the transverse wake will displace the centroid of each slice breaking the symmetry that is implied in the ellipsoidal model meaning that the model is not valid in strong-BBU regime unless correction schemes for the trajectories are introduced
The multi-slice approach overcomes both this limitations: it exhibits correlation between the planes and allows description of more arbitrary shapes. The drawback is that this method become more time consuming but remains faster than a PIC

## Slide 21: Modeling Space Charge Forces (2)
Longitudinal plane: ,
beam from the C-band hybrid photoinjector
Evolution in a field-free (drift) region with GPT (solid lines) and with the ellipsoidal model in MILES (dashed lines)
Transverse plane: ,
M. Ferrario et al., Direct measurement of the double emittance minimum in the beam dynamics of the Sparc high-brightness photoinjector, Phys. Rev. Lett. 99, 234801 (2007).
Equivalent ellipsoid method
Multi-slice superposition method
beam produced by the hybrid gun and matched to its invariant envelope in a booster linac
Emittance dynamics: oscillations in the drift and compensation in the linac
Injection in the booster
Notes: Here we can see some examples where our approach is compared to codes like GPT and ASTRA, both using PIC
In both cases we consider the beam produced by the hybrid photoinjector that, on the left, propagates in a long drift space and on the right is injected in a booster linac receiving emittance compensation
On the LHS MILES is using the Ellipsoidal model which, as anticipated, describes the transverse and the longitudinal dimensions as well as the energy spread correctly but it fails to reproduce the emittance oscillation
On the RHS the ellipsoidal model still fails in describing the evolution of the rms emittance however the multi-slice approach reproduces successfully both the oscillation in the drift and the compensation process

## Slide 22: Modeling Wakefield Effects
State after the charges have passed
particles operations
Evolution of the voltage state
Perturbation:
Kick induced by the passing charges
Recursive formula
Free-evolution:
Homogenous 2nd order differential equation
Interaction of a particle with a cavity resonant mode
The change in momentum (energy/deflection) is described by the equivalent shunt circuit voltage
Notes: Here I want to introduce the algebraic formalism that I developed in order to describe the effects of both longitudinal and transverse wakefields
The fundamental idea upon which the formalism relies is the interaction of a charged particle with a resonant cavity mode
Such modes can wither be the actual higher order modes excited in the accelerating structures or can be used to represent arbitrary wakefunctions
It can be shown that the energy variation as well as the deflection of a particle interacting with a resonant mode can be described in terms of the voltage across the equivalent RLC circuit representing the mode. Therefore, all is needed is to keep track of the evolution of the voltage continuously excited by the passing charges
The evolution of the voltage state, consisting of the voltage and its derivative, is described by this operator where the matrix M accounts for the free-evolution according to the usual homogeneous differential equation whereas the perturbation vector p modifies the state after the passage of a new charge
The voltage state after the transit of n charges is obtained by the composition of operators of such kind and provides a recursive formula which significantly reduces the number of operations with respect to the convolution integral approach

## Slide 23: Collective Effects in Linacs
Space Charge Forces
Wakefield Interaction
Beams consist of large ensembles of charged particles exerting mutual repulsive forces
For two particles at distance traveling with velocity one has the radial force ()
For an arbitrary distribution, the strength of the force depends on both its shape and size
Space charge forces – PIC Methods
Solve Poisson equation in the beam frame
Lorentz field transformation in the lab frame
Integration of the equations of motion
Wakefield interaction – Convolution integral
Knowledge of the wake-function
Calculate the wake-potential (convolution integral with the current)
Field generated by the beam, diffracted by the surrounding environment and acting back on the beam itself
Causality: for the self-field acts behind the source
Responsible for energy spread and transverse deflection
Courtesy of M. Migliorati
Notes: To be clear, when we talk about fast algorithms we should mention the conventional approaches utilized to describe the two types of collective effects we are interested in
The strength of the space charge forces arising from the local field produced by the charge distribution itself, generally depends on both the shape and the size of the beam and therefore common models utilize PIC methods
On the other hand the wakefields arising from the interaction of the charges with surrounding environment and responsible for energy spread as well as transverse deflections are commonly described by the convolution between the charge density and the so-called wakefunctions accounting for the interaction between two charges

## Slide 24: Modeling Wakefield Effects (2)
Energy spread induced by the longitudinal SRWF in a linac section (longitudinal phase space)
Misaligned linac section: the beam propagates off axis exciting dipole wakes which cause emittance growth
Transverse interaction
Injection
Extraction
Longitudinal interaction
rectangular beam propagating in two linac sections with transverse offset and
rectangular beam propagating on-axis in a long linac section: long. phase-space
Short-range wakefield (SRWF) effects in a distributed coupling linac
Longitudinal monopole and transverse dipole wake-functions from diffraction theory
Head
Tail
Notes: Here we consider an example where the SRWF excited in a distributed coupling linac cause mutual interaction among particles in the same bunch
The longitudinal and transverse binary interaction in a periodic accelerating structure is described by use of diffraction theory by means of well known wake-functions
In the first example the longitudinal wakefield excited in the linac affects the energy spread of an originally monochromatic beam modifying its projection on the LPS
In the second example a misaligned linac section causes the beam centroid to travel off-axis where dipole wakefields are excited causing a growth of the rms emittance
In both cases our model reproduces the expected behavior

## Slide 25: Trajectory Steering
Steering magnets: dipole fields of moderate strength providing correction of the trajectories
Transverse kick from a corrector of integrated field
Beam position monitors (BPMs) measure the transverse position of the beam
Beam based alignment (BBA): adjust the strength of the kickers as a function of the BPM readings
Courtesy of A. Mostacci
Notes: As shown by the previous example, dipole wakes excited in misaligned linacs are a cause of emittance dilution
Therefore it is useful to exploit our code to design correction schemes for the beam trajectories based on the combination of BPMs steering dipole magnets
BPMs measure the transverse displacement of the beam at various locations and such information can be exploited to adjust accordingly the strength of the dipole kickers upstream modifying the center-of-mass trajectory
This correction technique is known as beam based alignment

## Slide 26: Beam Based Alignment (BBA)
vs
vs
Moderate corrector strength ()
vs
vs
Alignment errors cause off-axis motion: excitation of dipole wakes leads to emittance growth
Design of correction schemes: BPM readings are used to adjust the strength in the steering dipole correctors
Reference case from the UC-XFEL
Two section linac ()
Section 1 is 100 off-axis
One-to-one steering: one corrector upstream each linac section
“Wake-free” steering: two correctors upstream each linac section
Notes: Here we show two possible correction schemes applied to a common reference case where the first section of the UCXFEL linac is 100 um off-axis
On the LHS we use one steering magnet per linac section forcing the trajectory to intersect the linac axis at the BPM locations which reduces but does not prevent the emittance growth since the algorithm aims for a local control of the trajectory instead of a global optimization
On the RHS instead, we use two steering magnets per linac section so that we can force the beam to propagate always on the axis of each section regardless of the misalignments. In this case the excitation of dipole wakes is minimized and the emittance is preserved
----
As shown by the previous example, dipole wakes excited in misaligned linacs are a cause of emittance dilution
Therefore it is useful to exploit our code to design correction schemes for the beam trajectories where measurements of the transverse offset are used to adjust the strength of the steering dipoles deflecting the beam

## Slide 27: Sources of Wakefields in Linacs
Longitudinal monopole and transverse dipole impedance from diffraction theory
Responsible for the short-range wakefield (SRWF) interaction in periodic accelerating structures
Modes in resonant cavities
Periodic accelerating structures
, ,
Field generated by the beam, diffracted by the surrounding environment and acting back on the beam
Responsible for energy spread and transverse deflection
Longitudinal monopole and transverse dipole higher order modes (HOMs) in the accelerating cavities
Responsible for the long-range wakefield (LRWF) interaction ( and )
Notes: So far we have only focused on the benefits associated with this type of structures but we should also say that high shunt impedance structures are accompanied by stronger wakefields
Wakefields are self-induced EM fields produced by the beam and diffracted by the discontinuity of in the surrounding geometry
Such parasitic fields introduce energy spread and transverse deflection that are described by a dedicated formalism that makes use of the wake-functions
In rf linacs the main contribution of wakefields is introduced by the interaction with the accelerating structures themselves
Depending on the time scale of the separation among the particles, two types of effects are observed: a long range interaction due to the excitation of HOMs introduces coupling among different bunches whereas a short range interaction due to the cell irises introduces intra-beam coupling described by diffraction theory

## Slide 28: Beam Breakup Effects
Long-range transverse interaction
Short-range transverse interaction
Off-axis bunches
Excitation of dipole HOMs
Transverse deflection
Instability: the amplitude of the center of mass oscillation grows
!
Phase space dilution: the correlation between the planes is a cause of emittance growth
!
Notes: These two types of interaction in the transverse plane are responsible for BBU effects
In particular, in the LR time-scale bunches traveling off-axis will excite dipole HOMs which causes deflection of the trailing bunches. Eventually, this process repeats itself in a cycle leading to an instability: the amplitude of the transverse oscillation grows without control
In the short-range time-scale the slice-dependent deflection induced by the SRWF introduces a correlation between the longitudinal and transverse planes leading to a growth of the projected emittance

## Slide 29: Beam Loading Effects
Long-range longitudinal interaction
Short-range longitudinal interaction
Energy exchange with self-EM fields:
bunch-to-bunch and intra-beam energy spread
!
Energy spread induced by the longitudinal SRWF in a linac section (LPS)
Before
After
Bunch to bunch final energy variation due to the longitudinal LRWF
Notes: Similarly, on the longitudinal plane particle exchange energy with the longitudinal wakefields which leads to bunch to bunch energy spread in the long-range time scale and intra-beam energy spread in the short range time scale

## Slide 30: Wakefields in the Structures
Monopole HOMs
Dipole HOMs
SRWF
LRWF
Dipole
Monopole
Solid - -mode
Dashed -- -mode
= -mode
Notes: We should start by a quantitative description of our wakefields
In the SR case the wakefunctions can be calculated by the geometric parameters of the cell and we can notice that such fields are sligthly stronger for the 3pi/4 mode (in solid lines)
And the same is true for the R/Q of the higher order modes so me must be prepared more serious problems

## Slide 31: Long-range BBU in the Linac
BBU studies for the 250 GeV CM working point of the linear collider
Center of mass oscillations and beam loading effects in multi-bunch operation: sequence of point-like, structureless macro-particles carrying the whole bunch charge
Notes: The following example takes into account the 250 GeV CM working point of the C3 linear collider
The relevant parameters for our purposes can be read from this column

## Slide 32: Long-range BBU in the Linac (2)
RF-pulse (flat-top) filled with 133 bunches, each, and separation (30 RF-periods)
Acceleration at an avg loaded gradient of
Injection off axis causes excitation of dipole HOMs
Amplitude of the transverse oscillation for each bunch in the rf-pulse at the interaction point normalized to the first bunch’s amplitude
Mitigation: detuning of the HOMs
Unstable motion if the ratio is close to an integer (see Mosnier)
Small variations of the original geometry: HOMs exhibit different frequencies in subsequent linac sections
Notes: Here we investigate an injection error of 100 um in absence of mitigation techniques and
The plot shows the amplitude of the transverse oscillation and the energy for each one of the 133 bunches in the rf-macro pulse at the end of the linac.
Allow me a quick comment on the beam loading: I shouldn’t have included this effect as the loaded gradient already accounts for it. The reason why I did is to show that this effect is indeed strong and this energy droop is consistent with the beam power to rf power ratio
For the transverse oscillations, amplitudes are normalized to the value of the first bunch (which by causality doesn’t experience dipole wakes) showing grow factors ranging from 20k to 140k that require clearly require mitigation

## Slide 33: Long-range BBU in the Linac (3)
Amplitude of the transverse oscillation for each bunch in the rf-pulse at the interaction point normalized to the first bunch’s amplitude
Detuning of the HOMs
Unstable motion if the ratio is close to an integer (see Mosnier)
Mitigation through frequency spread (or detuning)
Small variations of the original cavity geometry: HOMs exhibit different random frequencies in subsequent linac sections
Notes: It is possible to demonstrate that the motion becomes highly unstable when the ratio of the HOM frequency and the bunch repetition rate is close to an integer as the mode and the pulsed beam fulfill a resonant condition
A possible mitigation scheme, known as frequency spread, consists in applying small changes to the nominal geometry of the cavity so that the mode will appear with different frequencies in subsequent linac sections
Such fluctuations break the coherent interplay of the pulsed beam with the mode
Repeating the previous simulation with frequency spread. We can observe that, since all the normalized amplitudes are close to 1, breaking the interaction pattern cancels the BBU-effects completely

## Slide 34: SRWF and LRWF Simultaneously
Reference case
UC-XFEL scenario (100 bunches, 6 RF-bucket () separation: 100 pC, 0.5 mm rms long beam, ~100 nm emittance at injection)
2 linac sections: with the 1st section is 100 um off-axis
Notes: The last bit that I want to show is an extension of the capabilities of our simulations in order to include simultaneously space charge, sr and long range wakefields in the same simulations and observe some of their subtle interplays
Here we are considering again the same scenario from the previous slide ust without correction magnets but we accelerate a train of 100 bunches to observe, ina ddition their mutual coupling.
A subtle effect that we notice is that the bunch to bunch energy variations due to the beam loading affect the beam trajectories so that one observes slightly different emittances between the first and the last bunch of the RF pulse

## Slide 35: Acknowledgements
La Sapienza
M. Carillo
E. Chiadroni
L. Ficcadenti
D. Francescone
G. Franciosini
L. Giuliano
M. Migliorati
A. Mostacci
L. Palumbo
G. J. Silvi
INFN-LNF
D. Alesini
M. Behtouei
A. Cianchi
L. Faillace
M. Ferrario
A. Gallo
A. Giribono
B. Spataro
C. Vaccarezza
UCLA
G. Andonian
O. Camacho
S. Crisp
A. Fisher
A. Fukasawa
G. Lawler
M. Lenz
W. Lynn
J. Mann
P. Manwani
P. Musumeci
J. B. Rosenzweig
Y. Sakai
O. Williams
M. Yadav
SLAC
C. Emma
Z. Li
N. Majernik
E. Nanni
R. Robles
S. Tantawi
Radiabeam
P. Carriere
M. Kravchenko
A. Murokh
M. Ruleas
LANL
P. Anisimov
D. Kim
E. Symakov
Notes: I want to thank my supervisors prof. MM and LP but also I want to acknowledge all the people with whom I had positive scientific discussions during daily work, meetings and workshops