## Slide 1: Machine Learning Applications for Improving Accelerator Operations at Brookhaven National Laboratory
July 20, 2023
Lucy Lin
Advisor: Georg Hoffstaetter de Torquat
CBB Annual Meeting

## Slide 2: The Electron Ion Collider (EIC)
Collisions between fundamental particles produce a 3-D snapshot of their internal arrangement of quarks and gluons
Understand strong nuclear force: how are quarks and gluons held together within ordinary matter?
Solve spin crisis: The three main constituent quarks cannot account for a proton’s total spin. How exactly do quarks and gluons contribute to a proton’s spin?
We improve EIC luminosity, polarization, and operation with machine learning (ML) techniques

## Slide 3: Injector compound for RHIC and EIC
Relativistic Heavy Ion Collider (RHIC): largest operating accelerator in the US.
Electron Ion Collider (EIC): the nation’s largest particle accelerator project.
Alternating Gradient Synchrotron (AGS) and its Booster serve as part of the injector compound for RHIC and future EIC.
Bright ion beams in the AGS and Booster are required for optimal luminosity and highest polarization in RHIC and EIC.
Obtaining bright beam requires more accurate beam control in the injector compound, which is currently mostly hand tuned by operators.
Injector Compound

## Slide 4: ML Method 101: Neural Network (NN)
Establish mapping between a given set of inputs and corresponding outputs
No prior knowledge about the mapping is needed for training
Trained NN model is faster and cheaper to evaluate than the real system

## Slide 5: Machine Learning for Better Orbit Correction

## Slide 6: Orbit in an Accelerator
Design orbit: ideal orbit the particles should move on, defined as
Particles need to be bent (by dipoles) and focused (by quadrupoles)
Closed orbit: equilibrium orbit actually moved on, with harmonic oscillations around the design orbit caused by magnet focusing force

## Slide 7: Orbit Measurement and Correction
Beam Position Monitor (BPM): pick up electrodes (PUE) measure charges induced by electric field of the beam
Corrector magnet: dipole magnets for closed orbit correction, give horizontal / vertical kicks to charged particles

## Slide 8: Orbit Correction with Neural Network
Traditional orbit correction
  obtain mapping from corrector settings to orbit measurements
  inverse mapping to get corrector settings needed to cancel orbit deviations
Orbit correction with NN
  train directly to get inverse mapping, no need for extra calculation
  easily update with new data and stay accurate

## Slide 9: NN model: corrector orbit
Input vertical corrector kick Output y orbit measured at BPM
Trained on 800 data pairs, tested on 200 data pairs: accuracy = 99.8%

## Slide 10: Inverse NN model: orbit corrector
Input y orbit measured at BPM Output vertical corrector kick
Trained on 800 data pairs, tested on 200 data pairs: accuracy = 99.3%

## Slide 11: Future work: error identification
Neural Network
Beam properties (e.g. orbit)
Magnet settings + Machine errors
Neural network can establish mapping between any inputs and outputs with sufficient data
Machine error sources (e.g., misalignment, gradient / calibration errors, etc.) can be included as outputs of an inverse NN model for beam-based error diagnostic algorithm

## Slide 12: Current to Magnet Strength Calibration with Neural Network

## Slide 13: Magnet current to strength mapping
Magnet transfer function: mapping between the power supply (PS) current and the resulting strength of a magnet
Example: 5th order polynomial for Booster quadrupoles
Transfer functions are measured before the magnets were installed in the ring, and there is no existing way to verify them after installation.

## Slide 14
Preliminary NN model training results
Input y orbit under different quadrupole PS currents Output corresponding vertical quadrupole strength
Initial data was collected with magnet settings within the linear range of the transfer function, working on collecting more data
Trained on 800 data pairs, tested on 200 data pairs: accuracy = 99.5%

## Slide 15: Future work: Optimization with ML
Control parameters + Environmental factors
Evaluation Metric (e.g., agreement with real measurements)
Neural Network
Bayesian Optimization
Find best settings for desired machine state

## Slide 16: References
[1] W. Lin, et al., “Machine Learning Applications for Orbit and Optics Correction at the Alternating Gradient Synchrotron”, in Proc. IPAC’23, Venice, Italy, May 2023.
[2] W. Lin, et al., “AGS Booster Beam-based Main Quadrupole Transfer Function Measurements”, in Proc. IPAC’23, Venice, Italy, May 2023.
[3] N. Ketkar, “Feed forward neural networks,” in Deep Learning with Python: A Hands-on Introduction. 2017, pp. 17–33.
[4] K. Brown, et al., “A high precision model of AGS Booster Tune Control,” in Proc. EPAC’02, Paris, France, June 2002, pp. 548–550.

## Slide 17: Thanks
Petra Adams, Kevin Brown, Bhawin Dhital, Yuan Gao, Levente Hajdu, Kiel Hock, Vincent Schoefer
Georg Hoffstaetter de Torquat, David Sagan
Weining Dai, Bohong Huang, Thomas Robertazzi

## Slide 18: Thank you! Questions?