## Slide 1
TFPX Mechanics Mini Workshop
Karl Smolenski
Feb. 8, 2024

## Slide 2: Where are we?
NSF MREFC Review
Year of Covid
Recent Phase
Production
TFPX

## Slide 3: Scope of TFPX Mechanics
ITST design and manufacture, indico: 685933 & 682294
TEPX
TFPX
TBPX
Tracker Bulkhead Disk
CMS endcap beam-pipe
Inner Tracker Support Tube (ITST)
Beam-pipe support collar,
Dee
Beam-pipe support “fishing rods”
IT installation/support rails in the ITST
Beam-pipe connection flanges and bellow
Beam interaction point
CMS central beam-pipe
Module
Service Cylinder
image source:
Antti Onnela
Indico /682359

## Slide 4: What do we need to do?
Collect 2D “images” of passing particles over a series of 8 planes, in the forward regime on both sides of the interaction point.
IP
TFPX

## Slide 5: Systems architecture
TFPX
Electrical power
CO2 cooling
Particles
Dry air
Track (XYZ)
Time stamp (?)
Fiber optic data link

## Slide 6: Cartridge layout (sort of)
Cartridge is the core element of TFPX layout
2 dees (sensors support) + local electronics
Final issues being resolved:
  thermal pathways
  cable routing
  kinematic mounts
  mechanical attachments
kinematic mounts
e-link routing, rear disk
mechanical – dee attachment
Portcard and DC/DC converter mezzanine
e-link paths
Serial Power (to outside of service cylinder
e-link connector
e-link routing, front disk
modules
FiberOptics Ring

## Slide 7: Cartridge layout (sort of)
Currently water jetting PEEK edges to be bonded into layout
Allows for structural and module mounting tapped holes
mechanical – dee attachment
Module Mounting

## Slide 8: Key Tasks for Summer
Dee structure (CF / foam / tube / foam / CF)
  Slicing of carbon foam
  Epoxy vs. Co-curing CF to carbon foam
  Machining of perimeter, groove for tube, and recesses for threaded inserts
  Application of glue to groove for tube
  Glue / install Peek perimeter
  Bonding of two halves together
  Metrology of final product (flatness, mass, stiffness)

## Slide 9: Tube Gluing into Carbon Foam
Cross Section X-ray CT scan shows minimal leakage of epoxy into foam
Loctite / Hysol / Henkel EA9396 Epoxy – as used by TED OT group

## Slide 10: Key Tasks
Module (sensor) Thermal Performance
  Thermal Interface Material (TIM) between module and dee
  Thermal stack up (tube to foam to CF to TIM to module)
  Radiation damage of TIM
  How to positively locate module
  How to clamp it in place
  Gantry operations for assembly / TIM application
  Tube routing, optimization, and simulation

## Slide 11: Thermal Modeling
Francesco Bianchi

## Slide 12: Thermal Modeling
Francesco Bianchi

## Slide 13: Busy !!!
Other topics
  E-links
  Prototype serial power flex circuits
  Thermal mock-up modules
  Prototype portcards
  Portcard structure
  Sapphire cartridge mounting structure