## Slide 1: Thermal Simulations of TFPX Dee
Shikha

## Slide 2: Objective of the Simulation
To track the temperature on the surface of Dee
Check for temperature gradients and track it’s cause while aiming for low temperature
To perform a comparative study of thermal performance from experimental and simulation results
Currently running the simulation test with plaquette

## Slide 3: Different Cases for 2-D Simulation in Ansys Steady Thermal
1. Sandwich Model
2. Hot Dog Model
3. Short Hot Dog Model
4. Hot Dog + Toppings Model

## Slide 4: Boundary Conditions for 2-D Simulation

## Slide 5: 2-D Simulation
Ran steady thermal simulation in Ansys for all the 4 cases, with three different values of thermal conductivity of carbon fiber – 20, 2, 0.2 (all in W/mK), and keeping the thermal conductivity of carbon foam 25 W/mK
Temperature trend:
4 < 1< 2 < 3
if we keep the thermal conductivity of carbon fiber and carbon foam same for each trial

## Slide 6: 2-D Simulation Results
1. Sandwich Model
2. Hot Dog Model
3. Short Hot Dog Model
4. Hot Dog + Toppings Model

## Slide 7: 3-D Simulation in Ansys Fluent: Geometry

## Slide 8: Boundary Conditions for 3-D Simulation
INLET:
coolant at Temperature: -29.9 ℃, Pressure: 13.34 bar
OUTLET:
coolant at Temperature: -33.5 ℃, Pressure: 11.84 bar
AMBIENT is Air at -21.5 ℃ with heat transfer coefficient of 5 W/K

## Slide 9: 3-D Simulation Results

## Slide 10: Further Plan
Mesh improvement
Grid-independent test
Extracting heat transfer coefficient of the coolant from Ansys Fluent
Transient simulation with ambient temperature changing