## Slide 1: CyberInfrastructure Training and Education for Synchrotron X-Ray Science (X-CITE) Overview of CHESS Research Workflow & CI
Anirban Mandal, Erik Scott, Sajith Sasidharan (RENCI, UNC Chapel Hill)
Ewa Deelman, Karan Vahi, Mats Rynge (ISI, USC)
Matthew Miller, Werner Sun, Peter Ko, Kelly Nygren, Keara Soloway, Rolf Verberg (CHESS, Cornell)
Brandon Sorge (IUPUI)
NSF OAC Award Numbers: 2320373, 2320375, 2320374

## Slide 2: CHESS Experiment Timeline
For MOST projects, experiments begin BEFORE the beamtime.
Material/Sample Fabrication
Experiment Planning
Beamtime
Data Reduction
Analysis
Dissemination
Detailed experimental plans should be generated and agreed upon with your beamline scientist
Input Arrays for data collection campaigns may be generated ahead of the beamtime for some experiments
(may require python + pandas, numpy package)
Provenance should be included in metadata collected during beamtime
You may need to perform calculations or SIMULATIONS prior to your beamtime to prepare for your data collection strategy
(may require using domain-specific software prior to beamtime)
Work with your staff scientist to know what to expect at different times in your experiment life-cycle which trainings are relevant at which times

## Slide 3: Data Collection at CHESS
The beamtime/data collection part of the research workflow is often overwhelming in terms of CI/computing for many users - we will focus on this part of the research workflow in this session.

## Slide 4: Large Burden of Expertise For Users
Users need to become proficient (often experts) across multiple fields
DOMAIN SCIENCE
X-RAY SCIENCE
COMPUTING & CYBER INFRASTRUCTURE
OTHER
(e.g. MODELING, SIMUALTIONS etc.)
Historically users were on their own to learn this - learned on-the-fly AT the beamline
When they start their synchrotron journey: most users - regardless of discipline
do not have a sufficiently strong background in scientific computing or cyber infrastructure to perform synchrotron measurements and subsequent analysis
Increasing user cyber and computing literacy before the time of data collection will allow users to focus on science decisions at the beamline, rather than being overwhelmed by learning these skills in real time

## Slide 5: Diverse Science Drivers & Communities at CHESS
7 Beamlines – each specializing in a specific scientific domain & set of techniques
Partner model - 3 subfacilities – each with their own missions, deliverables, structure, and allocation policies

## Slide 6: Data Collection: Computing & CI
Computing and CI literacy needs vary across beamlines and even for different techniques within a beamline.
All programs
Program/Technique Specific
Most Programs/Techniques
Many of these categories have XCITE courses associated with them.
Users should work with their beamline scientists to understand what is required for their experiment.
Experimental station | XS100
CHESS Networks | XS100
CHESS Filesystem | XS100
CHESS Compute Farm | DC200
CHESS BYOD Policies | XS100
Python | PE100-2
SPEC | 
Git | PE103
Program-Specific Software Packages (e.g. GSASII, DIALS, HEXRD, PyMCA, NEXUS, etc.) | 
Pandas | 
Matlab | 

## Slide 7: Anatomy of an Experimental Station: Station Computer
All experimental stations are controlled by a special computer , the station computer that communicates to all the hardware and software needed for data collection.
The station computer typically runs a number of processes and is responsible for orchestrating data collection, motor motions, synchronized triggers, metadata logging, and more.
The station computer has special permissions that allows it to communicate with protected devices and filesystems.
Be a good steward:
Only interact with processes that your staff scientist has approved or trained you on
Do not launch additional terminals from the station computer without consulting your staff scientist (some programs will overload and crash the computer if run locally and disrupt data collection)
Controls
Station Computer
Centralized
Data Storage
Compute Farm
Experimental Station

## Slide 8: Station Computer: Linux and CLI
The station computers run on Linux - currently Scientific Linux 7
Users should be familiar with the
- Linux OS,
- Terminal and using a Command Line Interface (CLI)

## Slide 9: Anatomy of an Experimental Station: Station Computer
Many stations use SPEC as the data acquisition software and EPICS for instrument control
SPEC is a language, loosely based on C, used for instrument control and data acquisition at many synchrotrons.
When using spec, you will interact with a SPEC terminal and run a combination of “standard” SPEC commands and/or a series of compiled programs for your technique
EPICS is a set of software tools and applications which provide a software infrastructure for use in building distributed control systems to operate devices
Many of the devices at CHESS leverage EPICS drivers for operation EPICS PVs (process variables) are commonly used for signal monitoring and metadata/data logging.
Your staff scientist will tell you which commands are appropriate at your station

## Slide 10: Station Computer: ID1A3 Example

## Slide 11: Station Computer: ID1A3 Example

## Slide 12: Station Networking
Ethernet/Fiber
CHESS Public Network
CHESS DAQ
Station Isolated Network (10Gb)
Direct Network Lines between equipment (sometimes >100Gb lines)
WiFi
Eduroam
RedRover
Cornell Visitor
LNS Protected (requires registration with CLASSE-IT)
Data is traveling rapidly between devices, computers, and storage locations
Specialized, fast pathways to move data between equipment are protected and/or isolated. Only approved instruments/devices can be connected to these networks.
Ethernet cables are color coded:
CHESS Public Network = White
DAQ = orange
Station isolated network = pink

## Slide 13: CHESS-DAQ Filesystems
Data Tier | Description | Total size | Nightly Incremental | Full Backup | Paths
DAQ/RAW | Raw data | 1587 TB (4/23) | ✓ | Per cycle | Linux: /nfs/chess/daq, /nfs/chess/raw Win: \\chessdaq\daq, \\chesssamba\raw
METADATA | Metadata | 150 TB (AUX) | ✓ | Per cycle | Linux: /nfs/chess/aux/metadata Win: \\chesssamba\aux\metadata
REDUCED DATA | Reduced non-BTR |  |  | Per cycle | Linux: /nfs/chess/aux/reduced_data/user Win: \\chesssamba\aux\reduced_data\user
 | Reduced BTR |  |  | Per cycle | Linux: /nfs/chess/aux/reduced_data/cycles Win: \\chesssamba\aux\reduced_data\cycles
USER | Project space | 40 TB | ✓ | Monthly | Linux: /nfs/chess/user Win: \\chesssamba\user
SCRATCH | Temp files non-BTR | 30 TB |  | — | Linux: /nfs/chess/scratch/user Win: \\chesssamba\scratch\user
 | Temp files BTR |  |  | — | Linux: /nfs/chess/scratch/cycles Win: \\chesssamba\scratch\cycles

## Slide 14: Protected Data: Intellectual Property (IP) and Export Control
Some data needs to be protected, e.g. data covered under Intellectual Property or Export Control agreements
All such data must be declared and all agreements signed before ANY data is on CHESS/Cornell computing systems (including preparatory material that falls under IP or Export Control categories).
Data Collection, Storage, and Analysis can be customized to comply with data agreements, including:
Modifying isolated networks
Mounting encrypted drives
Configuring encrypted computers
Modifying permissions on filesystem locations
Securing the experimental station with an entry password
Disconnecting streaming video to the experimental station

## Slide 15: Bring Your Own Device (BYOD)
Examples include:
Controls computer for equipment they have integrated for an experiment
Analysis computer for on-the-fly analysis
All devices must be approved at least two weeks in advance. It may not be possible to consider integration on a shorter time period.
If you are bringing a computer that needs to read the DAQ (raw data directory), computer must be registered to be added to the LNS Protected WiFi network:
https://wiki.classe.cornell.edu/Computing/LaptopRegistration
Users may need to bring their own devices to be beamline - either physically in the lab or remotely connected to the CHESS networks

## Slide 16: Large Data Volumes and File Transfers
Hot/Cold Data Storage
The preferred method for file transfer is using Globus: https://wiki.classe.cornell.edu/Computing/GlobusDataTransfer
Data may be too large to easily transfer to user’s home institution / not enough requisite compute resources home institution.
When data is initially written to the “raw” data drive, it is available for direct access for data transfer or analysis.
Due to the volumes of data produced at each beamline, your raw data may be moved to “cold” storage (aka tape) after approx. 6 months.
The data is still saved, but to transfer or perform analysis on the files you will need to arrange to have it rolled back into “hot storage” - AKA take out an IT ticket: https://wiki.classe.cornell.edu/Computing/ServiceRequestTips

## Slide 17: Real Time Visualizing, Computing, Data Reduction
National Science Data Fabric (NSDF) Dashboard (deployed at 3A & 4B)
Inline Data Processing/Computing
Many beamlines have an initial “data reduction” procedure that reduces the size of the data through compression or on-the-fly analysis to have smaller file sizes that are more manageable to analyze at your home institution.
Some of these processes are software procedures performed on the data after it is written to the raw directory, while other beamlines utilize inline data processing/compression prior to writing their files to the raw directory.
Large data sizes and volumes are historically hard to visualize
Dashboard built on OpenViSUS to enable real time visualization
https://services.nationalsciencedatafabric.org/chess/

## Slide 18: Metadata Services
Metadata and parallel data streams are generated at every stage of your experiment.
CHESS is continuing to develop and implement services to help with this creation. From programs like Galaxy, to our Metadata service (see right).
Metadata Service
Providing tools to record and automatically ingest machine-readable metadata in a systematic way.
Includes variables that historically were not recorded via a second data stream (e.g. the material processing parameters)
Ideally, all the data necessary to fully reproduce your results are recorded and disseminated in a manner that others can interpret after your experiment. Ideally the provenance remains unbroken from experiment planning.
https://wiki.classe.cornell.edu/bin/viewauth/CHESS/Private/CHESSMetadataService

## Slide 19: Experimental Beamtime Notes
Beamtime Notes / Supplementary Documentation Best Practices
Commenting Software
For recording notes during the beamtime, we recommend using plain text or Markdown language (formatted text file) because it is easy to read in many systems, rather than a Microsoft Word Document which has a proprietary format. Images can be rendered in markdown formats.
Ultimately, some of the most important metadata comes from your experimental logbook. Your beamtime notes must supplement metadata provided during data collection in such a way that your experiment could be entirely reproduced. It is important to record any scientist decisions and the reasons for making those decisions in your beamtime notes.
Your beamline scientist may not remember every detail of your beamtime - it is not their responsibility - it’s yours.
Save your beamtime notes or a copy of your beamtime notes or (link to your google doc / equivalent) on the CHESS filesystem with your data (your beamline scientist will tell you where the best place is)
Friendly Reminder:
No spaces in file names. Use _underscores_ or CamelCase.
File names should start with a letter, not a number.
Comment any code produced at the beamtime. If this code was used to make decisions about the experiment, it should be saved and referred to in your experimental log.

## Slide 20: JupyterHub
Most software will be domain and technique specific. CHESS has many common X-ray software packages available on the system.
Science/Technique Specific Software
For at-beamline code development, we recommend leveraging our JupyterHub :
https://wiki.classe.cornell.edu/Computing/JupyterHub
https://jupyter01.classe.cornell.edu/
or using an Integrated Development Environment (IDE) at your beamline (e.g. Visual Studio Code, Spyder, Matlab, etc.)
Software Development

## Slide 21: Data Analysis Science Specific Software Packages
CHESS has many common X-ray software packages available on the system.
Speak with your beamline scientist for the preferred software package for your experiment.
If YOU are interested in creating a tutorial or linking us to one for an XCITE module, we’re interested!
…and so many more!!!

## Slide 22: CLASSE Compute Farm
See “CI Resources at CHESS and Beyond”
More information available at
https://wiki.classe.cornell.edu/Computing/ComputeFarmIntro

## Slide 23: CHESS Analysis Pipeline (CHAP)
Object-oriented framework
Data analysis code organized into reusable modules
  Reader
  Processor
  Writer
Multiple inputs
User interface
  Command line (expert)
  Galaxy (non-expert)
  CHAPBook (coding interface)

## Slide 24: X-CITE Workshop Agenda
Time | Content
8:30 - 8:50 am | Introduction to X-CITE training program
8:50 - 9:40 am | Overview of CHESS research workflow and CI (data collection software, data analysis software, Compute Farm, preparing for beamtime)
9:40 - 09:55 am | Break
9:55 - 10:55 am | Programming modules (Python and Jupyter, packages/libraries Conda, numerical analysis with Python)
10:55 - 11:20 am | Systems Fundamentals (Linux, command line, scripting)
11:20 - 11:40 am | CI resources at CHESS and beyond (job submission, CHESS systems, other NSF resources (ACCESS))
11:40 - 12:15 pm | Town Hall on CHESS User Experiences and Challenges
12:15 - 1:15 pm | Lunch
1:15 - 3:15 pm | Hands-on session with complete end-to-end data analysis examples
3:15 - 3:30 pm | User survey and feedback
3:30 - 4:30 pm | Office hours

## Slide 25: Thanks
NSF Cybertraining Award # 2320373
Project website: https://sites.google.com/view/x-cite-nsf/home
Training materials: https://xcitecourse.org