## Slide 1: From Limits to Breakthroughs: Short-Pulse RF Acceleration at GV/m level gradient
Afosr+nsf scientific opportunities with compact, high intensity accelerators
erhtjhtyhy
Chunguang Jing
Euclid Techlabs LLC,
Argonne National Laboratory
2/24/2026

## Slide 2: outline
Dependence of Gradient on RF pulse length
  Scaling law?
  Observation from CLIC 30GHz era
  Discovery of BIAR (breakdown insensitive accelerator regime) at AWA
Make a short RF pulse case for >500MeV/m gradient
Challenges and R&D work

## Slide 3
Dependence of Gradient on RF pulse length

## Slide 4
Relevant history of studying RF breakdowns dependences on rf pulse length
Theoretical model
Experimental efforts

## Slide 5
Empirical scaling law
BDRE305
A. Grudiev et al., Phys. Rev. ST-AB, 12, 102001 (2009).
Empirical formula summarized from decade of high gradient accelerator research (x+ka bands)
110 MV/m
SLAC Breakdown and pulse heating study 2010 (from F. Wang, AAC10 presentation)
SLAC Breakdown study 2008 (from V.A. Dolgashev, AAC10 presentation)
Freq. | Pulse length (ns) | Max. Grad. (MV/m)
S-band at FERMI 2.0 | 700 | 28
C-band in Japan | 300 | 50
X-band at CERN | 180 | 120
Shorter pulse length
Shorter pulse length

## Slide 6
A 30-cell structure with Mo irises and low ES/EA largely exceeded the CLIC accelerating field requirements without any damage
190 MV/m accelerating gradient in first cell - tested with beam ! (but only 16 ns pulse length)
Observation from CLIC 30GHz era
30-cell clamped tungsten-iris structure

## Slide 7: Discovery of BIAR (breakdown insensitive accelerator regime) at AWA-I
Single-cell structure
- Optimized for maximum transient gradient
Normal cell properties (11.7 GHz) | 
Iris diameter | 6.1 mm
Iris thickness | 2.9 mm
Phase advance | 120 degree
Quality factor | 6070
Shunt impedance r/Q | 1.4x104 Ω/m
Group velocity | 0.0114c
80%
92%
93%
100%
- The input matching cell has higher gradient and surface field than the normal cell

## Slide 8
Main pulse
Secondary pulse
Input
pulse
RF conditioning
Experimental setup
Main pulse
Secondary pulse
Normal transmitted pulse
- 7.7x104 pulses accumulated at 2 Hz repetition
Conditioning
Testing
Discovery of BIAR at AWA-II

## Slide 9
BD type I
BD type II
- Distorted main pulse
- Disappeared after conditioning
- Likely to be caused by multipacting
Main pulse
Secondary pulse
H. Xu et al., PRAB 22, 021002 (2019)
- Blocked secondary pulse and normal main pulse
- Probability decreases after conditioning
- Likely to be caused by RF breakdown
Main pulse
Secondary pulse
Discovery of BIAR at AWA-III

## Slide 10: Long-pulse high-power test at Tsinghua
RF conditioning
Experimental setup
- 2.3x107 pulses accumulated at 40 Hz repetition
- Driven by klystron with pulse compressor
Y. Jiang et al., IEEE Trans. Microw. Theory Tech., 69, 1586-1593, (2021)
Courtesy of Hao Zha

## Slide 11: Results discussion (I)
Comparison of short and long pulse results
Fit to BDRE30
Accelerating gradient of the normal cell and the input matching cell reaches 270 MV/m and 310 MV/m
Surface field of the input matching cell reaches 500 MV/m
Gradient improved at least twofold using short pulse (limited conditioning period, only secondary pulse taken into consideration)
BDR vs. pulse length doesn’t follow the empirical scaling law in short-pulse regime
New physics of RF breakdown in short-pulse regime
Eap1/6 =Const.

## Slide 12
Breakdown Insensitive Acceleration Regime (BIAR)
RF causes BD and plasma generation
RF pulse
0 ns
Plasma expansion to block RF transmission
after ~10 ns
ANL: ϕ10-20 μm
Tsinghua: ϕ30-100 μm
Transmitted RF pulse and accelerated beam not influenced by RF breakdown
Reduced structure damage due to limited energy available for breakdown avalanche
Results discussion (II)

## Slide 13
PETS
beam
RF
Prototype TW-gun
Reflection signal from bi-directional coupler
a
a
b
b
c
c
d
d
Quick ramp-up
Dark current loading
Conditioning & dark current reduction
Achieved 350MV/m on cathode
Observed strong dark current loading regime but quickly conditioned away
It only took 70k pulses for a full condition
Back to 200MV/m to 250MV/m region, no breakdown, no measurable dark current
Euclid, SBIR Grant #DE-SC0018709, 2020
Another example: short pulse RF photogun

## Slide 14
Make a short RF pulse case
for
>500MeV/m gradient

## Slide 15
Short Pulse Acceleration to achieve 500MeV/m of geographical gradient
We are currently developing an X-band accelerator operating in the short pulse regime.
Simply scale this structure to 11.7*3=35.1GHz, then R/Q is the same, Vg is the same, then 300MW will build up ~500 MV/m. If double the power from PETS to 600MW, the gradient will be ~700 MV/m. If the fill factor is 0.7, the geographical gradient will be ~500MeV/m.
But, the beam aperture will be <1.5mm. (ref. CLIC 30GHz has aperture 2.4mm~3.2mm.)
Parameters | Designed Values
Freq. | 11.7 GHz
Filling time | 6 ns
Structure length | 25 cm
Input Power | 320 MW
Gradient | 170 MV/m
BW
FW
Hybrid FW-BW-accelerator

## Slide 16
On the power source side
 | AWA X-band PETS in operation | Scale 3 X frequency |  | 
PETS basics | Metallic ID=17.6 mm ¦ L=30 cm | Metallic ID=5.9 mm ¦ L=30 cm |  | 
PETS freq. | 11.7 GHz | 35.1 GHz |  | 
Power | ~400 MW | ~600 MW |  | 
Pulse length | ~9 ns (full) | ~15 ns (full) |  | 
σz ¦ F(ω) | 1 mm ¦ 0.94 | 0.5 mm ¦ 0.93 |  | 
Qb | 50 nC | 9 nC | 3 nC | 1 nC
Bunch spacing | 796 ps | 256 ps | 85 ps | 28 ps

## Slide 17
Challenges and R&D work

## Slide 18
Accelerators Subject to study tailed to short pulse regime
  Main accelerating structure (WF, BD)
  Power extractor (WF)
  Drive beam production

## Slide 19: single bunch applications
 | Klystron power | Energy gain | MeV/(MW*Trf[us]) per Str.
S-band standard | 50MW, 3us | 50MeV in 3m (16.7MeV/m) | 0.33
NLC Xband | 75MW x 2=150MW, 1.6us, compress to 450MW, 400ns | 270MeV in 6.5m ( 6 structures, total 5.4m structures,83% fill factor, 50MeV/m) | 1.5
CLIC-Kly Xband | 53MW x 2=106MW, 2us, compress to 170MW x 2=340MW, 334ns | 276MeV in 4.6m (80% fill factor, 8 structures, 0.46m ea., 75MeV/m) | 2.43
CLIC-TBA Xband | 132MW from ea. PETS, 176.5ns | 46MeV in 57.5cm (80% fill factor, 2 structures, 23cm ea. , 100MeV/m) | 2
Short Pulse X-band-TBA | 537MW from ea. DPETS, 22ns | 36MeV in 37.5cm (80% fill factor, one structure, 30cm, 120MeV/m) | 3
Short pulse X-band Kly | 20MW, 1us, compress to 250MW, 10ns | 40MeV in 25cm (80% fill factor, one structure, 20cm, 200MeV/m) | 16*
If we use this as a Figure of Merit for an accelerating structure,
Def: RF usage rate
Notes: One drive beam to rule them all (simple), drive beam gives the accelerator designer frequency freedom
Could energy jitter get translated to timing jitter in the kickers?

## Slide 20: Remarks
  CLIC 30GHz era left abundant data and many unanswered questions, which is worth revisiting them.
  Experiments in short pulse regime exhibits some unique performance which is worth exploring.
  Challenges on wakefield damping are tremendous, but it may work perfectly for the single bunch or light beam loading applications.
Notes: One drive beam to rule them all (simple), drive beam gives the accelerator designer frequency freedom
Could energy jitter get translated to timing jitter in the kickers?

## Slide 21
Thanks for your attention!