## Slide 1: Rapid Density-Modulated Electron Beam Sources for Next-Generation X-ray Communications
Brandon E.J. Cortez, Halil Topözlü, Melisa Bozdemir, John Lambrecht, John H. Booske, Nader Behdad
Department of Electrical & Computer Engineering
University of Wisconsin-Madison
2026 AFOSR + NSF Scientific Opportunities with Compact, High Intensity Accelerators
This material is based upon work supported by the Air Force Office of Scientific Research under AFOSR awards FA9550-21-1-0367 and FA9550-18-1-0062 and by the National Science Foundation Graduate Research Fellowship for Brandon Cortez.

## Slide 2: Motivation for X-ray Communications
Hypersonic vehicles develop plasma sheaths
Plasma sheaths repel RF/microwave  comms blackout
X-rays can penetrate plasma sheaths
X-ray Communications (XCOM)
Potential benefits
  Penetrative
  Security
  Ultra fast data rate
Notes: Problem, Solution, More Benefits

## Slide 3: X-ray Production
Kramer’s Law for Bremsstrahlung
  X-ray intensity at energy E, I(E)
  Atomic number (Z)
  Beam current (I0)
  Electron energy (E0)
  X-ray energy (E)
Characteristic X-rays
X-ray spectra
Notes: X-ray Production Basics

## Slide 4: State of the Art
XCOM proposed in 2007 by Gendreau, et al
2015 Gendreau, et al awarded patent for miniaturized high-speed modulated x-ray source
Grid voltage modulation [Chen, et al 2021]
Photocathodes [Li, et al 2025]
Magnetic deflection to leverage characteristic x-rays [Jin, et al 2021]
Demonstrated only up to ~10 MHz modulation rates
Notes: SOTA Gap

## Slide 5: TWT Beam Modulation
Slow-wave circuits  wave-particle energy exchange
Wideband helix Traveling Wave Tube (TWT)
  0.2 – 1 GHz frequency range
Modulated RF signal into TWT  output density-modulated electron beam (spent beam)
Notes: Our Solution: Use a TWT as the transmitter

## Slide 6: Fast X-ray Detector: Avalanche Photodiode (APD)
APD used to detect soft X-ray intensity
Avalanche effect  high gain  highly sensitive
X-rays ionize to create even more electron-hole pairs
APD’s can be very fast
Notes: Need a fast X-ray detector: use an APD

## Slide 7: Experimental Configuration
Notes: Put components together to get full system configuration

## Slide 8: Internal Set-up
Target
Shielded APD
E-beam
X-rays
Target
Shielded APD
Notes: Follow system figure up with real internals

## Slide 9: External Set-up
LaB6 thermionic cathode on externally adjustable track
20 kV/650 mA power supply; pulse generator and HV switch pulses cathode negative; chamber, anode are grounded
500 Gauss axial magnetic field confines beam
Magnet Power Supply
Magnets
O’scope
High Voltage Power Supply
Electron Gun
TWT
XCOM Components
Notes: Zoom out to see the externals

## Slide 10: Leveraging Titanium Characteristic X-rays
Simulation of Ti/Mo target X-ray production
Ti/Tungsten Target Spectra
Notes: X-ray efficiency is awful, so for accessibility we leverage Ti

## Slide 11: Performed Test: 50 us Pulse Measurement
Simulation:
Al-Filtered X-ray Spectra
Measurement:
50 us X-ray Pulse
Notes: Test: Confirmed slow X-ray signal measurement, no amplifier

## Slide 12: Measured Electron Beam Modulation: 575 MHz Carrier, 125 MHz On-Off Keying
Notes: Test: How well does our TWT output preserve input signal

## Slide 13: Proposed Test: Sinusoidally Modulated X-rays
Notes: Proposed Test (not measured/simmed): Can APD resolve sinusoidally varying X-ray intensity from our modulated beam?

## Slide 14: Proposed Test: Amplitude Modulation
Notes: Proposed Test (not measured/simmed): Use OOK with our set-up, determine limitations.

## Slide 15: The Direct Approach
The Hot Electron Light Assisted Cathode (HELAC)
Notes: The Direct Appraoch: modulate beam at the source

## Slide 16: Hot Electron Light Assisted Cathode
A. Priyoti, et al, https://doi.org/10.1021/acsphotonics.3c01383
Notes: HELAC basic principles

## Slide 17: Hot Electron Light Assisted Cathode
A. Priyoti, et al, https://doi.org/10.1021/acsphotonics.3c01383
Notes: HELAC basic principles

## Slide 18: HELAC Testing Fixture

## Slide 19: Thermally Enhanced Quantum Efficiency
Emission/Device Currents v. Temperature (With Varied Device Bias)

## Slide 20: Conclusions
Takeaways:
  XCOM-TWT: Proof-of-concept for much higher modulation rates
  HELAC: Novel thermally-enhanced photo-gated cathode
Our next steps:
  XCOM-TWT: Reduce EMI beam coupling; Explore modulation schemes
  HELAC: Develop NIR-sensitive HELAC-based e-gun for XCOM