## Slide 1: The Cornell High Brightness Injector
Colwyn Gulliford, Adam Bartnik

## Slide 2: Outline
Previous results
  Introduction
  Emittance ≤ 77 pC
  High current ≤ 75 mA
High brightness at higher charge?
  Good emittance with Q ≥ 100 pC?
  Is high current still possible?

## Slide 3: Injector Layout
NaKSb: MTE = 140 meV, QE roughly 5%
Superconducting
RF Cavities (niobium)
400 kV DC Gun +
Bunching/Focusing
Short SRF Linac
5 – 15 MeV
6 Dimensional Phase Space Diagnostics + High Power Beam Dump + Chicane (Compton Scattering)
Viewscreen
Emittance Measurement System
1st Scanner
Magnet Pair
2nd Scanner
Magnet Pair
1st Slit
2nd Slit
Deflecting Cavity
Faraday Cup
+ Viewscreen
Faraday Cup
400 kV DC Gun
50 MHz
520 nm

## Slide 4
Laser Shaping
Transversely: clip Gaussian laser profile at a given intensity
fraction (typically 50%)
Longitudinally: Birefringent Crystals for pulse stacking:

## Slide 5: Previous results
Emittance measurements1 (merger section, 7 MeV)
350 kV Gun
Met requirements for ERL
Bunch charge | Bunch length | Horz Emit. (100%) | Vert Emit. (100%)
19 pC | 2.1 ps | 0.33 mm | 0.20 mm
77 pC | 3.0 ps | 0.69 mm | 0.40 mm
High current operation2,3 (straight section, 4 MeV)
250 kV Gun
Up to 75 mA peak, reliable operation at 65 mA
> 60 hour cathode lifetime at 65 mA (NaKSb)
1. Gulliford el al., Phys. Rev. ST Accel. Beams 16, 073401 – 2013
2. Cultrera el al., Appl. Phys. Lett. 103, 103504 (2013)
3. Dunham el al., Appl. Phys. Lett. 102, 034105 (2013)
Asymmetry Due to the Merger?

## Slide 6
Low emittance at high charge

## Slide 7: LCLS-II Injector Tests
CU Injector as possible injector for high rep. rate FEL (LCLS-II)
9.5 MeV
Straight linac - No ERL merger section!
Goal: measure emittance at specified charge / peak current:
Bunch charge | Peak current | Emittance (95%)
20 pC | 5 A | 0.25 mm
100 pC | 10 A | 0.4 mm
300 pC | 30 A | 0.6 mm

## Slide 8: Expectations: Simple Scaling
Use previous results to get a rough estimate of what to expect:
Assume optimal emittance scales like
Previously:
(in merger)
Need around 0.8 mm (100%) emittance to get 0.6 mm (95%)
Requires removal of asymmetry (Merger? Couplers?)
Note: emittance may scale worse than
Bunch charge | εn,x(100%) | εn,y(100%)
19 pC | 0.33 mm | 0.20 mm
77 pC | 0.69 mm | 0.40 mm
300 pC | 1.36 mm | 0.79 mm
Note prior asymmetry in x , y

## Slide 9: Expectations: Simple Scaling
Use previous results to get a rough estimate of what to expect:
Assume optimal emittance scales like
Previously:
(in merger)
Need around 0.8 mm (100%) emittance to get 0.6 mm (95%)
Requires removal of asymmetry (Merger? Couplers?)
Note: emittance may scale worse than
Bunch charge | εn,x(100%) | εn,y(100%)
19 pC | 0.33 mm | 0.20 mm
77 pC | 0.69 mm | 0.40 mm
300 pC | 1.36 mm | 0.79 mm

## Slide 10: Initial trouble at 20 pC
Bunch charge | Peak current | Emittance (95%)
20 pC | 5 A | 0.25 mm
100 pC | 10 A | 0.4 mm
300 pC | 30 A | 0.6 mm
Beam Based Alignment
Loaded optimized settings
Tuned machine (few weeks)

## Slide 11: Initial trouble at 20 pC
Bunch charge | Peak current | Emittance (95%)
20 pC | 5 A | 0.25 mm
100 pC | 10 A | 0.4 mm
300 pC | 30 A | 0.6 mm
Beam Based Alignment
Loaded optimized settings
Tuned machine (few weeks)
Found emittance X/Y asymmetry that could not be removed!
V: 0.62 mm (95%)
H: 0.26 mm (95%)
Can’t be from the merger….

## Slide 12: Origin of asymmetry
Increasing solenoid current
Found a beam asymmetry after (only) the first solenoid!
Tilt = half Larmor angle -> stray quad inside solenoid
Wired simple corrector quad through BPM feedthrus
Quad wiring
Increasing solenoid current
+
+
-
-
R
20pC, before correction:
20pC, after correction:

## Slide 13: Results
Q (pC) | Ipeak Target (A) | Ipeak (A) | εn Target (95%, mm) | εn (95%, mm) | εn,th /εn
20 | 5 | 5 | 0.25 | H: 0.18, V: 0.19 | 60%
100 | 10 | 11.5 | 0.40 | H: 0.32, V: 0.30 | 80%
300 | 30 | 32 | 0.60 | H: 0.62, V: 0.60 | 70%
After another month of work…
Emittance asymmetry is gone
Met spec at all charges
Same SRF settings for all charges

## Slide 14: Agreement with Simulation
Current profile agrees well at all charges

## Slide 15: Effects of the Laser Shape
Ideal Shape
Measured Shape

## Slide 16: Even larger charge?
Q (pC) | Peak current (A) | Emittance (95%, mm)
20 | 5 | H: 0.18 V: 0.19
100 | 11.5 | H: 0.32 V: 0.30
300 | 32 | H: 0.62 V: 0.60
1000 | 50 | H: 1.6 V: 1.6
2000 | 56 | H: 4.4 V: 4.0
Primary result (omitting details): Emittance trend becomes more linear above 300 pC

## Slide 17
High current with high charge

## Slide 18: Off center cathode
Laser profile during high current
High charge -> Large laser spot
Anode clips laser light more than 9 mm from cathode center
  To avoid central 3 mm, laser size must be <6 mm
  Sets a hard upper limit to charge
Practically, at the time of the experiment, we only had a 3 mm cathode
  Simulation -> Hard limit to charge with 3 mm ~ 450 pC
3 mm

## Slide 19: High current operation
Space charge limit?
High current machine settings (more conservative)
  350 kV gun
  5 MeV final energy
See dramatic increase in radiation around 320 pC
  Changing machine settings did not help
  Made laser size (slightly) bigger: same problem at 375 pC (~ 20 mA)
  Even bigger would require larger cathode… future work!
Radiation while increasing charge

## Slide 20: Laser Modifications
Laser size scales as
Problem:
1 nC, laser size > 6 mm
Solution:
Lengthen laser pulse:
  4 crystals -> 5 crystals
  8 ps -> 25 ps
1 nC, optimal D = 5 mm
  Feasible!

## Slide 21: Summary
DOE Nuclear Physics awards
DE-SC0012493, DE-AC02-76SF00515
The CU injector meets all LCLS – II requirements
  Emittance growth well compensated up to 300 pC
  (at 300 pC) εth = 0.41 mm, final at 9.5 MeV: εn = 0.6 mm
  Emittance scales roughly as
At higher charge, compensation is worse
  1nC: εth = 0.6 mm, εn = 1.6 mm
  Emittance scales roughly as Q
Full (50 MHz) duty factor demonstrated up to 375 pC (20 mA)
  Likely need a larger (off-center) cathode to go further

## Slide 22
Acknowledgements
Thanks to the Cornell High-brightness Beam Group: