## Slide 1: FFAG Recirculation and Permanent Magnet Technology for ERL’s
N.Tsoupas, S. Brooks, A. Jain, G. Mahler, F. Meot, V. Ptitsyn, D. Trbojevic BNL
M. Severance SBU
1/17

## Slide 2: ERL & FFAG based eRHIC
arXiv:1409.1633
Novel FFAG lattice allows 16 beam re-circulations using only two beam transport loops
2/17

## Slide 3: FFAG recirculation passes
E=21.2 GeV
E=6.6 GeV
E=5.3 GeV
E=1.3 GeV
QF
BD
eRHIC uses two FFAG beamlines to do multiple recirculations. (FFAG-I: 1.3-5.4 GeV, FFAG-II: 6.6-21.2 GeV)
All sections of a FFAG beamline is formed using a same FODO cell. Required bending in different sections is arranged by proper selection of the offsets between cell magnets (or, alternatively, with dipole field correctors).
Permanent magnets can used for the FFAG beamline magnets (no need for power supplies/cables and cooling).
Orbits in Transition section
Each of two eRHIC FFAGs contain 1066 FFAG cells
Orbits in Detector bypass section
Quad offsets evolve adiabatically
@S.Brooks, D.Trbojevic
3/17

## Slide 4: FFAG Cell of the eRHIC
N=212 cells per arc, 1.680 m
0.48 m
6.622 GeV
BD = 0.0813 T,
Gd = -30 T/m
xDoffset=+2.7 mm
x(mm)
1.334 GeV
2.656 GeV
5.3 GeV
Bf= 0.0813 T,
Gf= 30 T/m
xFoffset= -2.7 mm
8.1 mm
-8.8 mm
3.978 GeV
70 cm
6 cm
o
0.44 m
2.7 mm
2.7 mm
=0.283o
4/17

## Slide 5
2D Design establishes the magnet’s cross section
-The 12pole multipole=0 for R=1 cm
-NdFeB-N45 allows for larger inner radius
Perm. Magnet Material SmCO
Perm. Magnet Material NdFeB
5/17

## Slide 6: 3D Magnetic field calculations for the FFAG cells
6/17
3Dimensional Field map is
obtained over the volume of
a single cell where beam exists.
QF
QD
=0.283o
cell

## Slide 7
 | [Gauss] | Q_Diff/Qmeas | [Gauss.cm-4] | 12p_diff/Qmeas
SmCo R26HS Temp.=20o Calculations | 18730.5 |  | 337.4 | 
Magnet#1 Measurement | 18650.0 | 4.3x10-3 | 350.6 | 7x10-4
Magnet#2 Measurement | 19096.0 | 20x10-3 | 371.5 | 17x10-4
Long coil measurement of the magnetic multipoles at R=1 cm
7/17

## Slide 8: The Optics of the Low Energy FFAG cell*
Calculate the closed orbits in the range 1.3 GeV to 6.6 GeV
Calculations of tunes Qx,Qy and chromaticities x, y per cell.
Calculations of the maximum beam emittances x, y transported in the low energy arc for each of the five orbits.
Calculations on the dynamic aperture of the transport ring.
Calculation of the beta functions.
3D Field Maps were obtained from the 3D EM Calculations
* The zgoubi computer code was used in the calculations.
8/17

## Slide 9
1.3 GeV
2.6 GeV
6.6 GeV
QF
QD
Beta functions of 3 different energies
x
y
9/17

## Slide 10: Cornell-BNL FFAG-ERL Test Facility (Cb)
NS-FFAG arcs, four passes (similar to first eRHIC loop)
Momentum aperture of x4, as for eRHIC
Uses Cornell DC gun, injector (ICM), dump, 70MeV SRF CW Linac
Prototyping of essential components of eRHIC design

## Slide 11: 76 – 286 MeV NS-FFAG Cornell Lattice 100 cells : Orbits and magnets in the 10.5 m diameter
BD
QF/2
x (mm)
32.99 cm
10.99 cm
3 cm
-8.98 mm
GD = -27.493 T/m
ByD = 0.5044 T
x = + 18.331 mm
GF = 42.54 T/m
ByF =-0.104 T
x = 2.44 mm
11.9 mm
4.0 cm
11 cm
286 MeV
216MeV
76 MeV
146 MeV
4.0 cm
QF/2
ECEN=225 MeV
qD=73.93 mrad
11.2 mm
15.8 mm
qF/2=-11.088/2 mrad
2.44

## Slide 12
QF Quadrupole is displaced -2.44 mm with respect to the central Orbit (CO)
Version # 1
Material NdFeB-N45
Gradient = 42.54 T/m
Inside a radius of 1.7 cm all multipoles including 12pole have strength <10-4
Inside a radius of 12 mm all multipoles including 12pole have strength <10-4
Halbach Dipole=0.504 T
Halbach Quad=–27.493(T/m)

## Slide 13
Z-axis of each cell

## Slide 15
Inside a radius of 1.7 cm all multipoles have zero strength
QF Quadrupole is displaced -2.44 mm with respect to the central Orbit (CO)
Gradiend = +42.54 T/m
Version # 2
Material NdFeB-N45
In a circle R=~12 mm with center (x=18.346 mm, 0)
Multipoles strength 10-5 or less
Gradiend = -27.5 T/m

## Slide 17
Thank you
for your attentions