## Slide 1: SRF Technology for High Current Application
Matthias Liepe
Associate Professor of Physics
Cornell University
M. Liepe June 18, 2015 Slide 1

## Slide 2: Outline
Introduction
High Current Injector SRF
ERL High Current Main Linac SRF
Conclusions
M. Liepe June 18, 2015 Slide 2

## Slide 3: Introduction
M. Liepe June 18, 2015 Slide 3

## Slide 4: Energy-Recovery-Linacs Linac Quality Beams with Storage Ring Beam Currents
M. Liepe June 18, 2015 Slide 4
3. Use beam for science, e.g. x-ray generation
6. dump beam:
low dump energy,
less radioactivity
2. acceleration
4. Recirculate beam
5. deceleration
to re-use energy
Example: 5 GeV linac, 100 mA
S.C. without energy-recovery: >1 GW
S.C. with energy-recovery: <15 MW
1. Injection
fresh beam

## Slide 5: Example: The Cornell ERL X-Ray Light Source
M. Liepe June 18, 2015 Slide 5
ERL main linac: 5 GeV SRF linac, 100 mA with energy recovery, 5 kW RF power per 7-cell cavity
ERL injector: 12 MeV SRF linac, 100 mA without energy recovery, >100 kW RF power per cavity
Beam Parameter | Injector Linac | Main Linac
CW beam current [mA] | 100 | 2 x 100
Bunch charge [pC] | 77 | 77
Bunch length [ps] | 2 (600 µm) | 2 (600 µm)
Bunch repetition rate | 1.3 GHz | 2.6 GHz
Average HOM power / cavity [W] | 40 | 200

## Slide 6: Example: Higher-Order Modes (HOMs) in the Cornell ERL
M. Liepe June 18, 2015 Slide 6
Bunch excites EM cavity eigenmodes (Higher-Order Modes)
The ERL beam will excite 1000s of HOMs up to f >100 GHz.
Average HOM power per ERL cavity = 200 W!
-5
-4
-3
-2
-1
0
1
2
3
4
5
-30
-20
-10
0
S [mm]
wake potential W [V/pC]
0
50
100
150
200
250
10
-6
10
-4
10
-2
10
0
frequency [GHz]
normalized integral of losses
600
m
m
Loss Factor:
bunch

## Slide 7: Higher-Order Modes: The Challenge
M. Liepe June 18, 2015 Slide 7
Beam instability at high currents!
Cavity with dipole higher-order mode
Resonant Monopole Mode Excitation if fHOM=Nfbunch
Need QHOM< 1000 for resonant modes in 100 mA ERL
Note: Q without damping ~1010
Need QHOM< 103 to 104 for dipole modes in 100 mA ERL

## Slide 8: HOM Damping Schemes
M. Liepe June 18, 2015 Slide 8
Antenna / loop HOM couplers
Beamline HOM loads
Waveguide HOM dampers
RF absorbing materials

## Slide 9
Depending on the project, the HOM damping scheme must
  Efficiently handle high power up to several kW per cavity
  Provide very strong HOM suppression of monopole, dipole, quadrupole modes with Q=100 - 10,000
  Be broadband (up to >100 GHz)
  Be inexpensive / require little beam line length
Fortunately, usually not all of these are required at the same time
Different requirements  different solutions
HOM Damping
M. Liepe June 18, 2015 Slide 9

## Slide 10: High Current Injector SRF Main Challenge: High beam loading
M. Liepe June 18, 2015 Slide 10

## Slide 11: Cornell ERL HOM Damping Solution
M. Liepe June 18, 2015 Slide 11
HOM Power
80 K
Cavity at 1.8 K
Beam tube diameter optimized
  to trap accelerating mode in cavity and
  to propagate all monopole and dipole HOMs
RF absorbers in the beam pipes between the cavities
  Simple HOM damping design
  Broadband way of HOM damping
80 K

## Slide 12: Cornell’s HOM Beamline Absorber (I)
M. Liepe June 18, 2015 Slide 12
Flange to cavity
RF absorbing tiles
80K cooling channel
SiC absorber ring
Extensive research program to find absorber materials which
  are effective at 80 K,
  absorb over the required wide frequency range (1 GHz to >100 GHz),
  are vacuum compatible and radiation hard.
Ferrites, graphite loaded SiC, carbon-nanotube loaded ceramics…
Graphene-containing compositions

## Slide 13: Cornell’s HOM Beamline Absorber (II)
M. Liepe June 18, 2015 Slide 13
Broadband (<1 GHz to >50 GHz) SiC absorber ring
Full-circumference heat sink to allow >500W dissipation @ 40K
Includes shielded bellow sections
Flanges allow easy cleaning
Zero-impedance beamline flanges

## Slide 14: Cornell 100 mA ERL Injector Cryomodule
M. Liepe June 18, 2015 Slide 14
RF cavity
Inside He vessel
HOM absorber
 Damp unwanted Higher-Order Modes
Frequency tuner
 Adjust cavity frequency
Input Coupler
 Couple RF power into cavity
Cryogenic system
 Bring cavity to 2K
~5 m

## Slide 15: Pushing the Envelope in Many Ways
M. Liepe June 18, 2015 Slide 15
2K
5K
80K
300K
Coax
-
transition
2K
5K
80K
300K
-
waveguide
transition
piezo
SRF cavity: design for high beam current
RF input coupler: design for high power (50 kW)
HOM damper: design for strong HOM suppression
Frequency tuner: stabilize cavity length on nm scale
Module design: support high cryo loads and provide excellent alignment

## Slide 16: Module Assembly
M. Liepe June 18, 2015 Slide 16
1100 aluminum
80K shield
2K 2
-
phase pipe
Cold mass assembly
-
5K manifold
Beam Line in Clean Room

## Slide 17: High Current ERL Injector Prototype
M. Liepe June 18, 2015 Slide 17
SRF cryomodule
Photocathode DC gun
Diagnostic beam line
0.5 MW RF power

## Slide 18: Cornell ERL Injector Performance
M. Liepe June 18, 2015 Slide 18
photocathode
DC gun
buncher
cryomodule
beam dump
experimental beam lines
deflector
design parameters
Nominal bunch charge 77 pC
Bunch repetition rate 1.3 GHz
Beam power up to 550 kW
SC linac beam energy gain 5 to 15 MeV
Bunch length 0.6 mm (rms)
Beam current 100 mA at 5 MeV
33 mA at 15 MeV
Achieved so far
77 pC
50 MHz and 1.3 GHz
260 kW
5 to 15 MeV
0.6 mm
75 mA
World record for CW injector
Notes: 90% normalized transverse emittances for 19 (77) pC=bunch were 0.23 (0.51) um in the horizontal plane, and 0.14 (0.29) um in the vertical plane,

## Slide 19: Does it work? Results from the Injector SRF Module
M. Liepe June 18, 2015 Slide 19
Frequency [GHz]
1.5
2
2.5
3
3.5
4
-140
-120
-100
-80
-60
S21 [dB]
HOM absorber performance
Accelerated beam currents of up to 75 mA over many hours
No signs of beam instability or excessive heating by HOMs
Spectrum in good agreement with simulation results
Excellent damping with typical Qs of a few 1000
High beam current operation
HOM spectrum

## Slide 20: HZB 100 mA ERL Injector SRF (I)
M. Liepe June 18, 2015 Slide 20
Courtesy: J. Knobloch, ERL15

## Slide 21: HZB 100 mA ERL Injector SRF (II)
M. Liepe June 18, 2015 Slide 21
Courtesy: J. Knobloch, ERL15

## Slide 22: KEK 100 mA ERL Injector SRF
M. Liepe June 18, 2015 Slide 22
Three 2-cell cavities with HOM couplers
Conditioned up to Eacc=8 MV/m (CW); limited by heating-up of HOM couplers
So far, low current operation (<1mA)
Input Coupler
HOM Coupler &
RF Feedthrough
2-cell Cavity
Cryostat
e-
RF frequency: 1.3 GHz
Input power :
10kW/coupler (10mA, 5MeV)
180kW/coupler (100mA, 10MeV)
Eacc: 7.6MV/m（5MeV）
15MV/m (10MeV)
Unloaded-Q: Q0 > 11010
Courtesy: Hiroshi Sakai, ERL15

## Slide 23: ERL High Current Main Linac SRF
M. Liepe June 18, 2015 Slide 23

## Slide 24: Cornell ERL Main Linac Cryomodule
M. Liepe June 18, 2015 Slide 24
HGRP support post
Beamline HOM absorber
Helium Gas Return Pipe
~40K thermal shield
SC magnet
~10 m
7-cell cavity

## Slide 25: Main Linac Cavity Design for very high Beam Currents
M. Liepe June 18, 2015 Slide 25
Dipole mode damping calculated up to 10 GHz with realistic RF absorbers
Worst mode limits beam current!
Franklin Cray XT4
Cell shape optimization
  ~20 free parameters
  1000’s of eigenmodes
  Impact of cell shape errors
    Supports beam current >400 mA (previous record: 10 mA)

## Slide 26: Main Linac Cavity Design: Beam Tracking Results
M. Liepe June 18, 2015 Slide 26
Maximum stable beam current (simulation) vs. cavity to cavity HOM frequency variation due to cavity shape errors
±0.125 mm
±0.250 mm
±0.500 mm
±1.000 mm

## Slide 27: Prototype Cavity Fabrication
M. Liepe June 18, 2015 Slide 27
Quality control: CMM and frequency check
Electron Beam Welding
Finished main linac cavity with very tight (±0.25 mm) shape precision  important for supporting high currents (avoid risk of trapped HOMs!)

## Slide 28: Full System Test of a 1-Cavity Main Linac Unit in a Cryomodule
M. Liepe June 18, 2015 Slide 28
cavity
HOM load
HOM load
HGRP
80K shield
Gate valve
First full main linac system test
  1st test: cavity and tuner only
  2nd test: add high power RF input coupler
  3rd test: add HOM beamline loads
Test cryomodule installed at Wilson Lab

## Slide 29: Does it work? Results from the Main Linac 1-Cavity Prototype Module (I)
M. Liepe June 18, 2015 Slide 29
Detailed HOM spectra measurements confirmed strong damping (QHOM<104 for dipole modes)
Good agreement with 3D damping simulations
Record Q0 for cavity accelerating mode:
  Q(2.0 K) = 3.5 x 1010
  Q(1.8 K) = 6 x 1010 (3 x spec!)
  Q(1.6 K) = 1 x 1011
1.6K
1.8K
2K

## Slide 30: Does it work? Results from the Main Linac 1-Cavity Prototype Module (II)
M. Liepe June 18, 2015 Slide 30
HTC-2: No HOM Absorbers
HTC-3: With HOM Absorbers
Beamline HOM absorbers strongly damp dipole HOMs to under Q ~ 104
5K intercept
40 to 80K intercept
SiC absorber ring
Shielded bellow
Flange for disassembly
Flange to cavity
Notes: I lead Nb3Sn program !

## Slide 31: Does it work? Results from the Main Linac 1-Cavity Prototype Module (III)
M. Liepe June 18, 2015 Slide 31
Beam direction
Charge-modulated beam
BPM2
BPM1
BPM3
Beam operation:
  High currents >40 mA
  No significant heating from HOMs
  No sign of beam instability or weakly damped modes

## Slide 32: HZB 300 mA BESSY VSR SRF
M. Liepe June 18, 2015 Slide 32
Courtesy: J. Knobloch, ERL15
Notes: I lead Nb3Sn program !

## Slide 33: HZB 100 mA ERL Main Linac SRF
M. Liepe June 18, 2015 Slide 33
Courtesy: J. Knobloch, ERL15
Notes: I lead Nb3Sn program !

## Slide 34: KEK 100 mA ERL Main Linac SRF
M. Liepe June 18, 2015 Slide 34
Input couplers
Cryostat
Tuner
HOM absorber
Two 9-cell SC cavities
RF frequency: 1.3 GHz
Input power : 20kW CW (SW)
Eacc: 15 MV/m（design）
Unloaded-Q: Q0 > 11010
Courtesy: Hiroshi Sakai, ERL15
2014.Feb—Mar.
2012.Dec.
Operation
voltage
Fatal Q decrease potentially due to crack of Hom damper was observed
Decrease Q0
during operation
Ferrite based beamline HOM damped (for 100mA operation)
So far only operated at low beam currents (<1mA)
Notes: I lead Nb3Sn program !

## Slide 35: BNL ERL Main Linac SRF (I)
M. Liepe June 18, 2015 Slide 35
Courtesy: Wencan Xu, ERL15
704 MHz BNL1 cavity for R&D ERL
704 MHz BNL3 cavity for conventional lattice ERL eRHIC
High current ERL based (3.5 nC, 50 mA 6-pass ) => Heavy damped HOM
7.3 kW per average HOM power/cavity
Notes: I lead Nb3Sn program !

## Slide 36: BNL ERL Main Linac SRF (II)
M. Liepe June 18, 2015 Slide 36
Courtesy: Wencan Xu, ERL15
422 MHz BNL4 cavity for FFAG lattice ERL eRHIC (18 mA 16-pass ERL)
6 coaxial-line HOM couplers on the cavity for low frequency HOMs: ~ 5.6 kW
3 rectangular waveguide HOM dampers on the beamline taper for high frequency HOMs: ~2.2 kW
Notes: I lead Nb3Sn program !

## Slide 37: JLAB High Current Cavity Work
M. Liepe June 18, 2015 Slide 37
748.5 MHz High Current Cavity
Courtesy: Bob Rimmer
Notes: I lead Nb3Sn program !

## Slide 38: Conclusions
M. Liepe June 18, 2015 Slide 38

## Slide 39: Conclusions
Injector (non ERL) high current SRF:
  Several 100 mA+ designs (Cornell, HZB, KEK…)
  Cornell injector has reached >70 mA with no sign of limitation by SRF
  Future: need higher power CWRF couplers (especially at f >1 GHz) to reduce cost
ERL main linac high current SRF:
  Several 100 mA+ designs (BNL, Cornell, HZB, JLAB…)
  Cornell 7-cell cavity has been tested at ~40mA in 1-pass (non ERL) operation with no sign of beam instability or excessive HOM power
  Non of these cavities ever have been operated in high current (~100mA) ERL mode!!
    Test facilities: CBETA, HZB, KEK…
M. Liepe June 18, 2015 Slide 39
Notes: I lead Nb3Sn program !

## Slide 40: Thank you for your attention!