## Slide 1: Operational Experience With CW SRF ERLs D. Douglas
Authored by Jefferson Science Associates, LLC under Contract No. DE-AC05-06OR23177 with the U.S. Department of Energy.

## Slide 2: This Sermon’s 3 Points
Energy recovery is a robust cost control measure:
  ERLs give bright beams at optimum cost
ERLs are really just fancy time of flight spectrometers
  They exist to create specific time/energy correlations
Consequence*: system architecture driven by evolution of energy/phase dynamics (longitudinal match)
*(sermons are, after all, about consequences…)

## Slide 3
ERLs are non-equilbrium systems
  no natural emittance (cf. storage rings);
  no closed orbit (really... there is no closed orbit…);
  inherent betatron/synchrotron stability may be unnecessary;
  beam and the lattice are different (sometimes deliberately…)
Consequence: an ERL is more similar to a storage ring injection chain than it is to the ring itself… (and recall, to our collective sorrow, that injection is when all the loss occurs… and notice that an ERL is a continuous, 100% duty cycle injector…!)

## Slide 4: But first, a quick overview…

## Slide 5: What are Energy Recovering Linacs? Compare to conventional accelerators…
Rings
  Recycle each accelerated particle an infinite number of times – adding a bit of energy each time
  High beam powers for modest input power: efficient acceleration
    MW of RF + MW DC  GW beam power (e.g., 0.5 A @ 2 GeV)
  Circulation of beam  radiation excitation  inherently limited beam quality
Linacs
  Accelerate each particle rapidly in a multiple RF structures
  Beam power inherently less than power required for acceleration (wall losses): inefficient acceleration
    MW of RF + MW of DC  MW beam power (e.g., 50 A @ 20 GeV)
  BUT… Beam is not in machine long enough for quality to degrade: performance is source limited

## Slide 6: Linac Cost/Performance Optimization: Recirculation and SRF
Linacs provide great beam quality, so its worthwhile to try to make them more cost effective
To control cost & improve performance, linac builders utilize certain “slight of hand” tricks
Recirculation : “reuse” accelerating structure, reducing linac size and hence cost
  Transport beam from end of linac & reinject in phase with the RF fields for further acceleration
Superconducting RF : avoids wall losses
  Allows high gradient CW operation
  Dramatically reduces required RF power (enough to offset cost of cryogenic plant and additional RF system complexity)
  Significantly improves beam quality
Notes: Linacs give such good quality beam, it has been worthwhile to try to make them more cost effective…
You might argue that using SRF simply shifts cost of machine from installed RF power to cost of cryogenic plant and

## Slide 7: Machine Topologies
RF Installation
Beam injector and dump
Beamline
Linac
Ring
Recirculating
Linac
Notes: Multiple recirculations allows reuse of accelerating cavities – makes acceleration more efficient while requiring little additional bending, and imposing little additional constraint on beam quality…

## Slide 8: Whence ERLs?
Use of recirculation reduces cost
  Beamline inexpensive relative to RF
Proper system design avoids instabilities, beam quality degradation
RF power still a problem:
  CEBAF: 200 mA x 4 GeV = 0.8 MW
    manageable (affordable)
  Light source 100 mA x 5 GeV = ½ GW
    needs dedicated nuclear power plant...
    and… what do you do with a GW of waste electrons?

## Slide 9: The Next Step: Energy Recovery
So, “consider a circular linac”… or at least a recirculated linac
To accelerate turn-to-turn, beam bunches must be synchronous with RF. Pass-to-pass phase is important!
You might wonder what will happen if you reinject the beam out of phase with the accelerating field, rather than in phase…
Subsequent pass is decelerated – the beam power is deposited back into the RF system…
and can be used to accelerate later bunches – replacing significant amounts of RF power (and cost)!
Linac energy gain
time

## Slide 10: Historical Overview
Jlab has built and operated five of the world’s six CW SRF ERLs:
  FET recirculation test – ca. 1991
    BBU validation for CEBAF
  IR Demo FEL Driver – 1997-2001
    1 kW CW IR FEL demonstration (2.1 kW achieved)
  CEBAF-ER – 2003
    GeV-scale ERL test
  IR Upgrade FEL Driver – 2003-present
    10 kW IR FEL scale-up test (14.3 kW achieved)
  UV Demo FEL Driver ERL – 2009-present
    “high” power CW UV FEL wavelength scaling validation test (100+ W CW)
~15,000 hours beam time/20 CY operational experience
Current (mA)

## Slide 11
DC Gun
SRF Linac
UV FEL Transport Line
Dump
IR Wiggler
Bunching Chicane
THz Line
IR/UV ERL Architecture
DC photocathode gun (350 keV)
9 MeV booster
Penner bend merger
3 cryomodule linac
Bates bend arcs
compression in chicane for IR;
arc/bypass for UV (“chicaneless”)
nonlinear compaction management &
  RF curvature compensation; energy compression during recovery
Issues
Drive laser
Gun
SRF performance/damage
Magnet field quality (time-of-flight
spectrometer);susceptibility to
small errors
DC power/field reproducibility

## Slide 12: ERL Parameters (Achieved)
Parameter | IR | UV
Energy (MeV) | 88-165 | 135
Iave (mA) | 9.1 | 2 (mirror limited)
Qbunch (pC) | 135 (270) | 60
eN transverse/longitudinal (mm-mrad/keV-psec) | 8/75 | 5/50
sdp/p, sl (fsec) | 0.4%, 150 | 0.4%, 100
Ipeak (A) | 400 | 250
FEL repetition rate (MHz) (cavity fundamental 4.6875) | 0.586-75 | 1.172-18.75
hFEL | 2.5% | 0.8%
(DE/E) full after FEL | ~15% | ~7%

## Slide 13: Top 10 Lessons Learned
Beam quality preservation: performance is source-limited – “as good as it gets…” (Liouville) => conservative design
  “bad” things at high energy (power extraction, beam-beam, beam-target, SR, etc, etc…) adiabatically anti-damp to limit performance at back end
  however…. “better is the enemy of good enough”: best injected emittance may not give best delivered emittance… (more rapid degradation in front end)
FET/Demo/CEBAF-ER=> longitudinal match constrains architecture
ERLs are time-of-flight spectrometers (create phase/energy correlations), not transport systems
  nonequilbrium systems
  no closed orbit; may not be betatron stable/have “matched” beam envelopes
  beam and lattice are different (mismatch often advantageous)
  spectrometer-grade components
  aberration management critical: nonlinear modeling/control needed
    e.g – octupoles in longitudinal match – need nonlinear control, but don’t need harmonic RF…
RF drive/transient management
  high Qext can require more power than low Qext …
What has been is what will be, and what has been done is what will be done; there is nothing new under the sun.
Ecclesiastes 1:9 NRSV

## Slide 14
  Hardware very robust, but… need to provide significant margin
  flexible system design allows ops despite abuse (3 of 4 modules damaged)
  performance can degrade over time
High power beam ⇒ power-flow management (i.e., “don’t lose beam or excite wakes”…)
  high duty cycle/CW a game-changer; worse as bunch charge increases
  CW operation equivalent to operating a ring injection chain with 99.999% efficiency
  Halo & collective effects…
Design robustness (redundancy, reliability) and flexibility
  needed major retrofits (THz chicane, phase space exchange)/had to run machine far from design operating point (lower energy) to achieve goals
  encounter “new” effects (LSC, resistive wall, THz heating, RF heating…)
Beam loss in CW ERLs is not like that in storage rings, its equivalent to loss in a storage ring injector chain
  high power ⇒ 99.999% capture efficiency – keep losses < 0.001%
  halo – major operational impediment
Collective effects in an inherently high-brightness system
  had to manage BBU (completely stabilized)
It’s always the drive laser…
  subtleties of CW synchronization/control amongst various different types of RF systems (esp. vendor issues)
courtesy C. Tennant

## Slide 15: Influence of Longitudinal Match
ERL=time of flight spectrometer => performance sensitive to longitudinal dynamics
Can switch between quite different operational modes with only minor parametric changes
  e.g. cross-phasing of linac modules: change single phase setpoint and go from short bunch to small dp/p
Allows management/control/improvement of beam quality (and degradation) in presence of collective effects, coherent phenomena, ...
  Examples:
    LSC management, bunch length compression during acceleration/transport; energy compression during energy recovery
    UV bunch compression w/o chicane
    RF curvature correction w/o harmonic RF
    Bunch length compression with positive compaction (M56>0)
    Suppression of RF curvature effects  reduction in dp/p (cf. to on-crest/in trough operation)
      Can run with longer bunch/mitigate LSC effects
    Enhancement/suppression of LSC/CSR/mBI
E (MeV)
t (nsec)
E (MeV)
t (nsec)

## Slide 16
Courtesy C. Tennant

## Slide 17: Longitudinal Matching Scenario
DC Gun
SRF Linac
Dump
IR Wiggler
Bunching Chicane
Requirements on phase space:
high peak current (short bunch) at FEL
  bunch length compression at wiggler
  using quads and sextupoles to adjust compactions
“small” energy spread at dump
  energy compress while energy recovering
  “short” RF wavelength/long bunch,
  large exhaust dp/p (~10%)
  get slope, curvature, and torsion right
  (quads, sextupoles, octupoles – no
  harmonic RF…)
E
f
E
f
E
f
E
f
E
f
E
f

## Slide 18: JLab IR Demo Dump
core of beam off center, even though BLMs showed
edges were centered
(high energy tail)

## Slide 19: Halo – a dominant CW performance issue
“Real beams do not occur in distributions named after dead European mathematicians” (P. O’Shea).
  typically multi-component (transversely and longitudinally)
  Makes betatron matching tricky (match phase space volumes to phase space volumes, not beam spots to beam spots)
“Halo” = large emittance, low intensity component(s) of beam
  mismatched to core
  sample large amplitudes
  can be tightly focused (but with large divergence)
  “stuff” that’s too dim to see with standard diagnostics (down by ~3+ orders of magnitude in density), but has enough power to burn things up
“Ns” not a good measure of required aperture
50 mm
6 mm
6s
Calibration: see losses from “10 mm-mrad” beam… at points with 5600 mm-mrad acceptance
Notes: Point out on this slide that ERLs are nonequilibrium systems – and thus much more like injection chains (and linacs) than rings – at least in terms of halo/scraping/activation. Compare fractional losses during injection (10s of % - due to low duty cycle) to what is tolerable in a high power ERL (0.001% or less)…

## Slide 20: Halo Experience
Sources of halo:
  stray light on cathode field emission
  dynamics of bunch formation dark current (primary source
  and evolution of background)
  …
We’ve seen
  Halo on beam in injector (measured/modeled – P. Evtushenko)
  CW beamlets at ~40-50 MeV, 110 MeV, ... (drive laser shutter closed)
  Loss at aperture constraints,
  High radiation background around machine (RF on, beam off)
Can map out halo patterns:
  Beam and lattice are different:
    lattice defines what happens to beam
    beam doesn’t a priori match lattice
  Halo almost always mismatched
  Assess where “big amplitude” stuff goes (e.g. by mapping out envelope of all correctors)
    Results match surveys/observed loss pretty well
Courtesy P. Evtushenko

## Slide 21: Halo
dark current
wiggler aperture
small bore module
beam dump
reinjection match

## Slide 22: Halo Management
Can control halo – to some extent
  Use mismatch to adjust halo envelopes at aperture constraints
    Find quad where halo large, core beam small;
    adjust “halo” knob, reduce halo size at aperture (vary phase advance);
    use BLMs as diagnostic
Need to have flexible transport system design…
Controls loss at wigglers and during “DarkLight” test
  Internal target validation run
  450 kW (4.5 mA CW at 100 MeV) through 2 mm aperture for 8 hrs; 6 ppm loss
Method becomes problematic when aperture is constrained over significant phase advance… halo envelopes ring…
“Quantitative/deterministic” control – will need large (106) dynamic range diagnostics, tomography, …
  P. Evtushenko (105 range achieved during DarkLight run)
“You can’t collimate electrons, you can only make ‘em mad…” (G. Neil)

## Slide 23: Halo-Related Issues We Didn’t Have
Intrabeam/beam-gas scattering
  No obvious evidence of beam-gas, IBS, Touschek, but…
  Beam brightness is modest (5-10 mm-mrad x 50 keV-psec at 135 pC)
Ions
  Estimates range from “no effect” to “fatal”
  No obvious evidence of ion accumulation, however…
  Beam current is modest (10 mA)

## Slide 24: RF Transient Effects
Beam off/on
  transient beam loading
  cavities detune
FEL off/on
  energy transients
  reinjection phase transient
  transient beam loading
  cavities detune
Need adequate RF control & power to avoid tripping
  Specs/methods depend on details of cavity design and operational modes
  Details can be counterintuitive
    Example – low Qext can sometimes require less power than high Qext

## Slide 25: ERL Magnet Field Quality Requirements
ERLs: time-of-flight spectrometers  differential B errors a problem:
DB  dx’= DBl/Br = (DB/B) qdipole
dx’  dl = M52 dx’
dl  DEdump = Elinac sin f0 (2p dl/lRF)
= Elinac sin f0 (2p M52(DB/B)qdipole/lRF)
  Tolerance DB/B needed for specific acceptance DEdump tighter for higher Elinac , shorter lRF , larger dispersion (M52 = M22M16 – M12M26)
  JLab numbers: DEdump ~ 3400 MeV * (DB/B)
    (observed at JLab… DB/B ~ 10-4  few 100s of keV at dump)
DB  dx’=DBl/Br~DBl/(33.3564 kg-m/GeV * Elinac)  dl=M52 dx’
dl  DEdump = sin f0 (2p M52(DBl/33.3564 kg-m)/lRF)
  Tolerable absolute “error integral” DBl is set by dump acceptance; is independent of linac length/energy gain; tolerable relative field error falls as energy (required field) goes up

## Slide 26: Dealing With Field Quality…
Palliative measures:
  make better magnets
  use lower energy linac
  reduce M52 (smaller dispersion, stronger focusing)
  provide means of compensation (diagnostics & correction knobs)

## Slide 27: Collective Effects: Inherent in High-brightness Systems
Collective contributions to halo
  dynamics of beam formation, Touschek/intrabeam scattering, …
  [you can’t collimate electrons, you can only make ‘em mad…],
wakes, impedances, interaction of beam with itself &/or environment
  BBU, CSR, LSC, mBI…
Space charge ->100+ MeV; “injector stretches from cathode to FEL”… and back to dump…
  losses can be worse at lower charge than at higher (e.g. 30 pC worse at dump than 135 pc due to loss of space charge focusing)
  dominates dynamics/performance down linac
THz, resistive wall, RF heating… all performance issues in IR Upgrade

## Slide 28: CSR Management During Recirculation & Compression
IR Upgrade generated high power THz (135 pC x 150 fsec)
  Observed extraction efficiency ~0.2% => ~2+ kW at full current
  Went unexpected places (e.g. FEL outcoupler…)
  Must learn to control/optimize
Impact of CSR on beam quality a serious concern during both recirculation and compression
Impact of high power THz on hardware a serious concern for high brightness systems

## Slide 29: CSR Solutions
Recirculate with periodically isochronous 2nd order achromats
  Emittance-compensates transverse effects up to fairly high charge/peak current
    Leaves imprint of wake longitudinally
  Suppresses microbunching
Compress with M56>0
  Avoids parasitic compressions; can suppress microbunching
  Lases like gangbusters… (UV Demo, April 2012)
“Optics balanced” emittance compensated compressor

## Slide 30: Implications for Diagnostics
What does this experience imply about diagnostic requirements (a topic for a very long discussion…)?
Need lots of longitudinal/time of flight/bunch length/energy diagnostics
  longitudinal matching, correction of field errors
Must measure positions of multiple beams in common transport in an operationally noninvasive manner
  beams out of phase: signals cancel in resonant structures like those used for some diagnostics
Must diagnose lattice and beam separately

## Slide 31: Other Lessons, Fear, and Loathing
Internal target operation
  Gas jet aperture validation (450 kW CW through 2 mm aperture with few ppm loss)
    Small spot + halo control via choice of phase advance
  Isotope production
    Tricky: momentum spread not unlike FEL; transverse spray difficult to manage due to adiabatic antidamping during recovery
      has implications for beam-beam if operating in the disruption regime
      want large divergence => small spot; good for collider (NP, HEP) bad for solid target…
Costing: optimum may not lie in clone/copying
  T. Powers/ILC cost workbook
ISR effects on longitudinal emittance (esp. at higher energy)
  Bunch lengthening (M56emission->reinjection not zero everywhere) + sdp/p => entertainment (as with magnetic field quality)…
High power FELs from ‘80s on serve as cautionary tale: use caution during scale-up

## Slide 32: and one more thing…
Common transport (two passes in one beam line) can be tricky (and risky).
  Done at MIT/Bates (3 pass – one up, one coast, one down), IR Demo (same scheme), and CEBAF-ER
  Limits flexibility and control; forces tighter specs (expensive); worse sensitivity
May be easier to use asymmetric gains in linacs & have separate transport of each pass on each end (GERBAL)
  Better control of beam envelopes in multipass operation
    “short” linac => “preaccelerator” to “long” linac
  More “knobs”
  Can deal with slight mismatches of energy pass-to-pass (reduced aperture requirements)
  Relaxed energy gain matching on linacs (if S/R acceptance adequate)
  Separates each pass for feedback stabilization

## Slide 33: Acknowledgments
Many thanks to the organizers for the opportunity to participate in this discussion!
My JLab colleagues have all contributed to the work on which this talk is based; specific information, ideas, and/or slides were provided by
  Pavel Evtushenko – George Neil
  Chris Tennant – Steve Benson
  Tom Powers – Jim Boyce
  Bob Legg – Gwyn Williams
  Carlos Hernandez-Garcia – Fay Hannon
  Shukui Zhang
Notice: Authored by Jefferson Science Associates, LLC under U.S. DOE Contract No. DE-AC05-06OR23177 and by the Southeastern Universities Research Association, Inc. under U.S. DOE Contract No. DE-AC05-84ER40150. The U.S. Government retains a non-exclusive, paid-up, irrevocable, world-wide license to publish or reproduce this manuscript for U.S. Government purposes.

## Slide 34: Backups

## Slide 35: JLab FEL bunch compression and diagnostics
Sextupoles
(B’dL) 10730 G
Sextupoles
(B’dL) 12730 G
Sextupoles
(B’dL) 8730 G
Trim quads
(B’dL) 700 G
Trim quads
(B’dL) 740 G
Trim quads
(B’dL) 660 G
JLab IR/UV Upgrade FEL operates with bunch compression ratio of 90-135 (cathode to wiggler); 17-25 (LINAC entrance to wiggler).
To achieve this compression ratio nonlinear compression is used – compensating for LINAC RF curvature (up to 2nd order).
The RF curvature compensation is made with multipoles installed in dispersive locations of 180° Bates bend with separate function magnets - no harmonic RF
Operationally longitudinal match relies on:
a. Bunch length measurements at full compression (Martin-Puplett Interferometer)
b. Longitudinal transfer function measurements R55, T555, U5555
c. Energy spread measurements in injector and exit of the LINAC
Martin-Puplett Interferometer data
in frequency domain – give upper limit on the RMS bunch length
Courtesy Pavel Evtushenko

## Slide 37: RF Transient Effects
Beam off/on
  transient beam loading
  cavities detune
FEL off/on
  energy transients
  reinjection phase transient
  transient beam loading
  cavities detune
Need adequate RF control & power to avoid tripping
  Specs/methods depend on details of cavity design and operational modes

## Slide 38: PREDICTED AND MEASURED FORWARD POWER/RF DRIVE PHASE IN AN ERL
The solid lines indicate the predicted values based on:
  QL = 2 x 107
  E = 5.6 MV/m.
  Δf = 10 Hz
Test Process:
  Tune the cavity with no current.
  Disable the mechanical tuners.
  Ramp the current up and record the forward power and phase.
  Repeat with Tuners enabled.