## Slide 1: BNL’s High-Current Program
Dmitry Kayran
Cornell University, June 17-19, 2015
Collider-Accelerator Department,
Brookhaven National Laboratory
INTENSE ELECTRON BEAMS WORKSHOP

## Slide 2: BNL high current program
High Average current R&D ERL
Polarized high current Gatling Gun
Low energy RHIC electron cooler (LEReC)
Coherent electron cooler for high energy ion/proton beams (proof of principal experiment)
Gatling Gun
Coherent electron cooling

## Slide 3
R&D ERL

## Slide 4: R&D ERL will serve as a test-bed for future RHIC projects
Test concepts relevant for electron-ion colliders and high-energy electron cooling (coherent and conventional)
  High average current
  SRF injector
  BBU
  e-dump
  Stability criteria for CW beam current
  Halo/losses control
Specifically for e-cooler
  High charge per bunch
  Low energy spread and emittances (3rd harmonic is needed)
  Conservation of beam parameter in merger at low energy (Z-bend test will give an answer)
  Ion bunch much longer then electron one (could use 703.75 MHz train of e-bunches, will split laser beam to 2, 4 or 8)
D. Kayran, IEBW’15 Cornell University

## Slide 5: BNL ERL layout. ~20m circumference
SRF Gun
with photocathode
SRF 5cell linac
Returning loop
Beam dump
Injection line
~7m straight section

## Slide 6: 704 MHz SRF Gun: 2 MV CW operation
1-2 MV CW operation of 704 MHZ SRF gun at BNL
SRF gun before installation into the crymodule. March 2011
Gun voltage
Beam line vacuum
Radiation inside
½ cell SRF gun
1MW CW Klystron
Dummy load
D. Kayran, ERL2015

## Slide 7: Laser system
Lumera Laser:
Commissioned and operational since 2009
Pulse Selector Performance
D. Kayran, IEBW’15 Cornell University

## Slide 8
8
Laser pulses manipulation
Sharma et al PRSTAB 2009
Tomizawa et al Quant Elec 2007
Birefringent Method
Interferometric Method
No adjustable parameters
Crystal length and quality issues
Extremely sensitive to alignment
Stability
Used to increase pulse width by 4, 8 and pulse flat.
Used to increase to increase rep. rate by 4. (to 4*9.38MHz)
Tested with e-beam
Ready to test with e-beam
D. Kayran, IEBW’15 Cornell University

## Slide 9
We find that by adopting a duty cycle of ~1:15 (on:off), we can safely turn the cavity up to an accelerating gradient of 18 MV/m. We demonstrated continuous running for 30 minutes with a pulse length of
2 seconds, and an off time of 30 seconds. During the “off” phase, the gradient is held at 3 MV/m. The longest pulse achieved before quenching was 5 seconds..
In cry module horizontal test results 2010.

## Slide 12: Gun to FC beam test setup
Inj. Dipole
ICT
Faraday Cup
BPM
Gate Valve
Laser cross
Halo monitors
Slit mask
Cavity
Cathode transport cart
Cathode
XY corrector
Solenoid
Profile monitor
Laser beam
D. Kayran, IEBW’15 Cornell University

## Slide 13: Goals of Gun to Dump commissioning stages (ARR stage I)
  Injection line commissioning (low current)
      transport beam through the ERL injection line (ZigZag)
      calibrate beam loss monitors
      establish routine and fault dose rates external to the shielding
  Extraction and beam dump commissioning (low current)
      transport beam through 5cell cavity and the ERL extraction line to beam dump
      calibrate beam loss monitors and DCCTs
      establish close to 100% beam to dump transport line propagation
      carry out beam measurements
      establish routine and fault dose rates external to the shielding
  High Intensity Studies (final stage)
      demonstrate stable gun operation at minimum 30 mA average current
      conduct cathode life time studies
      beam dump commissioning
      establish routine dose rates external to the shielding
Learning the machine performance during previous commissioning phases allows proceeding with smooth transition to loop commissioning.
D. Kayran, ERL2015

## Slide 14: R&D ERL full commissioning ARR-II
Laser
Commissioning goal:
Injection energy: 2 MeV
Top energy: 20 MeV
Multi-Alkali photocathode : QE>3e-3
Laser repetition rate: 9.4 MHz (40 MHz)
Operating: single or/and train pulses
Charge per bunch: 1 nC
Average current : 30 mA
ASE limits (controlled by design)
Max SRF Gun Energy <3.5 MeV
Power source for SRF < 1.5 MW
Max loop electron energy <25 MeV
Maximum Reactive Power: < 10MW
Power source for 5cell cavity < 60 kW
Extraction Beam energy <3.5 MeV
Extraction beam power < 1.5 MW
60 kW RF Amplifier
1MW RF Amplifier (klystron)
Beam Parameters
D. Kayran, IEBW Cornell 2015

## Slide 15
First beam, old cathode Nov 2014.
Set up
Laser: 6.1 Watt, green,
Pulse structure 7 μsec, every 500 μsec; 9.38MHz rep rate.
RF: 1.2 MV, 500 ms;
Beam:
  bunch charge: 7.7 pC,
  Average per RF pulse
  photocurrent 1 μA, dark current 38 nA;
Photocathode cold QE=2.7e-5 Very low!!!
Laser shutter open
Beam image at YAG screen
Faraday cup signal (1MΩ termination)
Laser shutter closed
D. Kayran, IEBW’15 Cornell University

## Slide 16: New cathode stalk with Ta tip
Courtesy Wencan Xu, more details on Tuesday, WG1+WG4 joint session.
D. Kayran, IEBW’15 Cornell University

## Slide 17: Conditioning Gun with new cathode stalk.
Vacuum signal
Gun voltage
Radiation inside
Klystron power
1.25MV CW
Good vacuum,
No radiation
Conditioning~4 hours
D. Kayran, IEBW’15 Cornell University

## Slide 18: QE with new Ta cathode
ERL Cathode deposition system at BLD912
~4% QE measured at room temperature
We tested 3.8% QE K2CsSb cathode in the 704MHz SRF gun.
The cathode survives well the gun and stalk RF conditioning.
The cathode QE inside the gun (cold) is 1%. We didn’t see any QE degradation after two days of high bunch charge operation. The vacuum at the gun exit is at 10-9 scale during gun operation.
After extracting the cathode out of the gun, the QE is still at 3.8%.
Dark current
Photo current
Courtesy Erdong Wang,
Peak current 1.65A, Gradient 10 MV/m
Schottky effect
D. Kayran, IEBW’15 Cornell University

## Slide 19: Laser pulses matching RF pulse structure and ICT for startt up test
Raw signal
Integrated signal
…….
……….
RF: adjustable pulse length
ICT window
charge measurement
7 μsec
Laser pulse
9.38 MHz
100 nsec
3-10 msec
500 μsec
1 sec
D. Kayran, IEBW’15 Cornell University
Bunch train
Bunch car
Bunch:
8.5 psec
22 psec
Notes: LUMERA: Nd: YVO4
Wavelength: 532nm
Power: up to 10 W
Pulse duration: ~ 8.5 ps

## Slide 20
Beam commissioning with new cathode June 2015.
Set up
Laser: 0.044 mWatt, green,
Pulse structure 5 μsec, every 500 μsec; 9.38MHz rep rate.
RF: 0.65 MV, 3 ms;
eBeam:
  charge per macro bunch 0.8nC/47bunches=17pC
  dark current 4 μ A;
Photocathode cold QE=1e-2 very Good!!!
Laser shutter open
Faraday cup signal (1MΩ termination)
Laser shutter closed
Increase laser spot size
D. Kayran, IEBW’15 Cornell University

## Slide 21: Beam charge measurements
DCCT
YAG crystal
Faraday Cup
Pepper pot
ICT
Beam direction
GUN
FC vs ICT. ICT signal 0.85 nC , FC signal 0.8 nC
Integrating Current Transformer
Faraday cup
D. Kayran, IEBW’15 Cornell University

## Slide 22: Charge per bunch 0.55nC
ICT signal for 9 pulses (4.4 nC> 4nC ICT saturation)
Reduce back to 2 laser pulses (1.1 nC) 0.55nC each.
2 laser pulses, 0.39uJ each
Q_ICT, nC
9 bunches,
Iav_per laser_car=5.3mA
2 bunches
Iav_per_RF_pulse 4.5uA
2 e-bunches at FC observed
D. Kayran, IEBW’15 Cornell University
Charge is enough to generate 386mA at 704MHz

## Slide 23: Solenoid scan to measure gun astigmatism (preliminary)
Ninja star shape
Axial symmetric system or not?
2 FPCs
Preliminary result focus length 64cm!!!. Required more investigation.
Courtesy V. Litvinenko
I_sol=6.7A
I_sol=7.24A
D. Kayran, IEBW’15 Cornell University

## Slide 24: Dark current and photocurrent
Dark current and photocurrent respond similar to solenoid and corrector change.
Photocurrent 0.8 nC /2 laser pulses
Dark current @ .85MV 4uA per 3 msec
D. Kayran, IEBW’15 Cornell University

## Slide 25
Try Solenoid scan, Q=133pC (preliminary)
 | Normalized emittance
full beam | 12 mm mrad
20% core | 0.25 mm mrad
Very Preliminary results
D. Kayran, IEBW’15 Cornell University
Notes: Siga: 1.4 mm

## Slide 26: BNL R&D ERL: designed parameters, progress
Parameter | Units | High current | High Charge | Measured
Energy max/inject | MeV | 20/2.5 | 20/3.0 | ?/1.2 (pulsed)
Charge per bunch | nC | 0.5 | 5 | 0.55
Average Current | mA | 350 | 50 | 0.004
RMS Bunch length | psec | 8-20 | 30 | 8.5; 22
Normalized emittance | 10-6 m | 1.4 | 5 | 20% core: 0.25 Full rms: 12
RMS energy spread, dE/E | 10-3 | 3.5 | 10 | ?
Repetition rate | MHz | 704 | 9.4 | 
Beam dump power | kW | 875 | 150 | 1e-3
Very preliminary
Laser pulse
Faraday Cup
Only gun measured
D. Kayran, IEBW’15 Cornell University

## Slide 27: R&D ERL: Installation and commissioning progress
Strategy: Start commission system by system of key components when systems and recourses are available.
Milestones : 
High power RF components installed and commissioned (2005-2007)
SRF 5‐cell installed and cold emission test completed (2009)
9.4MHz Laser system commissioned (2009)
Digital LLRF system commissioning (2012)
2 K LHe cryogenic system/refrigerator commissioned (2012)
SRF half‐cell gun cold emission test w/o cathode (2013)
Conditioning of the SRF gun with a copper cathode stalk (Jan 2014)
Beam instrumentation installed, commissioning continues.
D. Kayran, IEBW’15 Cornell University

## Slide 28: Mile stones: commissioning with beam
First beam from the SRF gun with CsK2Sb photo cathode (Nov. 2014)
DOE Approved to beam commissioning Gun to dump (Jan 2015)
New cathode conditioned (Jan 2015)
All ERL components installed, ARR for full ERL commissioning (May 2015)
First good QE cathode (May 2015)
High charge per bunch from the gun (achieved June 2015)
Future plans
Gun into beam dump commissioning (Summer 2015)
ERL beam test low current (Fall 2015)
Laser system upgrade (Fall 2015)
Gun to dump then ERL gradually increase current (until Feb 2017).
Preparing for commissioning ERL components at RHIC IP2 for Low Energy RHIC electron cooler. (Feb 2017-March 2018)
D. Kayran, IEBW’15 Cornell University

## Slide 29: R&D ERL summary
An ampere class 20 MeV superconducting Energy Recovery Linac (ERL) is presently under commissioning at BNL for testing of concepts relevant for high-energy electron cooling and electron-ion colliders.
There are two slightly different goals of ERL R&D:
  1. High charge ~1-5 nC per bunch
  2. Hundreds mA average current but moderate charge per bunch.
We may not be able to reach both simultaneously.
Our current laser system:
  without laser splitting can run 10 MHz
  with laser pulse splitting it can run 40MHz.
QE with Ta cathode tip: room temperature 4% , in gun cold 1%. No noticeable difference in QE before and after beam tests has been observed
During first new cathode stalk test.: charge .55 nC achieved, max average current per 3msec RF pulse 4.5uA .
Right now we are limited in charge per bunch because of space charge and low gradient at the cathode. (at 44mW Q=19pC at 4W 550pC).
We will increase voltage and make RF pulses longer by conditioning gun with stalk
Meanwhile our current plan will be study gun performance and try to resolve problems with unstable operation (laser, RF, timing etc).
Until we understand gun behavior it will be very difficult to run higher duty cycle.
D. Kayran, IEBW’15 Cornell University

## Slide 30
LEReC

## Slide 31: ERL for LeRHIC
Courtesy Jörg Kewisch
D. Kayran, IEBW’15 Cornell University

## Slide 32: LEReC Requirements
Energy [MeV] | Gamma | Charge per bunch [pC] | Bunches per bunch train | Beam Current [mA]
1.58 | 4.10 | 100 | 30 | 30
2.04 | 5.00 | 100 | 30 | 30
2.65 | 6.18 | 150 | 24 | 33
3.48 | 7.80 | 200 | 21 | 40
4.85 | 10.50 | 300 | 18 | 50
 | Parameters need for ultimate cooling performance
Normalized rms emittance | < 2.5e-6 m
RMS energy spread | 5e-4

## Slide 33: LEReC beam structure in cooling section Example for g= 4.1 (Eke=1.6 MeV)
110 nsec,
f=9.1 MHz
1.42 nsec
30 electron bunches
Electrons:
f_SRF=703.518MHz
Rms length=3 cm, I_peak=0.4 A
Q_e=100 pC
9 MHz RHIC RF

## Slide 34
SRF gun:
2015-2016: SRF gun commissioning w/beam with new cathode stalk.
High-current commissioning in CW mode (LEReC tests in 912).
DC gun:
May 2015 – mid 2016: DC gun construction by Cornell University.
2016: DC gun commissioning at Cornell.
Conversion of the SRF gun into the booster cavity
End of 2015: Start of cooling sections installation
2016: Start installation of electron beam transport and warm RF cavities
June 2017 – Feb.2018: Move and install SRF Gun, SRF cavity, beam dump, etc.
End of 2017-March 2018: Systems commissioning (RF, cryogenics, etc.)
April - Sept 2018: LEReC commissioning with e-beam in RHIC tunnel
October 2018: RHIC Run-19 BES-II physics program (commissioning of cooling with
Au ion beams). RHIC Run-20 BES-II program (LEReC Phase-II)
LEReC timeline
The new LEReC laser system will run 704MHz. As we demonstrate already .55 nC per laser pulse it should allow us to run 390mA as soon as it’ s available.

## Slide 35
Gatling gun

## Slide 36: Gatling Gun : Motivation
State-of-the-art
Polarized electron sources deliver either a high peak current, such as >5A achieved by the SLAC(High peak current, low average current)
Or a high average current, such as that up to 4mA reached by the Jlab. (Low peak current, high average current)
Operation requirement: weekly cathode exchange.
=> Operation lifetime min 85 hours (half week)
Average current :50mA
Charge lifetime: 15,300C
Current State-of-art single cathode charge lifetime: 1000C @ 2.5mA
Use set of 20 large area (6mm) cathodes => 50mA/20=2.5 mA
15300C/20=765C<1000C
What is needed?
High average current: 50mA; High Bunch charge:5.3nC; Long lifetime
Very important to demonstrate that the performance of an individual photocathode is not affected by the presence of other cathodes.
Courtesy Erdong Wang

## Slide 37: Injector concept based on Gatling gun
Single cathode:470 KHz*5.3nC=2.5mA
After funneling:9.4 MHz*5.3nC=50mA
10MeV
1% Energy spread
Combiner, 470kHz rotating magnetic bending
Courtesy Erdong Wang

## Slide 38: Beam Combiner
Bending the beam by dipole
Equalize the focusing by quadrupole
Parameters:
I(t)=Iod*cos(ωt+φ) where Iod=70.7A
I(t)=Ioq*cos2(ωt+φ) where Ioq=1.54A
B(0,0,0)=25.04G
Freq=470kHz
Bending angle=29 degrees
Courtesy Erdong Wang

## Slide 39: Initial tests results
Cathode preparation
QE~7%
Two low current beams were combined
At a few hundreds nano-amper current level, the test indicates #1 beam will not affect #2cathode lifetime. No cathode cross talk observed.
Lifetime ~2000sec
Good QE GaAs photocathodes have been activated
Courtesy Erdong Wang

## Slide 40: Gatling gun : future Plan
Conditioning the gun to 110kV
Reach 10-12 scale vacuum in DC gun vessel
Generate 2.5mA current from super-lattice GaAs photocathode.
Combine four beams to get 10 mA current.
Funneling proof of principle test.
Study cathode charge lifetime, beam quality, beam halo and beam polarization.
Courtesy Erdong Wang

## Slide 41: Coherent electron cooler

## Slide 42: CEC Motivation
Traditional stochastic cooling does not have sufficient bandwidth to cool intense proton beams (~3×1011 p/nsec) and can not provide two orders of density increase for heavy ion beams
Efficiency of traditional electron cooling falls as as high power of hadron’s energy
Synchrotron radiation is rather fable due to the heavy masses. For the same reason optical stochastic cooling is not suitable
Species | Energy, GeV/u | Stochastic cooling, hrs | Electron Cooling, hrs | CeC, hrs 1D/3D
Au | 130 | 1 | 1 | 0.015/0.3
p | 325 | 100 | > 30 | 0.3/1
Courtesy Igor Pinayev

## Slide 43: COHERENT ELECTRON COOLING
The CeC is a novel technique to cool stored ion beam which combines features of stochastic cooling and plasma acceleration. This cooling, with a bandwidth of 1013 Hz, can be used to cool RHIC proton beams at full energy, and is essential for any version of the EIC.

## Slide 44: eRHIC CEC requirements
Courtesy Igor Pinayev

## Slide 45: CeC proof of principal experement
SRF gun – 113 MHz, 2 MV design
Two 500 MHz bunching cavities
Drift space with diagnostics: ICT, BPMs,
profile monitors, BPMs, slits for emittance measurement, Faraday cup

## Slide 46: SUMMARY
Significant progress has been made at BNL during the last year in all high intensity beams frontiers.
First current has been observed from SRF gun and from polarized multi-cathodes Gatling gun.
ERL components installation completed
CEC POP SRF gun and other components installed conditioned beam test is scheduled for next week.
LEReC project has been approved
We are just at the beginning of a new adventure
To be continue…..

## Slide 47: Acknowledgment for providing material
Ilan Ben-Zvi, Jörg Kewisch, Vladimir Litvinenko, Toby Allen Miller, Igor Pinayev, Vadim Ptitsyn, Thomas Seda, Brian Sheehy, Erdong Wang, Wencan Xu and R&D ERL team.
D. Kayran, IEBW’15 Cornell University

## Slide 48: Thank you!

## Slide 49
Back up

## Slide 50: Gun at different stage of assembly