## Slide 1: RHIC and its EIC Future
Michiko Minty
Brookhaven National Laboratory

## Slide 2
High Energy Colliders in the US
Stanford Linear Collider (1989 – 1998)
2 miles
TeVatron (1987 – 2011)
1.2 miles
RHIC (>2001)
0.75 miles
The Relativistic Heavy Ion Collider (RHIC)
is now the only high energy collider in the Americas
is the only high energy polarized proton collider in the world

## Slide 3
Overview of RHIC facility
Electron Ion Collider
(Select)Technology Developments
Summary and Outlook
RHIC and its EIC Future

## Slide 4: Timeline of RHIC
The 1983 NSAC (Nuclear Science Advisory Committee) Long Range Plan included a relativistic heavy ion collider as the highest priority new facility
In 1990 the idea of a polarized proton collider was first discussed at the 1990 Polarized Collider Workshop
RHIC construction started in 1991
First beam in RHIC tunnel (sextant test) in 1998
RHIC commissioning started in 1999
First gold-gold collisions on June 12, 2000
Reached RHIC gold-gold design luminosity in 2001
First polarized proton collisions in RHIC in 2001
RHIC running time is shared between heavy ion collisions and polarized proton collisions
RHIC 20th anniversary celebrated just last month!

## Slide 5: The RHIC Accelerator Complex
Collider with two independently powered 3.8 km superconducting rings (~1750 SC magnets) that allows gold-gold, proton-gold, and proton-proton collisions at equal energies up to 100 GeV. Proton-proton collisions up to 250 GeV.
Six interaction regions and initially instrumented with four detectors: STAR, PHENIX, PHOBOS, BRAHMS.
RHIC
LINAC
Booster
AGS
Tandems
STAR
(s)PHENIX
Electron lenses
Polarized Jet Target
RF
Electron cooling
EBIS
(PHOBOS)
(BRAHMS)
Center for Bright Beams Symposium 2020

## Slide 6: Gold Ion Collisions in RHIC
RHIC
AGS
BOOSTER
TANDEMS
9 GeV/u
Q = +79
1 MeV/u
Q = +32
Beam Energy = 100 GeV/u

## Slide 7: RHIC – First Polarized Proton Collider
Two full Siberian snakes per ring preserve proton polarization to 255 GeV
Spin direction control at detectors with spin rotators
Minimally invasive polarimeters; also measure polarization profiles
Absolute polarimeter using an intense polarized H jet
STAR
PHENIX
AGS
LINAC
BOOSTER
Pol. H- Source
Spin Rotators
(longitudinal polarization)
Siberian Snakes
200 MeV Polarimeter
pC Polarimeters
Absolute Polarimeter (H jet)
pC Polarimeter
10-25% Helical Partial Siberian Snake
5.9% Helical Partial
Siberian Snake
Spin Rotators (long. pol.)
Spin Flipper
Siberian Snakes

## Slide 8
RHIC commissioning era (2000 to 2002)
first full energy (100 GeV/n) heavy ion runs, first 100 GeV polarized proton run
RHIC-I era (2003 to 2013)
first full energy (250 GeV) polarized proton runs
new technology: stochastic cooling proof-of-principle (2007)
new technology: high intensity electron beam ion source, EBIS (>2010)
RHIC-II era (2014 to 2016)
new technology: 3D stochastic cooling (>2014)
new technology: high intensity polarized ion source, OPPIS (>2015)
new technology: electron lenses for head-on beam-beam compensation (>2015)
new technology: superconducting rf cavity used in operations (>2016)
RHIC history and future
RHIC today (2017+)
new technology: low energy electron cooling (2017-2021)
physics operations with detector upgrade, sPHENIX (>2022)
Future electron-ion collider, EIC
Technology to be applied in EIC

## Slide 9
Overview of RHIC facility
Electron Ion Collider
development timeline
key parameters
how RHIC is transformed into an EIC (overview)
how RHIC is transformed into an EIC (detail)
(Select)Technology Developments
Summary and Outlook
RHIC and its EIC Future

## Slide 10
Timeline of the EIC
EIC White Paper (The Next QCD Frontier – Understanding the Glue that Binds us All) released in 2012. Commissioned by BNL and JLab as a follow-up to the 2007 NSAC Long Range Plan.
Two approaches were pursued (JLEIC at JLab, eRHIC at BNL)
The 2015 NSAC Long Range Plan recommended a high-energy, high-luminosity polarized EIC as the highest priority for a new facility construction following the completion of FRIB.
Pre-Conceptual Design Reports (pCDR) drafted in 2018 and evaluated together with scope and cost reviews in 2019.
Critical Decision 0 (CD0, “mission need”) for an EIC approved by the DOE in Dec, 2019 (enables work to begin on R&D and on the CDR).
Site decision made by DOE in Jan, 2020 for hosting the EIC at BNL in strong partnership with JLab
Next milestone is release of Conceptual Design Report (CDR) and CD1 (to allow release of Project Engineering and Design funds)

## Slide 11: Key parameters of the EIC
Highly polarized (70%) electron and light ion beams
Ion beams from deuteron to the heaviest nuclei (U, Pb)
Variable center of mass energies from 20 to 100 GeV upgradable to 140 GeV
High luminosity of 1033-1034 cm−2s−1
More than one interaction region possible

## Slide 12
Maximum Luminosity (1034/cm2s) Parameters
Parameter | Units | Proton | Electron
Energy | GeV | 275 | 10
Beam Current | Amperes | 1.0 | 2.5
Particles per bunch | 1010 | 6.9 | 17.2
Number of bunches |  | 1160 | 1160
Horizontal emittance | nm | 11.3 | 20.0
Vertical emittance | nm | 1.0 | 1.3
Hor/Ver beta at IP | cm | 80/7.2 | 45/5.6
Hor/Ver beam size at IP | mm | 95/8.5 | 95/8.5
Hor/Ver angular spread at IP | mrad | 119/119 | 211/152
Bunch length (rms) | cm | 6 | 2
Hor/Ver beam-beam parameter |  | 0.012/0.012 | 0.072/0.100
IBS growth time (Long/Hor) | hours | 2.9/2.0 | [na]

## Slide 13: How RHIC is transformed into an EIC
Existing RHIC with blue and yellow rings

## Slide 14: How RHIC is transformed into an EIC
Add electron storage ring

## Slide 15: How RHIC is transformed into an EIC
Add an electron injector complex with Rapid Cycling Synchrotron

## Slide 16: How RHIC is transformed into an EIC
Strong hadron cooling completes the facility
Alternate solution also shown using RHIC blue ring

## Slide 17: Cross-sectional view of the EIC tunnel
  Electron Storage Ring (eSR)
  Electron Injector Synchrotron (Rapid Cycling Synchrotron, RCS)
  Two detector halls available
RCS
eSR
RHIC
Existing RHIC
tunnel
~ 5 m

## Slide 18: Electron Storage Ring
Energy range, E = 2.5 – 18 GeV (beam injected at full energy)
11 superconducting 2-cell 591 MHz RF cavities
Design challenge: maintain electron beam emittance at all energies (~ 20 nm)
flexible design of magnetic lattice design comprising six FODO arcs with
adjustable proper phase advance:
90º /cell at E=18 GeV
60º /cell for E= 2.5-10 GeV plus radial shift and/or ‘super-bend’ lattice
Design challenge: 70% average polarization and fully flexible spin patterns
- polarized electron source and polarization-preserving pre-accelerators
- solenoid-based spin rotators
- bunch replacement at 1Hz (330 bunches in 5.5 minutes) to avoid stochastic
depolarization (Derbenev-Kondratenko)

## Slide 19: Bunch replacement
In the electron storage ring, single bunches will be replaced at a 1Hz rate
Replacing a 28 nC bunch requires accumulation of 7nC bunches in the RCS
Fast extraction kicker on top of slow bump to extract a single bunch

## Slide 20: Superconducting RF cavities in the Electron Storage Ring

## Slide 21: Electron Injector Synchrotron, RCS
Full energy injector for the electron storage ring
Energy range (at extraction), E = 2.5 – 18 GeV
Design challenge: preserve electron beam polarization during acceleration
spin-transparent, rapid-cycling synchrotron (RCS)

## Slide 22: Spin Resonance Review
Quadrupole
S is the spin vector, G is the electron gyromagnetic anomaly
Thomas-BMT equation
Imperfection resonances Gg = nP due to dipole rotations, quadrupole misalignments
Intrinsic resonances Gg = nP +/- Q due to (primarily) vertical betatron motion
Spin resonance conditions (n is an integer, P is lattice periodicity, Q is the betatron tune)

## Slide 23: RCS design: Spin Resonance Free Lattice
Acceleration from 400 MeV to 18 GeV (max): 0.9 < Gϒ < 41
By design of a lattice with periodicity P=96 and an integer betatron tune Q of ~50:
the strongest imperfection resonance occurs at Gg = 96 – 50 = 46
the strongest intrinsic resonances occur at
Gg = 50 +/- dQ (n=0)
Gg = 96 +/- (Q+dQ) = 46 – dQ (n = 1)
dQ is the fractional betatron tune
With this lattice design, highest-order spin resonances are avoided.
Imperfection resonances Gg = nP
Intrinsic resonances Gg = nP +/- Q

## Slide 24: RCS Polarization
Simulated polarization transmission efficiency vs acceleration cycle duration (‘ramp’)
High Quasi-symmetry
 Good spin transparency properties
200 ms ramp

## Slide 25: Strong Hadron Cooling
Two options
Coherent electron cooling with FEL amplifier or micro-bunching amplifier
Full on-energy injection with conventional electron cooling using the second (unused) RHIC storage ring

## Slide 26: Coherent Cooling with FEL amplifier
cooling of high energy Hadron beams with high band-width, ~ 1THz
short cooling times to balance strong intra-beam scattering
Modulator
Kicker
Dispersion section
( for hadrons)
Electrons
Hadrons
High gain FEL (for electrons)
Eh
E < Eh
E > Eh
Eh
E < Eh
E > Eh


## Slide 27: EIC Strong Hadron Cooling
Electron Beam Optics
Coherent Electron Cooling with m-bunching amplification
Design Cooling Rate Rcool= 2h-1
Electron beam current Ie=100 mA (1nC/bunch)
Relativistic factor g = 293
exyN= 2.5/0.5mm

## Slide 28: Frequent on-energy injection (FOEI)
Strong cooling as desirable but not necessary for high luminosity (especially high average luminosity) by using the existing second (Blue) ring, with conventional electron cooling, as a full-energy injector.
Bunch replenishment is accomplished using a series of kickers to simultaneously extract bunch(es) from the main (Yellow) hadron ring into the other (Blue) hadron ring while injecting bunches from the Blue ring into the Yellow ring.

## Slide 29
Overview of RHIC facility
Electron Ion Collider
(Select) Technology Developments
bunched-beam stochastic cooling
coherent electron beam cooling
bunched beam electron cooling
polarized electron source
Summary and Outlook
RHIC and its EIC Future

## Slide 30
Accelerator Technology: 3D stochastic cooling for heavy ions
3 GHz bandwidth, cooling times ~1 h
pickups
kickers
Motivation: counteract intrabeam scattering (IBS) and cool beam distributions for higher luminosity
M. Blaskiewicz, J.M. Brennan and F. Severino, Operational stochastic cooling in the Relativistic Heavy Ion Collider, PRL 100, 174802 (2008)
M. Blaskiewicz, J.M. Brennan and K. Mernick, Three-Dimensional Stochastic Cooling in the Relativistic Heavy Ion Collider, PRL 105, 094801 (2010)

## Slide 31
Technology: Coherent electron Cooling
Courtesy: V. Litvinenko and coworkers
< 2019, FEL-based cooling channel
2019+, PCA-based cooling channel
Electron beam parameters demonstrated 7/14/20
V. N. Litvinenko, Y.S. Derbenev, Coherent electron Cooling, PRL 102, 114801 (2009)

## Slide 32
Technology: Bunched-Beam electron Cooling

## Slide 33: Bunched-Beam electron Cooling at RHIC
Bunched-beam electron cooling used now in routine operation at RHIC in support of the Basic Energy Sciences Program at BNL
After FY21 RHIC Run, facility will be converted for high-current injector studies for the EIC
detector event rate
A. Fedotov, Experimental demonstration of hadron beam cooling using radio-frequency accelerated electron bunches, PRL 124, 084801 (2020)

## Slide 34: Technology: Polarized Electron Source
In development at Stony Brook University
achieved mid-10-12 Torr
first beams expected in August, 2020
planned R&D: cathode development and quantum efficiency lifetime
5-10 nC/bunch at 1-2 Hz repetition frequency
based on the JLAB inverted gun
XHV vacuum requirements (<10-12 Torr)

## Slide 35
Overview of RHIC facility
Electron Ion Collider
development timeline
design concept and key parameters
how RHIC is transformed into an EIC (overview)
how RHIC is transformed into an EIC (detail)
(Select) Technology Developments
Summary and Outlook

## Slide 36: Summary and Outlook
RHIC is the first heavy ion collider and also the first and only high energy polarized proton collide.
Over the last 20 years RHIC has been operated with unparalleled flexibility in collision energy and ion species from protons to Uranium.
The science case / mission need (CD-0) for an Electron-Ion Collider was approved by the DOE in Dec, 2019 with BNL chosen as host in Jan, 2020.
The next EIC milestone is completion of the CDR
Major technological advances in particle sources and beam cooling have been demonstrated and will be used at the EIC.

## Slide 37: Schedule
Commissioning and operations
sPHENIX
RHIC
Beam Energy Scan
EIC
Operations
Access to RHIC tunnel
EIC schedule is technically driven
All work planned to early finish – June 2029
One year of float to CD-4

## Slide 38
Thank you to everyone in the C-AD department whose collective accomplishments are presented here!
Thank you to those who have supported our efforts through many external reviews!
And thank you to All for your attention!
Acknowledgement and Thanks

## Slide 39
3D stochastic cooling for heavy ions
3 GHz bandwidth, cooling times ~1 h
pickups
kickers
Motivation: counteract intrabeam scattering (IBS) and cool beam distributions for higher luminosity
M. Blaskiewicz, J.M. Brennan and F. Severino, Operational stochastic cooling in the Relativistic Heavy Ion Collider, PRL 100, 174802 (2008)
M. Blaskiewicz, J.M. Brennan and K. Mernick, Three-Dimensional Stochastic Cooling in the Relativistic Heavy Ion Collider, PRL 105, 094801 (2010)