## Slide 1
Physics Design of CBETA Quadrupoles
Holger Witte

## Slide 2: Outline
Lattice and Magnet Requirements
General Concept
Physics Requirements on Design
Plans for Prototypes
Correctors

## Slide 3: Lattice and Magnets
EMMA: the first non-scaling FFAG built
Magnet-to-magnet field variation contributed to
  Significant closed orbit distortion, which
  Ultimately limited the energy range at the low energy end
Correctors
  Improved the situation
  Never fully eliminated the orbit distortion

## Slide 4: Cell
Qf/Qd: identical gradient / aperture (different length)
Beam excursion: +/- 31mm
Design: tracking with 3D field maps

## Slide 5: Magnet Concept
8.25’’
Based on permanent magnet design at Fermilab (recycler)
Advantages
  (Largely) conventional approach
  Field quality determined by pole
  Laminations
    Small magnet to magnet variation
  Permanent magnet tolerances easier to handle
    Magnetization 3%
    Magnetization angle 3-5º
  Scheme for temperature compensation
Adopted for CBETA
  Material NdFeB (not ferrite)
  Higher gradient (Fermilab: 2.6 T/m)

## Slide 6: 2D Geometry Qf/Qd
80% PM (N49M)
M
M
Size of magnets: driven by beam pipe requirements

## Slide 7: Gradient quality
Beam excursion: 31mm
Hump: orbit compression
Requested: 1%
ΔG/G0

## Slide 8: Temperature Compensation
NdFeB: (∆B/B)/∆T≈-1.1x10-3/K
Compensation scheme: 30-32% Ni-Fe
  Pioneered by Fermilab
  Curie temperature of 60°C
  Bsat=0.3-0.1 T (20-45°C)
Required Ni-Fe: about 20% of PM
NdFeB
NiFe
Top
Side
Chart: Temperature in °C
| 0 | 10 | 20 | 30 | 40 | 50 | 60
3A/cm | 193 | 182 | 161 | 120 | 72 | 34 | 12
10A/cm | 359 | 301 | 236 | 166 | 101 | 52 | 22
50A/cm | 391 | 328 | 261 | 192 | 127 | 73 | 37
80A/cm | 396 | 335 | 269 | 202 | 137 | 82 | 44
200A/cm | 407 | 350 | 289 | 225 | 163 | 108 | 65
 | 269 | 202 | 135 | 68 | 1 | -66
Thermoflux TX65/100

## Slide 9: 3D NiFe Temperature Compensation
Not shown: same for Qd / individual magnets
Qf, field at outermost aperture
20ºC
30ºC
Margin: 9.2% (approx. 4mm gaps in long. direction)
0.368T
0.3681T
z (m)
NiFe

## Slide 10: Bench Test
Material: VAC 745TP
Temperature coefficient (%/K)
  uncompensated: -0.103
  Compensated: <-0.003
Chart: 
| Point 1 Field (T) | Point 2 | Point 3 | Point 4 | Point 5 | Point 6 | Point 7 | Point 8
0 T_Room | -0.2155 | -0.215 | -0.2152 | -0.2152 | -0.219 | -0.2192 | -0.219 | -0.2187
0 T_Fridge | -0.2177 | -0.2172 | -0.2173 | -0.2177 | -0.2217 | -0.2215 | -0.2218 | -0.2216
24 T_Room | -0.2032 | -0.2029 | -0.203 | -0.2032 | -0.2065 | -0.2067 | -0.2067 | -0.2067
24 T_Fridge | -0.2032 | -0.2029 | -0.203 | -0.2032 | -0.2067 | -0.2069 | -0.2067 | -0.2068
NiFe

## Slide 11: Manufacturing
Sources of error
  Soft iron (spec this so that this is not an issue)
  Geometry
  PMs
Geometry: get it right from the beginning
  Aim: after assembly no modification required
  Poles are far out - possible to meet tolerances
PMs only source of error: imbalanced quadrants
  Measure PMs
  PMs can get damaged during assembly, …
  Approach: correct with shunts

## Slide 12: Geometry / Field Quality
Pole area
  Pole shape
  Distances / tilt
  Identical to other quadrupoles
Distance pole to back yoke
  NdFeB: μr≈1
  Adds to air gap
Engineering: George’s talk

## Slide 13: Pole Tolerance
Required pole accuracy?
Start with ideal pole and add error function
  Amplitude +/-50um
  (easily achievable with stamping)
Benchmarking
  3D tracking
  Look at orbit distortion
  Result: no issue
Choose worst error function
  Increase tolerance to 100 and 150 um
  Orbit distortion < 0.3mm
Pole shape very robust

## Slide 14: Permanent Magnets
Distance d needs to be identical for each pole
Permanent Magnets
  Magnetization 3%
  Magnetization angle 3-5º
Important for design
  Flux through surface perpendicular to pole piece
Can be measured using Helmholtz Coil
Yoke
Pole
Br
Br,x
Br,y
d

## Slide 15: Block Measurements
Blue: Qf
Green: Qd
Qd: +/-0.5%
Qf: +/-1%
Much smaller spread than expected
Br smaller than expected (but within +/-5% spec)
Matching (iterative): error < 1x10-5

## Slide 16: Demonstrator
Different lattice
  Higher gradients (28 & 41T/m)
  Smaller apertures (IR 16 & 22 mm)
Design freeze September 2015
  Not all necessary simulation work carried out
‘Aggressive’ design
  Sensitive to tolerances
Assembled without tooling
Harmonics measurement
  12 units out (of 10000)
Qf
Qd
80 mm
110 mm

## Slide 17: Prototype Magnet
Actual geometry + spacer
Use existing PMs
  Come measured
  Smaller than what we need (gradient lower)
Performance
  Gradient about 5.8T/m
  Harmonics identical
  Upgrade to correct PMs later
Tests
  Improved geometry
  New pole shape
  New assembly procedure
  Splitting magnet
Time estimate: 1 month?
Spacer

## Slide 18: Prototype Girder
Assembly
Integration
Alignment
Test with beam
  Cornell
  40/80 MeV
Test of BPMs
First test of beam dynamics

## Slide 19: Quad Corrector
Coil: 8x10mm2
J = 1A/mm2
+/-4%
Gradient quality unaffected by quad corrector
Can be air-cooled
G/G0,nominal
1.04
1.0
0.96
x (m)

## Slide 20: Skew Dipole Corrector
Skew dipole=590 Gcm
Four outermost conductors 4.5A/mm2
Increase area to lower current density
(otherwise 1A/mm2)
B/B~8x10-3
Courtesy of N. Tsoupas

## Slide 21: Dipole Corrector
Dipole 347.26 Gauss.cm
Current: cos(Θ) distribution (max J<1A/mm2)
with B/B~5x10-3
Can be air-cooled
-38.5 Gauss
-38.4 Gauss
-38.6 Gauss
Courtesy of N. Tsoupas

## Slide 22: Conclusion
Concept: iron dominated magnets
  Factors affecting field quality understood
  Large aperture magnets: pole and alignment tolerances not challenging
  Laminations: small magnet-to-magnet variation
Temperature compensation
  Concept shown to work at FNAL / CERN
Prototype magnet
  Tests pole shape, improved assembly procedure
Prototype girder: assembly, integration
  Test with beam: BPMs, beam dynamics
Concept for correctors

## Slide 23: Additional Slides

## Slide 24: Materials
Iron
  Low carbon steel
  JFE-EFE: procured recently for large magnetic shiedling project
  BH curves for as delivered, machined, machined+annealed
  (SiFe no change in gradient or quality)
Permanent Magnet
  Grade: N49

## Slide 25: Magnetization
200 MeV
150 MeV
1.8T
1.4T
Less stringent requirements on iron

## Slide 26: Gradient Quality
Gradient quality unaffected by quad corrector

## Slide 27: Temperature Compensation
NiFe
w (m)
dB(T)
Required cross-sectional area of NiFe can be determined in 2D simulation
Result translates from 2D linear → 2D non-linear → 3D linear → 3D non-linear
Linear relationship between compensation performance and NiFe fraction

## Slide 28: Angle of Magnetization
Qf
Qd
M
x
y
z
Angle: γ
Angle of magnetization not important for this type of magnet

## Slide 29: Helmholtz Coil
Thanks to Toshiya Tanabe & Chris Eng (BNL Insertion Devices Group)
Mike Anerella, Jesse, Ray + Mike
Variation in permanent magnets: Match PMs to deliver same amount of flux to each pole

## Slide 30: Shunting
Shunt
Thin strip of soft iron – locally shunts fraction of magnetic flux
Shunted flux depends on width, length and material
Attractive, because this can be done while coil on measurement bench
Affects harmonics up to sextupole (skew and normal)
PM