## Slide 1: BBU simulation
William Lou
Supervisor: Prof. Georg Hoffstaetter

## Slide 2: Outline
BBU overview
  Design current of CBETA
  Bmad simulation
2) 1-pass results
  statistics
  Results with additional phase-advances
  Results with x-y coupling
4-pass results
  (similar to 1-pass)

## Slide 3: Beam breakup Instability (BBU)
Higher Order Modes (HOM) in the cavities give undesired kick.
Off-orbit bunch returns to the cavities and excite more HOMs…
BBU limits the maximum achievable current
in an ERL threshold current
decreases with # recirculation turns.

## Slide 4: Design current of CBETA
Design current (mA) | KPP | UPP
1-pass | 1 | 40
4-pass | - | 40

## Slide 5: BBU simulation on Bmad
Given a complete lattice with multi-pass cavities and HOMs assigned…
Starts with a test current…
tracks off-orbit bunches through lattice
computes bunch-HOM momentum exchanges
determines stability of all HOM voltages
Attempts different test currents to pin down

## Slide 6: Simulated HOM data for one MLC cavity
Cavity construction error: ± 125 μm, 250 μm…
400 unique cavities provided per error case.
The “10 worst dipole HOMs” (large figure of merit) provided per cavity.

## Slide 7: CBETA 1-pass Cavity shape error: 125 μm HOM assignment: random (10 dipole/cavity)
All results above KPP (1mA)
20 out of 500 below UPP (40mA)

## Slide 8: Vary the optics in Bmad
Introduce either T matrix
at the end of LINAC 1st pass
Two cases:

## Slide 9: CBETA 1-pass v.s additional phase advances (decoupled optics)
results can improve significantly
Min = 140 mA
Max = 611 mA
nominal = 342 mA
Notes: The valley location depends on which cavity has the most dominant HOM

## Slide 10
Min = 175 mA
Max = 640 mA
Nominal = 218 mA
1-pass decoupled
with different HOM assignments…
Min = 165 mA
Max = 595 mA
Nominal = 248 mA
Notes: Valley location

## Slide 11: CBETA 1-pass with x-y coupling
results can improve significantly
Min = 140 mA
Max = 520 mA
nominal = 342 mA
Notes: Nominal ( no coupling ) = 342mA
(0,0) at 277mA

## Slide 12
Min = 136 mA
Max = 436 mA
Nominal = 218 mA
1-pass coupled
with different HOM assignments…
Min = 166 mA
Max = 678 mA
Nominal = 248 mA

## Slide 13: CBETA 4-pass Cavity shape error: 125 μm HOM assignment: random (10 dipole/cavity)
All results above 10 mA
32 out of 500 below UPP (40mA)
Notes: Before: 70 out of 300

## Slide 14: CBETA 4-pass Cavity shape error: 250 μm HOM assignment: random (10 dipole/cavity)
All results above 10mA
23 out of 500 below UPP (40mA)
Notes: Before: 33 out of 300

## Slide 15: CBETA 4-pass v.s additional phase advances (decoupled optics)
results can improve
Min = 61 mA
Max = 193 mA
Nominal = 69 mA
Notes: Location of the valley depends on which cavity has the most dominant HOM.

## Slide 16
Min = 37 mA
Max = 176 mA
Nominal = 38 mA
4-pass decoupled
with different HOM assignments…
Min = 39 mA
Max = 205 mA
Nominal = 49 mA

## Slide 17: CBETA 4-pass with x-y coupling
results can improve
Min = 89 mA
Max = 131 mA
Nominal = 69 mA
Notes: Nominal = 69mA
(0,0) = 99mA
Location of

## Slide 18
Min = 47 mA
Max = 100 mA
Nominal = 38 mA
4-pass coupled
with different HOM assignments…
Min = 57 mA
Max = 107 mA
Nominal = 49 mA

## Slide 19
Potential improvement on Ith from the current design (mA) | Additional phase advances (decoupled optics) | x-y coupling
1-pass | ~ 200 mA to 400 mA | ~ 200 mA to 400 mA
4-pass | ~150 mA | ~ 60 mA

## Slide 20: Summary
For 1-pass, all simulated are above the UPP (40mA)
For 4-pass, 93% simulated are above the UPP (40mA)
For 4-pass, introducing additional phase advances allows greater improvement in than x-y coupling

## Slide 21: Acknowledgment
References
BBU papers by Georg and Ivan
Bmad manual
Nick Valles’s dissertation
Special thanks to:
Prof. Georg Hoffstaetter
Christopher Mayes
Nick Valles
David Sagan

## Slide 22: THE END

## Slide 24: Find the critical which gives the maximum real eigenvalue of M
General analytic formula for BBU
The corresponding is
Helper Slide #1

## Slide 25: RFC cavity HOMs from Nick Valles
Helper Slide #2

## Slide 26: Aim for better
Potential ways to improve :
1) Change bunch frequency
2) Vary phase advance
3) x-y coupling of beam optics
Helper Slide #3

## Slide 27: Does vary with bunch frequency?
fb / (1.3 GHz) | 4-pass (mA)
1 | 40.0
1/2 | 48.8
1/4 | 49.5
1/8 | 46.0
1/16 | 45.8
Helper Slide #4