## Slide 1: Cornell-BNL ERL Test Accelerator Technical Review FFAG Magnet and Girders
George Mahler, Steven Trabocchi, J. Tuozzolo, Stephen Brooks

## Slide 2: Presentation Outline
WBS level 2 scope and interfaces
Halbach magnet development and requirements
Engineering design progress Halbach
Corrector magnet design
Magnet girder developments
Pre-production plans and testing
Production Plans

## Slide 3: Scope
Design, Fabricate, and Test:
211 Consistent Halbach permanent magnets, (5 types)
211 Powered correctors for beam line, (2 types)
Install on “girder” assemblies with vacuum chamber
Production planning:
Complete preproduction development and testing
Develop a fabrication plan and procurement documents
Vendor interface, statement of works and specification for vendor proposals and bids
Bid and place orders
Acceptance testing and production oversight
BNL final assembly & ship to Cornell

## Slide 4: Interfaces
Cornell/BNL physics, Halbach magnet and corrector specifications
Cornell power supply group, corrector power supply specifications
Cornell vacuum group, vacuum chamber/pump support/BPM clearance and alignment
Cornell civil, magnet stabilization water supply
Cornell civil, space, cable tray, installation, & survey

## Slide 5: Consistent Halbach Magnets
Proof-of-principle (PoP) magnets:
Demonstrated consistent field strength magnet to magnet.
Demonstrated the ability to reduce multipoles with interior steel rods.
Successfully reviewed by BNL committee: meets design specifications and “buildability”.
To be proven with pre-production magnets:
PoP magnets used a single batch of permanent magnet material blocks. Larger batches have larger variations in field strength. Magnets will be shimmed between PMM blocks (slide 10).
Mechanical tolerances: larger batches of PMM may have greater variation of dimensional tolerances. Shimming also adjusts for small variations in block dimensions.
PoP magnets used plastic frames and were not designed to be split for vacuum chamber installation. Production magnets will have aluminum frames with designed splits. (slides 7, 8, 9)

## Slide 6: Consistent Halbach Magnets
Permanent Magnet Material (PMM) specifications with magnetic tolerances for field vector (strength and direction) and dimensional mechanical tolerances. (Brooks)
Specifications, method, and equipment for acceptance testing PMM field vector. (Brooks)
Solid PMM mounting frame design with minimum deflection and accurate alignment. (Mahler)
Method for shimming PMM for matching field strength. (Mahler)
Method for analyzing block field measurement results to define field strength shimming dimension. (Brooks)
Method for analyzing magnet measurement results for multipole correction. (Brooks)
Magnet mounting and alignment method and tolerances. (Mahler)

## Slide 7: Halbach Magnet Frame Design
Split Magnet Deflection Analysis
Ansys using permanent magnet forces – worse case BD, thin side
Max. deflection .005” (.13mm) in + .0002" out
Max. stress 14,000 ksi

## Slide 8: Halbach Magnet Frame Design
Thermal Analysis, Water Stabilized +/- 1C
15 C water temp, 5 W/m^2 = H, 100 Watts top, 50 Watts sides
Re-analyze for corrector specifications
Cross drilled water passages & plugs
Interface for civil construction water systems
Aluminum components
Temperature stabilized (+/- 1.0 C)

## Slide 9: Shimming for Field Strength
Shimming design allowance 0.1mm to 0.8mm circumferentially between blocks.
Radial adjustment 0.2 mm to 2.2 mm.
PMM blocks of each type are measured for field strength and direction.
Measurement results are recorded and compared. Shim thickness specified.
Shims
Adhesive

## Slide 10: Halbach Magnet Frame Design
Final frame models/drawings with alignment pins
Alignment pins for repeatable assembly of Halbach magnet
Quadrupole / Horizontal OR Vertical dipole correctors
Permanent Halbach wedges glued in place to defined shimmed location on an aluminum frame
Corrector assembly disassembles to allow for vertical Halbach split
Alignment pins for repeatable assembly of Halbach magnet

## Slide 11: Halbach Corrector Magnets
Halbach Corrector Magnet details:
BD and QF correctors be the same configuration
Alternating horizontal & vertical dipole correction for orbit correction.
Dipole coils on steel core for efficient and best field quality
Asymmetric quadrupole correction coils for Halbach field strength correction, if needed. Good quality quadrupole field.
Dipole Field
Flatness

## Slide 12: Halbach Corrector Magnets
Dipole and Quadrupole field strength interface.
PS specifications, Quadrupole corrector power supplies will not be procured until field measurements verify the need.

## Slide 13: Halbach Corrector Magnets
Assembly / Disassembly procedure
Remove corner brackets
Remove Corrector / Separate Halbach

## Slide 14: Magnetic Measurement – Multipole Reduction
To reduce multipole errors a plastic steel rod holder is installed in the aperture.
Steel wires of various diameters and lengths inserted into the magnet bore., shown in Fig. 3.1.8.
There are 32 wire holders evenly-spaced around the bore of the magnet
If necessary wire holders for 48 or 64 wires can be used to increase multipole reduction strength & accuracy.

## Slide 15
FA-GD01
FA-GD02
FA-GD03
FA-GD04
TA-GD01
TA-GD02
TA-GD03
TA-GD04
TA-GD05
TA-GD06
ZA-GD01
ZA-GD02
ZB-GD03
ZB-GD02
TB-GD01
TB-GD02
TB-GD03
TB-GD04
TB-GD05
TB-GD06
FB-GD01
FB-GD02
FB-GD03
FB-GD04
NT
CT
NT
CT
NT
CT
NT
NT
CT
CT
CT
NT
CT
CT
NT
CT
CT
CT
NT
CT
NT
CT
NT
CT
CT
NT
NT
CT
CT X4
CT
NT X4
CT X4
NT
NT
NT
CT
IP
IP
CT
NT
NT
CT
CT
NT
NT
CT
NT
GV
GV
GV
GV
GV
GV
GV
GV
GV
CT
CT
CT
NT X4
CT
GV
NT
CT
GV
IP
Gate Valves (11) 10 RF shielded 3 New to CBETA
NexTorr Pump (28)
CapaciTorr Pump (34)
Ion Pump (2)
GA
Ion and Pirani Gauges (8)
GA
GA
GA
GA
GA
GA
GA
GA
(0,0)
(0,10m)
(10,10m)
(20,10m)
ZB-GD01
ZM-GD
ZA-GD03
Girder Types and Positions

## Slide 16: Girder Types and Positions
4 Cells per Girder, 2 Magnets per cell

## Slide 17: Girder Types and Positions
Alignment specifications:
+/- 0.2 mm (.008”) horizontal and vertical maximum allowance
+/- 0.1 mm (.004”) horizontal and vertical goal to provide corrector magnet design margin.
Allowance to resurvey and “retune” magnet positions after initial commissioning with beam (no shims or pins).
Magnet mounts – jacking screws for horizontal and vertical survey
Magnet mounts – integrated mounts for Halbach and Corrector
Crane lift points that do not cause deformation and misalignment, magnet assembly weight/girder assembly weight, deflection analysis

## Slide 18: Girder Types and Positions
Cable tray
“pusher block” array
Integrated H2O manifold
Flexible component mounting

## Slide 19: Pre-production Girder Assembly
Halbach magnets
Permanent Magnet Material Ordered for 6 (3 BD, 3 QF).
BNL PMM QA field vector measurement, dimension inspection, shim determination.
Aluminum frames designed, BNL machining.
BNL shim PMM, magnet assembly.
BNL field measurement, wire rod multipole reduction, field measurement.
Split magnets/realignment testing/field measurement.
Corrector magnets
Designed, in house machining.
BNL or vendor winding.
BNL field measurement.
Split magnets/realignment testing/field measurement.

## Slide 20: Production Manufacturing Plan
PMM: Request for Proposal, build to print & specification.
BNL or PMM vendor inspection & field vector measurement.
If vendor does field measurement, BNL will sample test/verify.
Halbach Magnets: Request for Proposal, build to print & specification.
BNL supplied PMM, PMM sorted & shimming specified by BNL.
Vendor fabricates frames, installs PMM, completes water lines.
BNL magnetic field measurement or magnet vendor option to measure.
BNL reviews measurement, specifies wire rod multipole reduction.
First article magnets, then release for production, option to cancel.
Corrector Magnets: Request for Bids, build to print.
First article magnets, then release for production, option to cancel.
BNL magnetic field testing of random magnets.
Girders and Stands: request for bids, build to print.
Girder assembly and survey: BNL

## Slide 21: Summary
BD & QF Halbach magnetic designs complete.
PMM ordered for pre-production BD & QF Halbach magnets.
BD & QF frame designs complete, analyzed for deflection, stress, and thermal stabilization; fabrication drawings underway.
Corrector magnet design complete, fabrication drawings underway.
Interface items are defined, understood, and in agreement.
Girder configuration defined, detailed design underway.

## Slide 22: Extra Slides

## Slide 23: Permanent Magnet Block Dimensions

## Slide 24: Halbach Corrector Magnets - Asymmetric
Halbach Corrector Magnet details:
BD and QF correctors be the same configuration
Alternating horizontal & vertical correction for orbit correction.
Dipole coils on steel core for efficient and best field quality
Asymmetric quadrupole correction coils for Halbach field strength correction, if needed. Good quality quadrupole field.

## Slide 25: Magnet Types and Counts